## Slide 1: HEz Polling Frame Format
Date: 2018-07-08
Authors:

## Slide 2: Introduction
The polling is the first stage in every HEz Txop measurement sequence.
It allow for ISTAs which established a session to dynamically change their measurement rate based (for example) on changing channel conditions, their movement, power save etc.

## Slide 3: Challenges
The design of polling TF and response needs to satisfy the following constraints:
  Allow for sufficiently large number of ISTAs to be polled.
  Allow RSTA to derive a TF Location Sounding allocating sounding resources to the subset of responding ISTAs (with SIFS time).
  Support for both associated and unassociated ISTAs.
In this presentation we propose a design for Polling TF satisfying the above constraints.

## Slide 4: Frame format for Polling TF – Previous Proposals
Option 1 (BSRP): use QoS NULL frames as Poll response.
  MAC Overhead: 40 bytes.
  Benefit: implementation simplicity.
  Con: Objections/comments from reviewers/rest of 802.11 group on the use of data frames by unassociated ISTAs, supports fewer ISTAs than Option 2.

## Slide 5: Frame format for Polling TF – Previous Proposals
Option 2 (NFRP): use Short NDP feedback.
  MAC overhead: 0 bytes.
  Benefit: can poll larger number of ISTAs simultaneously, shorter medium time (no MAC), shorter processing time (no decoding needed).
  Con: 11ax Rel 2.0 feature set is unknown at this time.

## Slide 6: Frame format for Polling TF(contd.)
Option 3: use CTS to Self as Poll response.
  RSTA identifies the responder from the RA field of the CTS frame.
    Allow CTS to be sent by unassociated STA.
  Duration field is Reserved.
  ISTAs use MAC padding/ packet extension to provide sufficient time for the RSTA to decode the Poll response.
  MAC Overhead: 14 bytes.
  Benefit: satisfy constraints in slide 1.
  Con: supports fewer ISTAs than Option 2.
Prefer Option 3.

## Slide 7: Polling TF format based on Option 3
If a CTS frame is used as Poll Response, the Polling TF can be based on the 11ax Basic Trigger frame with the following changes/constraints:
  The Trigger Dependent User Info field is absent because the response is not a MU-PPDU nor is a Data frame.
  Allocation is based on reception of a valid MAC header.
The Trigger Dependent Common Info field and its values are adopted from [11az Trigger Frame draft].

## Slide 8: Summary
Proposed usage of CTS as HEz Poll response to satisfy HEz Poll frame design constraints.

## Slide 9: References
Jonathan Segev etal, “802.11az Trigger Frame Format”, March 2018.

## Slide 10: Straw Poll 1
Do you support that the Poll response frame for HEz ranging shall be a CTS frame ?
Yes: No: Abstain:

## Slide 11: Straw Poll 2
Do you support that the Location Trigger frame subtype HEz Poll shall have the following constraints? :
1. No Trigger Dependent User Info field
2. OFDMA is the mandatory mode