## Slide 1: Multi-band Discovery Assistance for 802.11ay (CR on CID 1771)
Date: 2018-07-09
Name | Affiliation | Address | Phone | Email
Mohamed Abouelseoud | Sony | 1730 N. First Street, San Jose CA 95112 | +1-408-352-4027 | Mohamed.Abouelseoud(at)sony.com
Kazuyuki Sakoda | Sony | 1730 N. First Street, San Jose CA 95112 | +1-408-352-4405 | kazuyuki.sakoda(at)sony.com

## Slide 2: CR on CID 1771
CID | PP.LL | Comment | Proposed Change | Suggested Resolution
1771 | 135.2 | If TDD channel access is operated as shown in 11-17/1321, DMG Beacon frames are not transmitted periodically, and it would be hard for STAs to discover operating BSS. We need a procedure to enable network discovery for this mode of operation. | Please consider to add a network discovery method for TDD channel access mode that operates similar to 11-17/1321. There should be a way to enable it leveraging existing framework such as multiband operation. | REVISED: Adopt changes proposed in doc11-18/1203

## Slide 3: Overview
Robustness and latency are critical for consumer devices use cases
Previous contributions ([1],[2] and [3]), multi-band discovery assistance is introduced to:
  Reduce BHI overhead latency
  On-demand SLS is triggered using multi-band signaling and DMG beacon transmission is reduced to minimum
  Enable TDD channel access without relying on human triggering
  Use multi-band to signal a request for TDD-beamforming
In [3], a solution is presented to use FST Setup Request and Response frames to trigger discovery assistance
This contribution presents details on the multi-band on-demand sector sweeping through discovery assistance

## Slide 4: Multi-band Discovery Assistance
Announce on the lower band discovery assistance capability
  Multi-band element include discovery assistance feature indication
Lower band signal trigger mmW sector sweeping
  Send FST Setup Request frame containing the DMG Discovery Assistance element on lower band to request discovery assistance
  Respond with FST Setup Response frame containing DMG Discovery Assistance element on lower band to respond to the discovery assistance response
mmW sector sweeping
  On-demand sector sweeping triggering
    Send Sector Sweep Start Time to new STA
    Send Dwelling Time, slot schedule and structure to enable TDD synchronous beamforming
  Scheduled a period for beamforming with the new STA on the mmW band
    Allocate time on the mmW band to beamform with the new STA
    Send the mmW Extended Schedule element to new STA on lower band
    Send Dwelling Time, slot schedule and structure to enable TDD synchronous beamforming

## Slide 5: Discovery Assistance Capability Announcement
Beacons/Probe Responses advertise the multi-band and discovery assistance capabilities on lower band
Multi-band element contains 1-bit to indicate Discovery Assistance Enabled for the advertised frequency band and channel
 | B0 B2 | B3 | B4 | B5 | B5B6 B7
 | STA Role | STA MAC Address Present | Pairwise Cipher Suite Present | Discovery Assistance Enabled | Reserved
Bits: | 3 | 1 | 1 | 1 | 32
Multi-band element

## Slide 6: Lower band frame exchange (1)
New STA sends FST Setup Request frame containing DMG Discovery Assistance element on lower band
Discovery assistance can happen in conjunction with FST
FST Setup Request frame

## Slide 7: Lower band frame exchange (2)
FST Setup Response Frame
AP responds with FST Setup Response frame containing DMG Discovery Assistance element on lower band
Optionally add the extended Schedule element if beamforming is scheduled on the mmW band
Optionally add the TDD Slot Structure element and the TDD Slot Schedule element to enable synchronous TDD beamforming

## Slide 8: Multi-band Discovery Assistance Procedure *
* Normative Text available at 11-18/1203r0

## Slide 9: Straw poll
Do you support the use of the FST setup protocol as described in 11-18/1203r0 to enable multi-band discovery assistance in multi-band capable devices?
  Yes
  No
  Abstain

## Slide 10: References
[1] IEEE 802.11-18/486r0, “Multi-band Discovery Assistance”, Mohamed Abouelseoud, et.al.
[2] IEEE 802.11-18703r2, “Discussion the Multi-band Discovery Assistance Proposal”, Mohamed Abouelseoud, et.al.
[3] IEEE 802.11-18861r1, “Discovery Assistance for 802.11ay”, Mohamed Abouelseoud, et.al.