## Slide 1
11ba with Conventional Scheduled PS
Date: 2018-07-02
Authors:

## Slide 2: Introduction
TGba has defined WUR mode and following features[1]
  STAs in WUR mode could neglect Beacon schedule
    A STA operating in PS mode that is neither in WNM sleep mode nor in WUR Mode shall periodically listen for Beacon frames, as determined by the istenInterval parameter of the MLME-ASSOCIATE.request or MLMEREASSOCIATE.request primitive and the ReceiveDTIMs parameter of the MLMEPOWERMGT.request primitive.
  WUR duty cycle operation allows WURx to enter doze state
    WURx in WUR non-AP STA shall be in awake state during its ‘On duration’ every duty cycle period
  PCR schedule needs to be suspended in WUR mode but there are some exceptions
    STA is not required to wake up during the service period if the service period is suspended, except that the STA is expected to wake at the next service period following the existing baseline PCR operation (Note: The STA has indicated its intention to wake at the next service period by simply negotiating the PCR schedule).

## Slide 3: Scheduled PS and 11ba
If we allow 11ba STAs to maintain PCR’s schedule and its timer,
  the WURx may require more energy and complexity.
  the 11ba STAs may not require receiving WUR frame to wake-up to perform the scheduled power saving operation. (option 2)
Option 2 is more efficient because it does not requires additional WUR frame transmission and its channel access procedure
UL
AP
STA
WUR
frame
AP
STA
Duty Cycle Period
ON Duration
PCR delay
Trigger
TWT SP
DL
Ack
PCR awake state
WUR awake state
WUR doze state
PCR doze state
Target Wake Time
AP
STA
Duty Cycle Period
ON Duration
PCR delay
WUR awake state
WUR doze state
PCR awake interrupt time (= TWT-PCR delay-α)
Opt. 1
Opt. 2
Modified from Source: 802.11-18/834[2]

## Slide 4: Scheduled PS and 11ba
WUR frame can be transmitted but there could be some problem if there are some mismatch between duty cycle period and PS schedule
UL
AP
STA
WUR
frame
AP
STA
Duty Cycle Period
ON Duration
PCR delay
Trigger
TWT SP
DL
Ack
PCR awake state
WUR awake state
WUR doze state
PCR doze state
Target Wake Time
AP
STA
Duty Cycle Period
ON Duration
PCR delay
WUR awake state
WUR doze state
PCR awake interrupt (= TWT-PCR delay-α)
Opt. 1
Opt. 2
UL
AP
STA
Trigger
TWT SP
DL
Ack
PCR awake state
PCR doze state
Target Wake Time

## Slide 5: TWT and 11ba
TWT is representative schedule based power save operation
  A TWT requesting STA that is awake for an explicit TWT SP shall not enter doze state until it has received a nonzero Next TWT Info/Suspend Duration field from the TWT responding STA and has either been in the awake state for at least Nominal Minimum TWT Wake Duration time from the TWT SP start time as identified by the TWT responding STA or has received an EOSP field equal to 1 from the TWT responding STA.
If the exception for scheduled power save is valid, 11ba STAs with an explicit TWT SP shall not enter doze state during the TWT wake duration time
  STA is not required to wake up during the service period if the service period is suspended, except that the STA is expected to wake at the next service period following the existing baseline PCR operation (Note: The STA has indicated its intention to wake at the next service period by simply negotiating the PCR schedule)
  Following baseline spec, the STAs shall wake-up during TWT Wake Duration time from the TWT SP start time regardless of receiving WUR frame

## Slide 6: Discussion
Considering coexistence between scheduled PS and 11ba is valid and necessary
  Using scheduled PS would be more efficient in some traffic patterns
However, mandate all 11ba STAs to maintain PCR schedule may not be a good answer for simple WURx architecture
The expression ‘expected to wake at the next service period ’ can be interpreted in different ways for different PCR scheduled operations. Therefore, we need to clarify and simplify the operation maintaining the intention

## Slide 7: Suggestion
Adding 1 bit of scheduled PS in WUR capabilities or WUR Mode element field
  e.g., 1 bit in WUR Parameters field
If the bit is set to 0, all PCR schedule shall be suspended during WUR mode. However, if it is set to 1, the non-AP WUR STA shall maintain PCR schedule and shall enter awake state following PCR operation rule
Capability on maintaining PCR schedule needs to be discussed in TG
Following text modification is also suggested
  STA is not required to wake up during the service period if the service period is suspended, except that WUR with schedule PCR subfield is set to 1 during the WUR mode negotiation which is valid for present WUR mode the STA is expected to wake at the next service period following the existing baseline PCR operation (Note: The STA has indicated its intention to wake at the next service period by simply negotiating the PCR schedule)

## Slide 8: Conclusions
Scheduled PS with 11ba has been discussed and it could enhance efficiency of 11ba
In order to clarify and simplify 11ba operation, we suggested to use 1-bit indication for scheduled PS
If the bit is set to 0, PCR schedule is suspended in WUR mode, otherwise, 11ba STA shall maintain PCR schedule
Capability on this feature needs to be discussed (mandatory or optional)

## Slide 9: References
[1] IEEE Draft P802.11ba D0.3
[2] 11-18-0834-00 “Clarifications on WUR-PCR interactions”