## Slide 1: Extremely High Throughput (EHT) 802.11 – Features classification and early discussion on PAR
Date: 2018-09-09
Authors:
Name | Affiliation | Address | Phone | Email
Laurent Cariou | Intel | 2111 NE 25th Ave, Hillsboro OR 97124, USA | +1-503-712-5560 | laurent.cariou@intel.com
Robert Stacey |  |  |  | robert.stacey@intel.com
Xiaogang Chen |  |  |  | Xiaogang.chen@intel.com
Po-Kai Huang |  |  |  | Po-kai.huang@intel.com

## Slide 2: Content
This contribution proposes a classification of the main different technical directions for EHT proposed so far
  It groups several topics together (one possible classification)
  The intent is to ensure that we all use the same language to categorize the different proposals…
  … and that we can better discuss what should be in or out of EHT PAR
Based on this, the contribution discusses how this could be described in the PAR document
Laurent Cariou, Intel

## Slide 3: Classification of main EHT technical proposals (1/2)
Single band Frequency-dimension
  320MHz
  More efficient utilization of non-contiguous spectrum / better adaptation to regulatory rules at 6GHz
    e.g. enhanced preamble puncture, non-contiguous channel bonding, single user RU aggregation, …
  Enhancement to channel bonding protocol?
Multi-band
  Asynchronous multi-band aggregation for dual-radio devices
    Sometimes called Multi-band Full Duplex
  Multi-band channel bonding
  Management-plane enhancements for dual and single radio devices:
    Enhancements to FST/OCT: Separation of data and management plane (mobility, traffic steering, association across APs, …)
    Applicable to Collocated or non-collocated APs (single AP or multi-AP applicability)
Spatial-dimension
  16 spatial streams
  Sounding overhead reduction (feedback compression, implicit feedbacks, …)
  BF and MU-MIMO protocols enhancements
Slide 3
Laurent Cariou, Intel

## Slide 4: Classification of main EHT technical proposals (2/2)
Multi-AP coordination (Likely requires a selection among the following list)
  Time/frequency coordination: (a STA receives data from a single AP and provides sounding feedback to a single AP)
    Non trigger-based (no need for 802.11 work)
    Trigger-based (transmissions from Multiple APs are synchronized thanks to an over-the-air trigger frame):
      Multi-AP FDMA
    Enabler for spatial reuse or fractional frequency reuse (FFR)
  Coordinated beamforming (a STA receives data from a single AP and feedback to multiple APs)
    Non-trigger-based
    Trigger-based
  Joint transmissions (a STA receives data from multiple APs)
    No joint BF or MU-MIMO: sometimes called “non-coherent joint transmissions”
    STA provides sounding feedback to multiple APs: joint BF or MU-MIMO: called Joint processing
HARQ/Enhanced link adaptation (Under investigation)
Slide 4
Laurent Cariou, Intel

## Slide 5: How to write the PAR
  In order to ensure a more precise scope description, we propose the following guidelines for drafting the PAR:
    Section 5.2b Scope of the project:
      Define the objectives of the project (throughput increase)
      And list candidate features that can easily demonstrate feasibility (320MHz, Multiband aggregation and operation, 16 SS, Multi-AP…)
    Section 8.1 Explanatory notes:
      List more explicitly what is in the scope
      Provide flexibility for topics that are still under investigation
Laurent Cariou, Intel
Slide 5

## Slide 6: Section 5.2b Scope of the project Discussion on the objectives definition
We feel the simplest approach is to state the objective in terms of throughput increase:
  This allows to have a quantifiable value (4x over 11ax)
  This allows to demonstrate that we meet the PAR in a very easy way (for instance by peak throughput comparison)
  “throughput increase” captures peak throughput increase, but also efficiency improvements or throughput at range improvements
    Even in 11ax, we formalized efficiency improvements in terms of throughput
Another (more complex) approach would be to further detail the objectives for each category of improvements
  Provide a list of objectives: peak throughput objectives, efficiency objectives (5 percentile, …), …
  Provide scenarios on which objectives have to be met…
  But again, efficiency improvements are usually expressed also in terms of throughput
Laurent Cariou, Intel
Slide 7

## Slide 7: Section 5.2b Scope of the project Early proposal
  This amendment defines standardized modifications to both the 802.11 physical layers (PHY) and the 802.11 Medium Access Control Layer (MAC) that enable a mode of operation capable of supporting:
      4x link throughput increase over 11ax with the following features, but not limited to: 320MHz bandwidth, multiband aggregation and operation, 16 spatial streams, Multi-AP coordination.
      Carrier frequency operation between 1 and 7.125 GHz while ensuring backward compatibility and coexistence with legacy IEEE802.11 devices in the 2.4 and 5 GHz unlicensed bands, and with IEEE802.11ax devices in the 6GHz band.
Laurent Cariou, Intel
Slide 7

## Slide 8: Early proposal for 8.1 Explanatory notes (1/2)
The focus of this amendment is on WLAN indoor and outdoor operation in the 2.4 GHz, 5 GHz and 6GHz frequency bands. Outdoor operation is limited to stationary and pedestrian speeds.
Objectives
The objective of this group is to increase link throughput. The link throughput increase will also generate average user throughput increase, throughput at range increase in typical scenarios.
Laurent Cariou, Intel
Slide 8

## Slide 9: Early proposal for 8.1 Explanatory notes (2/2)
Features
The main candidate features are 320MHz bandwidth, multi-band aggregation, 16 spatial streams and Multi-AP coordination.
Along with these 4 features, solutions to the following objectives are considered to be in the scope of the project:
  Enable more efficient utilization of non-contiguous spectrum (e.g. enhance preamble puncturing, RU aggregation, …)
  More flexibility in multi-band operation for traffic steering, separation of data and management plane for collocated APs and non-collocated APs.
  Improvements of sounding, beamforming and MU-MIMO protocols
  If needed, adaptation to regulatory rules specific to 6GHz spectrum
Refinements of 802.11ax features to improve efficiency based on experience from the field may be proposed.
TBD:
provide a better description of Multi-AP coordination
HARQ?
Other?
Laurent Cariou, Intel
Slide 9