## Slide 1: Some (Measured) Characteristics of V2V Channels
Date: 2018-05-07
Authors:

## Slide 2: Abstract
This presentation discusses various characteristics related to V2V channels.
The results are extracted from various theoretical work and measurements campaigns conducted by Lund University during a number of years.

## Slide 3: Contents
Antenna patterns and antenna placements
Small scale fading – delay and Doppler spread
Shadowing – comparison with “cellular”
Pathloss LOS, NLOS – Comparing theory and measurements
Impact of correlation

## Slide 4: Antenna patterns and antenna placements
Roof antennas show a relatively omni-directional pattern
Antennas mounted in the front and rear show large variations
Front windscreen antenna show 10-15 dB gain difference between best and worst angle

## Slide 5: Highway measurements
Scenario:
V2V – Opposite direction
90km/h

## Slide 6: PDP over time

## Slide 7: Delay-Doppler Spectrum @ 5.2 GHz
LOS@83ns: Doppler = 868 Hz => 180 km/h
Scattering at buildings@371ns: Doppler 543 Hz
Scattering at buildings@304ns; Doppler -1107 Hz

## Slide 8: Shadowing by a truck

## Slide 9: Shadowing by a truck
In e.g. 802.11ax the shadowing is modeled having zero mean
With low angle spread, the shadowing may have much worse impact
An additional 10-12 dB average shadowing loss is seen, and in addition the variance is also higher

## Slide 10: Multilink communication

## Slide 11: Multilink on Highways
The multilink shadowing effects on V2V channels are not yet well understood
It is preferred to use geometry based models that can distinguish between LOS and NLOS
If a packet is not received, this packet cannot be ignored when estimating the pathloss

## Slide 14: Impact of correlation
If “system simulations” are used to estimate performance for successive packets (e.g. when data is retransmitted), the shadowing cannot be assumed to be uncorrelated
An exponential (Gudmundsson) autorcorrelation function may be used given that we distinguish between LOS and OLOS (blocking by other vehicles) and account for the additional path loss due to this.

## Slide 15: Straw Poll
Since the vehicular channel cannot be assumed to be wide sense stationary, are we willing to give up a tap delay line approach and define a geometry based stochastic channel model instead (with some typical geometries for urban intersections, highways etc)?
Y/N/A: