## Slide 1
Project: IEEE 802.11bb Task Group
Submission Title: IEEE 802.11bb Reference Channel Models for Indoor Environments
Date Submitted: July 06, 2018
Source: Murat Uysal (Ozyegin University), Farshad Miramirkhani (Ozyegin University), Tuncer Baykas (Istanbul Medipol University), Nikola Serafimovski (pureLiFi Ltd.), and Volker Jungnickel (Fraunhofer HHI).
Address: Ozyegin University, Nisantepe Mh. Orman Sk. No:34-36 Çekmekoy 34794 Istanbul, Turkey
Voice: +90 (216) 5649329, Fax: +90 (216) 5649450, E-Mail: murat.uysal@ozyegin.edu.tr
Abstract: This contribution proposes LiFi reference channel models for indoor environments such as office, home and manufacturing cell.
Purpose: To introduce reference channel models for the evaluation of different PHY proposals.
Notice: This document has been prepared to assist the IEEE 802.11. It is offered as a basis for discussion and is not binding on the contributing individual(s) or organization(s). The material in this document is subject to change in form and content after further study. The contributor(s) reserve(s) the right to add, amend or withdraw material contained herein.
Release: The contributor acknowledges and accepts that this contribution becomes the property of IEEE and may be made publicly available by 802.11.
July 2018
doc.: IEEE 11-18-1236-00-00bb
Submission
M. Uysal, F. Miramirkhani, T. Baykas, et al.

## Slide 2
IEEE 802.11bb
Reference Channel Models for Indoor Environments
July 2018
doc.: IEEE 11-18-1236-00-00bb
Submission
M. Uysal, F. Miramirkhani, T. Baykas, et al.

## Slide 3
Outline
  Introduction
  Overview of Channel Modeling Methodology
  Indoor Scenarios under Consideration: Empty Room, Office, Home, Manufacturing Cell
  Modeling of the Indoor Environment
  Source Modeling
  Illumination Level Requirements
  Channel Impulse Responses (CIRs)
  Effective Channel Responses
  Channel Characteristics
Conclusions
July 2018
doc.: IEEE 11-18-1236-00-00bb
Submission
M. Uysal, F. Miramirkhani, T. Baykas, et al.

## Slide 4
Overview of Channel Modeling Methodology
July 2018
doc.: IEEE 11-18-1236-00-00bb
Submission
  A flexible and efficient method for realistic VLC channel modeling
    Wavelength dependency
    Realistic light sources
    Effect of objects within the environment and types of surface (coating) materials
For additional details see
IEEE 15-15-0352-01-007a, “Channel Modeling for Visible Light Communications”
IEEE 15-15-0746-01-007a, “TG7r1 channel model document for high-rate PD communications”
M. Uysal, F. Miramirkhani, T. Baykas, et al.

## Slide 5
  Based on Monte Carlo Ray Tracing.
  Sobol sampling is used for speeding up ray tracing.
  The Zemax® non-sequential ray-tracing tool generates an output file, which includes all the data about rays such as the detected power and path lengths for each ray.
  The data from Zemax® output file is imported to MATLAB® and using these information, the multipath CIR is expressed as
Pi = the power of the ith ray
τi = the propagation time of the ith ray
δ(t) = the Dirac delta function
Nr = the number of rays received at the detector
Channel Impulse Response (CIR)
July 2018
doc.: IEEE 11-18-1236-00-00bb
Submission
M. Uysal, F. Miramirkhani, T. Baykas, et al.

## Slide 6
Effect of LED Response
  In addition to the multipath propagation environment, the low-pass characteristics of the LED sources should be further taken into account in channel modelling.
July 2018
doc.: IEEE 11-18-1236-00-00bb
Submission
  LED Model 1 [1]
  : 3 dB cut-off frequency of the LED
  LED Model 2 [2]
M. Uysal, F. Miramirkhani, T. Baykas, et al.
[1] L. Grobe, and K. D. Langer, “Block-based PAM with frequency domain equalization in visible light communications,” In IEEE Globecom Workshops (GC Wkshps), pp. 1070-1075, 2013.
[2] M. Wolf, S. A. Cheema, M. Haardt, and L. Grobe, “On the performance of block transmission schemes in optical channels with a Gaussian profile,” In 16th International Conference on Transparent Optical Networks (ICTON), pp. 1-8, 2014.

## Slide 7
We consider an empty room with a size of 6 m × 6 m × 3 m with plaster ceiling/walls and pinewood floor.
Simulation Scenario 0: Empty Room
July 2018
doc.: IEEE 11-18-1236-00-00bb
Submission
M. Uysal, F. Miramirkhani, T. Baykas, et al.

## Slide 8
Simulation Parameters
Room size | 6 m × 6 m × 3 m
Materials | Walls: Plaster, Ceiling: Plaster, Floor: Pinewood
Objects specifications | Cell phone: Black gloss paint (5.5 cm × 10.5 cm × 0.5 cm) Human body: Shoes: Black gloss paint Head & Hands: Absorbing Clothes: Cotton
Luminary Specifications | Brand: CR6-800L Cree Inc. Half viewing angle: 40º
Number of luminaries | 9
Number of PDs | 7
Receiver area | 1 cm2
July 2018
doc.: IEEE 11-18-1236-00-00bb
Submission
M. Uysal, F. Miramirkhani, T. Baykas, et al.

## Slide 9
Light Source
In simulation study, we use the LED luminary “CR6-800L” from Cree.
Simulated emission pattern in Zemax®
July 2018
doc.: IEEE 11-18-1236-00-00bb
Submission
M. Uysal, F. Miramirkhani, T. Baykas, et al.

## Slide 10
Based on the properties of luminary, required illumination level (150 lx) and the size of room, we arrange the luminaries as follows:
Illumination Levels
Arrangement of luminaries
Delivered light output from each luminary | 737 lumens
Average of illumination level | 153 lx
Uniformity of illumination | 0.6422
Evaluation of illumination level in Zemax®
July 2018
doc.: IEEE 11-18-1236-00-00bb
Submission
M. Uysal, F. Miramirkhani, T. Baykas, et al.

## Slide 11
Illumination Patterns
Simulated illumination levels in Zemax®
Illumination level contours in Matlab®
The minimum and maximum values of illumination are 98.69 lx and 176.40 lx.
July 2018
doc.: IEEE 11-18-1236-00-00bb
Submission
M. Uysal, F. Miramirkhani, T. Baykas, et al.

## Slide 12
Location of Test Points (Receivers)
We consider 100 cells with equidistant spacing of 0.6 m in x and y directions.
We consider a user with a height of 1.8 m who holds the phone in his hand next to his ear with 45° rotation upward the ceiling and at a height of 1.65 m. The cell phone is equipped with a single photodetector. We consider seven possible locations for the photodetectors.
Location and rotation of test points
Room under consideration
with green circles denoting luminaires
July 2018
doc.: IEEE 11-18-1236-00-00bb
Submission
M. Uysal, F. Miramirkhani, T. Baykas, et al.

## Slide 13
Sample CIR Results for D5 (1/2)
July 2018
doc.: IEEE 11-18-1236-00-00bb
Submission
M. Uysal, F. Miramirkhani, T. Baykas, et al.

## Slide 14
Sample CIR Results for D5 (2/2)
July 2018
doc.: IEEE 11-18-1236-00-00bb
Submission
M. Uysal, F. Miramirkhani, T. Baykas, et al.

## Slide 15
Sample Optical Channel Responses for D5
July 2018
doc.: IEEE 11-18-1236-00-00bb
Submission
M. Uysal, F. Miramirkhani, T. Baykas, et al.

## Slide 16
Sample Effective Channel Responses for D5
July 2018
doc.: IEEE 11-18-1236-00-00bb
Submission
M. Uysal, F. Miramirkhani, T. Baykas, et al.
In the effective channel responses of P1,3, P10,6 and P9,10, frequency selectivity are more pronounced. It is a result of the fact that these locations are close to the walls (see p. 12) and therefore more reflected rays are received (see corresponding CIRs in p. 13 and p. 14).
In the rest of this presentation, the “LED Model 1” with cut-off frequency of 20 MHz is considered.

## Slide 17
Spatial Distribution of DC Gains &
Channel Characteristics (1/2)
 | Average over 100 Cells | 
 | (ns) | 
D1 | 13.92 | 6.00×10-6
D2 | 14.10 | 6.08×10-6
D3 | 14.07 | 6.33×10-6
D4 | 14.09 | 6.89×10-6
D5 | 14.10 | 7.19×10-6
D6 | 14.06 | 6.25×10-6
D7 | 13.22 | 3.05×10-6
July 2018
doc.: IEEE 11-18-1236-00-00bb
Submission
M. Uysal, F. Miramirkhani, T. Baykas, et al.

## Slide 18
July 2018
doc.: IEEE 11-18-1236-00-00bb
Submission
M. Uysal, F. Miramirkhani, T. Baykas, et al.
Spatial Distribution of DC Gains &
Channel Characteristics (2/2)

## Slide 19
Cumulative Distribution Function (CDF)
of Path Loss
It can be noted that D1, D2, D3, D4, D5 and D6 have similar path loss values in the range of 51.95 dB-52.94 dB. In comparison to them, D7 has about 2.2 dB-3.2 dB more path loss on average since there is no LOS component.
M. Uysal, F. Miramirkhani, T. Baykas, et al.
Submission

## Slide 20
Typical office places include furniture (e.g., desk, chairs, cubicles etc), various equipments (e.g., computers, printers etc) and personnel.
Simulation Scenario 1: Office
Open Office
Office With Cubicles
July 2018
doc.: IEEE 11-18-1236-00-00bb
Submission
M. Uysal, F. Miramirkhani, T. Baykas, et al.

## Slide 21
Simulation Parameters
Room size | 14 m × 14 m × 3 m
Materials | Walls: Plaster, Ceiling: Plaster, Floor: Pinewood
Objects | 6 desks and a chair paired with each desk 6 laptops on each desk 6 cubicles (optional) 9 human bodies
Objects specifications | Cubicles: Plaster Desk: Pinewood (Typical height of 0.85 m) Chair: Pinewood Laptop: Black gloss paint Human body: Shoes: Black gloss paint Head & Hands: Absorbing Clothes: Cotton
Luminary Specifications | Brand: LR24-38SKA35 Cree Inc. Half viewing angle: 40º
Number of luminaries | 32
Receiver area | 1 cm2
July 2018
doc.: IEEE 11-18-1236-00-00bb
Submission
M. Uysal, F. Miramirkhani, T. Baykas, et al.

## Slide 22
Light Source (Transmitter)
In simulation study, we use the LED luminary “LR24-38SKA35” from Cree.
Simulated emission pattern in Zemax®
July 2018
doc.: IEEE 11-18-1236-00-00bb
Submission
M. Uysal, F. Miramirkhani, T. Baykas, et al.

## Slide 23
Based on the properties of employed luminary, required illumination level (500 lx) and the size of office place, we arrange the luminaries as follows:
Illumination Levels
Delivered light output from each luminary | 3504 lumens
Average of illumination level | 533 lx
Uniformity of illumination | 0.5211
Arrangement of luminaries
Evaluation of illumination levels in Zemax®
July 2018
doc.: IEEE 11-18-1236-00-00bb
Submission
M. Uysal, F. Miramirkhani, T. Baykas, et al.

## Slide 24
Illumination Patterns
Simulated illumination levels in Zemax®
Illumination level contours in Matlab®
Different colors show different values of illumination (lx) at the height of desk in office place. Red indicates the highest illumination level.
The minimum and maximum values of illumination are 278 lx and 712 lx respectively.
July 2018
doc.: IEEE 11-18-1236-00-00bb
Submission
M. Uysal, F. Miramirkhani, T. Baykas, et al.

## Slide 25
Location of Test Points (Receivers)
24 test points are chosen which are categorized into three groups:
In the corridors at a height of 1.7 m with 45º rotation (e.g., people who stand with a cell phone in hand) | D1-D12
On the top of chairs at a height of 0.95 m with 45º rotation (i.e., people with a cell phone in hand) | D13-D18
On the top of chairs at a height of 1.1 m with 45º rotation (e.g., people who sit with a cell phone in hand to his/her ear) | D19-D24
Location and rotation of test points
D1
D19
D13
July 2018
doc.: IEEE 11-18-1236-00-00bb
Submission
M. Uysal, F. Miramirkhani, T. Baykas, et al.

## Slide 26
Test Points (Open Office)
July 2018
doc.: IEEE 11-18-1236-00-00bb
Submission
M. Uysal, F. Miramirkhani, T. Baykas, et al.

## Slide 27
Test Points (Office with Cubicles)
July 2018
doc.: IEEE 11-18-1236-00-00bb
Submission
M. Uysal, F. Miramirkhani, T. Baykas, et al.

## Slide 28
Optical Channel Responses (Open Office)
July 2018
doc.: IEEE 11-18-1236-00-00bb
Submission
M. Uysal, F. Miramirkhani, T. Baykas, et al.

## Slide 29
Effective Channel Responses (Open Office)
July 2018
doc.: IEEE 11-18-1236-00-00bb
Submission
M. Uysal, F. Miramirkhani, T. Baykas, et al.

## Slide 30
Channel Characteristics
 | (ns) | 
D1 | 15.51 | 2.60×10-6
D2 | 18.84 | 1.36×10-6
D3 | 18.92 | 2.40×10-6
D4 | 16.97 | 3.32×10-6
D5 | 16.75 | 2.34×10-6
D6 | 17.33 | 2.60×10-6
D7 | 20.44 | 1.36×10-6
D8 | 17.83 | 2.79×10-6
D9 | 16.11 | 2.40×10-6
D10 | 15.97 | 3.12×10-6
D11 | 18.99 | 2.40×10-6
D12 | 19.57 | 1.82×10-6
D13 | 15.37 | 2.27×10-6
D14 | 16.09 | 2.21×10-6
D15 | 17.70 | 1.36×10-6
D16 | 14.74 | 2.34×10-6
D17 | 18.10 | 1.30×10-6
D18 | 16.67 | 1.95×10-6
D19 | 15.25 | 2.73×10-6
D20 | 15.81 | 1.82×10-6
D21 | 17.36 | 1.69×10-6
D22 | 18.02 | 1.36×10-6
D23 | 17.99 | 1.49×10-6
D24 | 17.85 | 1.75×10-6
July 2018
doc.: IEEE 11-18-1236-00-00bb
Submission
M. Uysal, F. Miramirkhani, T. Baykas, et al.

## Slide 31
Optical Channel Responses
(Office with Cubicles)
July 2018
doc.: IEEE 11-18-1236-00-00bb
Submission
M. Uysal, F. Miramirkhani, T. Baykas, et al.

## Slide 32
July 2018
doc.: IEEE 11-18-1236-00-00bb
Submission
Effective Channel Responses
(Office with Cubicles)
M. Uysal, F. Miramirkhani, T. Baykas, et al.

## Slide 33
 | (ns) | 
D1 | 13.80 | 2.48×10-6
D2 | 17.33 | 1.30×10-6
D3 | 16.47 | 2.30×10-6
D4 | 14.39 | 3.18×10-6
D5 | 15.17 | 2.16×10-6
D6 | 16.14 | 2.48×10-6
D7 | 18.87 | 1.24×10-6
D8 | 16.77 | 2.76×10-6
D9 | 13.91 | 2.30×10-6
D10 | 14.80 | 2.97×10-6
D11 | 16.64 | 2.39×10-6
D12 | 17.80 | 1.79×10-6
D13 | 12.80 | 2.08×10-6
D14 | 14.31 | 1.38×10-6
D15 | 14.74 | 1.27×10-6
D16 | 12.36 | 2.31×10-6
D17 | 14.92 | 1.07×10-6
D18 | 13.35 | 1.76×10-6
D19 | 13.49 | 1.95×10-6
D20 | 13.36 | 1.73×10-6
D21 | 13.38 | 1.67×10-6
D22 | 15.79 | 1.23×10-6
D23 | 15.45 | 1.44×10-6
D24 | 14.54 | 1.62×10-6
July 2018
doc.: IEEE 11-18-1236-00-00bb
Submission
M. Uysal, F. Miramirkhani, T. Baykas, et al.
Channel Characteristics

## Slide 34
In this office environment, there are two light sources; one of them is the main light source at the ceiling and the other one is mounted on the desk to provide task lighting.
Simulation Scenario 2:
Office with Secondary Light
July 2018
doc.: IEEE 11-18-1236-00-00bb
Submission
M. Uysal, F. Miramirkhani, T. Baykas, et al.

## Slide 35
Simulation Parameters
Room size | 5 m × 5 m × 3 m
Materials | Walls: Plaster, Ceiling: Plaster, Floor: Pinewood
Objects | 1 desk and a chair paired with desk 1 laptop on the desk, 1 desk light on the desk, 1 library 1 couch, 1 coffee table, window, 2 human bodies
Objects specifications | Desk: Pinewood (Typical height of 0.88 m) Chair: Black gloss paint, Laptop: Black gloss paint Desk light: Black gloss paint, Library: Pinewood, Window: Glass Couch: Cotton, Coffee table: Pinewood Human body: Shoes: Black gloss paint Head & Hands: Absorbing Clothes: Cotton
Luminary Specifications | Brand: LR24-38SKA35 Cree Inc. Half viewing angle: 40º
Number of luminaries | 1 on the ceiling 1 for the desk light
Receiver area | 1 cm2
July 2018
doc.: IEEE 11-18-1236-00-00bb
Submission
M. Uysal, F. Miramirkhani, T. Baykas, et al.

## Slide 36
Light Source (Transmitter)
In simulation study, we use the LED luminary “LR24-38SKA35” from Cree.
Simulated emission pattern in Zemax®
July 2018
doc.: IEEE 11-18-1236-00-00bb
Submission
M. Uysal, F. Miramirkhani, T. Baykas, et al.

## Slide 37
Illumination Levels
Arrangement of luminaries
Delivered light output from each luminary | 3796 lumens
Average of illumination level | 270 lx
Uniformity of illumination | 0.4409
Based on the properties of employed luminary, required illumination level (500 lx) and the size of office place, we arrange the luminaries as follows:
Evaluation of illumination levels in Zemax®
July 2018
doc.: IEEE 11-18-1236-00-00bb
Submission
M. Uysal, F. Miramirkhani, T. Baykas, et al.

## Slide 38
Illumination Patterns
Simulated illumination levels in Zemax®
Illumination level contours in Matlab®
The minimum and maximum values of illumination are 119 lx and 902 lx respectively.
July 2018
doc.: IEEE 11-18-1236-00-00bb
Submission
M. Uysal, F. Miramirkhani, T. Baykas, et al.

## Slide 39
Location of Test Points (Receivers)
2 test points are chosen:
On the desk next to the laptop at a height of 0.88 m (e.g., a USB-type device connected to laptop) | D1
On the top of desk light at a height of 1.5 m with 45º rotation toward the source on the ceiling | D2
D1
D2
July 2018
doc.: IEEE 11-18-1236-00-00bb
Submission
M. Uysal, F. Miramirkhani, T. Baykas, et al.

## Slide 40
Optical and Effective Channel Responses &
Channel Characteristics
 | (ns) | 
S→R | 11.52 | 2.84×10-5
R→D | 8.07 | 5.21×10-4
S→D | 11.11 | 1.12×10-5
July 2018
doc.: IEEE 11-18-1236-00-00bb
Submission
M. Uysal, F. Miramirkhani, T. Baykas, et al.

## Slide 41
We consider a living room with table, chairs, couch, coffee table and human bodies.
Simulation Scenario 3: Home
July 2018
doc.: IEEE 11-18-1236-00-00bb
Submission
M. Uysal, F. Miramirkhani, T. Baykas, et al.

## Slide 42
Room size | 6 m × 6 m × 3 m
Materials | Walls: Plaster, Ceiling: Plaster, Floor: Pinewood
Objects | Table with 4 chairs Couch Coffee table 4 human bodies
Object Specifications | Tables: Wooden with size of 2 m × 1 m × 0.9 m Chairs: Wooden matched with table Couch: Cotton Coffee table: Glass Human body: Shoes: Black gloss paint Head & Hands: Absorbing Clothes: Cotton
Luminary Specifications | Brand: CR6-800L Cree Inc. Half viewing angle: 40º
Number of luminaries | 9
Receiver area | 1 cm2
Simulation Parameters
July 2018
doc.: IEEE 11-18-1236-00-00bb
Submission
M. Uysal, F. Miramirkhani, T. Baykas, et al.

## Slide 43
Light Source
In simulation study, we use the LED luminary “CR6-800L” from Cree.
Simulated emission pattern in Zemax®
July 2018
doc.: IEEE 11-18-1236-00-00bb
Submission
M. Uysal, F. Miramirkhani, T. Baykas, et al.

## Slide 44
Based on the properties of luminary, required illumination level (150 lx) and the size of room, we arrange the luminaries as follows:
Illumination Levels
Arrangement of luminaries
Delivered light output from each luminary | 804 lumens
Average of illumination level | 153 lx
Uniformity of illumination | 0.9068
Evaluation of illumination level in Zemax®
July 2018
doc.: IEEE 11-18-1236-00-00bb
Submission
M. Uysal, F. Miramirkhani, T. Baykas, et al.

## Slide 45
Illumination Patterns
Simulated illumination levels in Zemax®
Illumination level contours in Matlab®
The minimum and maximum values of illumination are 139 lx and 169 lx.
July 2018
doc.: IEEE 11-18-1236-00-00bb
Submission
M. Uysal, F. Miramirkhani, T. Baykas, et al.

## Slide 46
On the coffee table at a height of 0.6 m with 45º rotation | D1
Next to the wall at a height of 1.7 m (e.g., standing people) with 45º rotation | D2-D3
On the table at a height of 0.9 m | D4-D7
On the top of couch at height of 1.1 m (e.g., sitting people) with 45º rotation | D8
Location of Test Points (Receivers)
8 test points are chosen which are categorized into four groups:
July 2018
doc.: IEEE 11-18-1236-00-00bb
Submission
M. Uysal, F. Miramirkhani, T. Baykas, et al.

## Slide 47
Optical Channel Responses
July 2018
doc.: IEEE 11-18-1236-00-00bb
Submission
M. Uysal, F. Miramirkhani, T. Baykas, et al.

## Slide 48
July 2018
doc.: IEEE 11-18-1236-00-00bb
Submission
Effective Channel Responses
M. Uysal, F. Miramirkhani, T. Baykas, et al.

## Slide 49
Channel Characteristics
July 2018
doc.: IEEE 11-18-1236-00-00bb
Submission
 | (ns) | 
D1 | 12.49 | 6.75×10-6
D2 | 11.50 | 1.22×10-5
D3 | 10.72 | 1.20×10-5
D4 | 12.70 | 9.03×10-6
D5 | 12.90 | 9.56×10-6
D6 | 12.48 | 1.01×10-5
D7 | 13.01 | 8.55×10-6
D8 | 11.88 | 9.13×10-6
M. Uysal, F. Miramirkhani, T. Baykas, et al.

## Slide 50
We consider a manufacturing cell with two robots.
Simulation Scenario 4: Manufacturing Cell
July 2018
doc.: IEEE 11-18-1236-00-00bb
Submission
M. Uysal, F. Miramirkhani, T. Baykas, et al.

## Slide 51
Room size | 8.03 m × 9.45 m × 6.8 m (See p.48 for exact layout)
Materials | Red Walls: Concrete Green Walls: Aluminum metal Blue Walls: Plexiglas (PMMA) Ceiling: Aluminum metal Floor: Concrete
Objects | Two robots
Object Specifications | Robot: Galvanized steel metal Height of Robot: 2.7 m Height of Plexiglas boundary: 2.5 m
LED Specifications | Brand: MC-E Cree Xlamp Inc. Half viewing angle: 60º
Number of LEDs | 6
Receiver area | 1 cm2
Simulation Parameters
July 2018
doc.: IEEE 11-18-1236-00-00bb
Submission
M. Uysal, F. Miramirkhani, T. Baykas, et al.

## Slide 52
Light Source (Transmitter)
In simulation study, we use the LED “Xlamp MC-E” from Cree.
Simulated emission pattern in Zemax®
Emission pattern of six LEDs which cover 360º
July 2018
doc.: IEEE 11-18-1236-00-00bb
Submission
M. Uysal, F. Miramirkhani, T. Baykas, et al.

## Slide 53
6 transmitters are located at the head of the robot, arranged on the six sides of a cube to cover 360º.
Location of Luminaries (Transmitters)
LED4
LED1
LED2
LED5
LED3
LED6
July 2018
doc.: IEEE 11-18-1236-00-00bb
Submission
M. Uysal, F. Miramirkhani, T. Baykas, et al.

## Slide 54
Test points are considered on the top of the Plexiglas boundary which are looking in the direction of the robots.
Location of Test Points (Receivers)
July 2018
doc.: IEEE 11-18-1236-00-00bb
Submission
M. Uysal, F. Miramirkhani, T. Baykas, et al.

## Slide 55
Optical Channel Responses
July 2018
doc.: IEEE 11-18-1236-00-00bb
Submission
M. Uysal, F. Miramirkhani, T. Baykas, et al.

## Slide 56
July 2018
doc.: IEEE 11-18-1236-00-00bb
Submission
Effective Channel Responses
M. Uysal, F. Miramirkhani, T. Baykas, et al.

## Slide 57
July 2018
doc.: IEEE 11-18-1236-00-00bb
Submission
TX-RX |  | (ns) | 
LED1 | D1 | 15.20 | 5.81×10-7
 | D2 | 15.68 | 1.08×10-6
 | D3 | 17.84 | 4.64×10-7
 | D4 | 17.53 | 1.01×10-6
 | D5 | 10.96 | 5.79×10-6
 | D6 | 15.13 | 7.67×10-7
 | D7 | 15.03 | 4.82×10-7
 | D8 | 12.11 | 4.77×10-6
LED2 | D1 | 13.29 | 6.94×10-7
 | D2 | 13.51 | 5.21×10-7
 | D3 | 13.66 | 4.68×10-7
 | D4 | 9.64 | 2.50×10-5
 | D5 | 14.03 | 6.30×10-7
 | D6 | 16.79 | 4.05×10-7
 | D7 | 13.00 | 5.47×10-7
 | D8 | 18.82 | 1.96×10-6
LED3 | D1 | 13.93 | 8.78×10-7
 | D2 | 11.16 | 6.35×10-6
 | D3 | 10.09 | 1.09×10-5
 | D4 | 17.59 | 5.70×10-7
 | D5 | 14.66 | 1.32×10-7
 | D6 | 15.94 | 3.55×10-7
 | D7 | 14.29 | 3.53×10-7
 | D8 | 14.24 | 1.13×10-6
TX-RX |  | (ns) | 
LED4 | D1 | 12.71 | 6.79×10-7
 | D2 | 13.23 | 1.01×10-6
 | D3 | 17.82 | 5.61×10-7
 | D4 | 16.81 | 6.60×10-7
 | D5 | 16.81 | 2.17×10-7
 | D6 | 12.92 | 3.90×10-7
 | D7 | 11.66 | 4.29×10-7
 | D8 | 11.48 | 1.27×10-6
LED5 | D1 | 16.99 | 2.55×10-7
 | D2 | 15.89 | 4.21×10-7
 | D3 | 12.96 | 4.32×10-7
 | D4 | 16.52 | 6.92×10-7
 | D5 | 14.77 | 2.88×10-7
 | D6 | 13.00 | 7.10×10-7
 | D7 | 14.48 | 3.37×10-7
 | D8 | 10.08 | 8.34×10-6
LED6 | D1 | 14.81 | 1.05×10-6
 | D2 | 13.98 | 2.68×10-6
 | D3 | 12.19 | 5.75×10-6
 | D4 | 8.84 | 5.78×10-5
 | D5 | 15.39 | 3.48×10-7
 | D6 | 14.40 | 1.25×10-6
 | D7 | 14.24 | 9.74×10-7
 | D8 | 13.19 | 2.75×10-6
TX-RX |  | (ns) | 
All LEDs | D1 | 15.66 | 7.78×10-7
 | D2 | 15.52 | 1.99×10-6
 | D3 | 14.13 | 2.96×10-6
 | D4 | 10.45 | 1.43×10-5
 | D5 | 16.42 | 1.29×10-6
 | D6 | 14.85 | 8.15×10-7
 | D7 | 15.83 | 3.78×10-7
 | D8 | 13.58 | 3.10×10-6
M. Uysal, F. Miramirkhani, T. Baykas, et al.
Channel Characteristics

## Slide 58
July 2018
doc.: IEEE 11-18-1236-00-00bb
Submission
M. Uysal, F. Miramirkhani, T. Baykas, et al.
Conclusions
  This contribution proposes LiFi reference channel models for indoor environments to assist the IEEE 802.11bb.
  Our results are extended versions of the previous contribution in 802.15.7r1 where the effect of LED response is further considered.

## Slide 59
July 2018
doc.: IEEE 11-18-1236-00-00bb
Submission
M. Uysal, F. Miramirkhani, T. Baykas, et al.
Acknowledgement
The work of M. Uysal and T. Baykas was supported by the Turkish Scientific and Research Council (TUBITAK) under Grant 215E311.