## Slide 1: Remaining issues on individually-addressed BU delivery
Date: 2018-07-09
Authors:

## Slide 2: Remaining issues on individually-addressed BU delivery
WUR AP may send a WUR Wake Up frame to indicate that individually addressed BU(s) are available
  If the Wake-up frame is addressed more than one STAs, AP may use any AC for sending the Wake-up frame
  1) The AC for sending individually-addressed Wake-up frame hasn’t been defined
The STA wakes up its PCR after receiving a Wake-up frame addressed to it
  After the STA wakes up, it sends a poll frame in response to the received Wake-up frame
    PS-Poll, U-APSD trigger, A frame with PM bit of 0 for Active mode
The delivery of buffered BU starts, following the existing PS operation
  2) Poll frame mismatch problem might increase the latency of BU delivery

## Slide 3: Background: Legacy power save operation
The AP shall buffer individually addressed BUs addressed to a PS STA
  These buffered BUs shall be transmitted only at designated times
The existing PS operations (e.g., PSP, U-APSD) define the designated condition for transmitting the buffered BUs
  PS STA designates each AC to use either PSP or U-APSD
  In PSP,
    STA checks TIM element and transmits PS-poll
    AP delivers buffered BUs using non delivery-enabled AC in response to the PS-poll
  In U-APSD,
    STA transmits an U-APSD trigger to retrieve buffered BUs of delivery(trigger)-enabled AC in an active manner
    AP delivers buffered BUs using delivery-enabled AC in response to the U-APSD trigger
In legacy PS operation, non-AP STA triggers AP to deliver buffered BU by sending a poll frame

## Slide 4: Poll frame mismatch problem in WUR Mode
In WUR operation, AP triggers a non-AP STA to retrieve buffered BUs by sending a Wake-up frame
  for both delivery-enabled ACs (U-APSD) and non delivery-enabled ACs (PSP)
However, the STA can not know in which AC buffered BUs are present
If a wrong poll frame is sent, AP may not deliver intended buffered BU properly
  In the worst case, the STA may enter doze state without having buffered BU delivered
Further clarification is necessary for better integration with legacy PS operation
WUF
PS-poll
Ack
VO
VI
U-APSD
BE
BK
Normal PS
BU for VO
WUF
trigger frame
Ack
VO
VI
U-APSD
BE
BK
Normal PS
BU for BE
SP early termination
QoS Null EOSP:1
Ack
STA remains awake until it receives one BU
AP
STA
AP
STA
Beacon
TIM:0
Enter to doze state
Response frame
Response frame

## Slide 5: Poll frame mismatch situation (1)
AP sends a Wake-up frame to indicate the availability of buffered BUs using non delivery-enabled AC
The STA sends a U-APSD trigger as a response frame after its PCR wakes up
Since the AP doesn’t have any buffered BU using delivery-enabled AC, it transmits QoS Null frame with EOSP:1
  AP may set More Data subfield to 1 indicating the availability of BU using non delivery-enabled AC
STA sends PS poll in the next TXOP
WUF
trigger frame
Ack
VO
VI
U-APSD
BE
BK
Normal PS
BU for BE
SP early termination
QoS Null EOSP:1
MD: 1
Ack
AP
STA
Response frame
PS-poll
Ack
Ack
BU
(VO)

## Slide 6: Poll frame mismatch situation (2)
AP sends a Wake-up frame to indicate the availability of buffered BUs using delivery-enabled AC
The STA sends a PS-poll as a response frame after its PCR wakes up
Since the AP doesn’t have any buffered BU using non delivery-enabled AC, it may not transmit anything
The STA remains awake until it checks TIM element in the Beacon
Since the TIM element does not indicate the availability of BUs using delivery-enabled AC, the STA enter to doze state and WURx operation
WUF
PS-poll
Ack
VO
VI
U-APSD
BE
BK
Normal PS
BU for VO
STA remains awake until it receives one BU
AP
STA
Beacon
TIM:0
Enter to doze state
Response frame

## Slide 7: Possible approaches (1)
1) Not sending a Wake-up frame for U-APSD data
  Following the concept of the legacy operation, let the STA trigger BU retrieving for U-APSD traffic
  However, not only the usage of wake-up frame is restricted, but also it requires STA to send U-APSD trigger frames periodically using PCR
2) Having a 1-bit indication in Wake-up frame (PSP/U-APSD flag)
  Using the information, STA can choose an appropriate poll frame, and may choose the retrieving timing for U-APSD
  However, it is not desirable that Wake-up frame contains PCR control information influencing PCR behavior of the non-AP STA

## Slide 8: Possible approaches (2)
3) AP sending buffered BU without regard to the type of received poll
  Once the AP delivers the intended buffered BU to the STA, the STA may follow the existing PCR operation subject to the received BU
We prefer option 3)
  It requires minimal change only on AP’s behavior
  No additional signaling overhead is required
WUF
PS-poll
Ack
VO
VI
U-APSD
BE
BK
Normal PS
BU for VO
WUF
trigger frame
Ack
VO
VI
U-APSD
BE
BK
Normal PS
BU for BE
Ack
BU
(VO)
Ack
AP
STA
AP
STA
Ack
BU
(VO) EOSP:1
Enter to doze state
BU
(BE)
MD:1
PS-poll
Ack
BU
(BE)
MD:0
Enter to doze state

## Slide 9: Proposal
31.7.3 non-AP STA Operation
  An AP that transmits a WUR Wake-up frame to a non-AP STA that indicates the availability of individually addressed buffered BU(s) via the PCR shall follow the existing PCR operation to deliver individually addressed buffered BU(s) to the non-AP STA, except that AP may deliver the buffered BU(s) without regarding the type of the response frame sent by the non-AP STA. When the AP schedules a transmission to the non-AP STA, the AP shall ensure that either of the conditions below is met:
    The PCR transition delay indicated by the non-AP STA in the WUR Capabilities elements following the most recent transmitted WUR Wake-up frame intended to the non-AP STA has expired.
    The non-AP STA has indicated that it is in awake state by transmitting a frame through the PCR to the AP.

## Slide 10: Strawpoll 1
Do you agree the following modification?
31.7.3 non-AP STA Operation
  An AP that transmits a WUR Wake-up frame to a non-AP STA that indicates the availability of individually addressed buffered BU(s) via the PCR shall follow the existing PCR operation to deliver individually addressed buffered BU(s) to the non-AP STA, except that AP may deliver the buffered BU(s) without regarding the type of the response frame sent by the non-AP STA. When the AP schedules a transmission to the non-AP STA, the AP shall ensure that either of the conditions below is met:
    The PCR transition delay indicated by the non-AP STA in the WUR Capabilities elements following the most recent transmitted WUR Wake-up frame intended to the non-AP STA has expired.
    The non-AP STA has indicated that it is in awake state by transmitting a frame through the PCR to the AP.
  Y/N/A