## Slide 1: 802.11ax operation in 6GHz band
Date: 2018-07-08
Authors:

## Slide 2: Background
IEEE802.11ax has enabled these main features
  Downlink (DL)/ Uplink (UL) Multi-user (MU) operation based on
    Spatial (MIMO) and frequency (OFDMA) multiplexing
  AP-centric scheduling based on
    UL Trigger-based operation
    Target Wake Time (TWT) operation
      TDMA-like mechanism used to efficiently allocate DL/UL (MU) resources
  Spatial Reuse (SR) operation
    Transmit on top of ongoing transmissions under certain conditions
    Both managed and unmanaged SR (using OBSS PD and SRP)
  Dual band operation in 2.4 GHz and 5 GHz
    Using bandwidths of up to 40 MHz in 2.4 GHz and up to 160MHz in 5 GHz
    Preserving backwards compatibility with legacy 11a/b/n/ac devices
TGax PAR already accounts for 6 GHz operation
  However the details for operating in this greenfield band are yet to be defined

## Slide 3: Network Discovery And Scanning
Scanning may be due to two reasons:
  Initial Network Discovery: STAs that are not associated with any APs, scanning for a network
  Roaming: STAs that are associated with an AP, trying to find a better AP
Proposal: Have a unified signaling that addresses both cases
General assumptions & principles for the solutions considered
  Use 5/2.4 GHz bands for discovery purposes
  Allow 6 GHz roaming only under certain conditions
  AP should be able to control Probe Req. sent in 6 GHz

## Slide 4: Active scanning in 6 GHz band
STAs send Probe Req to 5/2.4 GHz AP
  Active scanning is concentrated in 2.4 and/or 5 GHz bands
5/2.4 GHz AP sends Probe Resp containing information related to 6 GHz discovery/operation
  E.g., channel number, BSSID, EDCA intervals of the target co-located 6 GHz AP
STA sends management frame in the 6 GHz channel only during the allowed time window
  E.g., STA sends unicast Probe Req to that AP using EDCA access or in response to a Trigger frame for random access
STA associates with 6 GHz BSS using 6 GHz radio
  No need for sharing of association between 2.4/5 GHz & 6 GHz
For roaming in 6 GHz, STA gets information to access neighboring BSS from the associated 6 GHz AP
  If the AP does not provide this information, the STA sends Probe Req in 5/2.4 GHz and follow the above procedure
5/2.4GHz
6GHz
Beacon
Beacon
Beacon
Beacon
Probe Req
Probe Resp
Beacon
EDCA periods/intervals
Probe Req
Probe Resp
STA tunes to 6GHz
for the next EDCA interval

## Slide 5: Post-association medium access
Relies on the following concepts
    Trigger-based access: STAs respond to Trigger frames
      Preferred mode of operation
    Scheduled EDCA access: EDCA only in scheduled SPs
      AP indicates intervals of time during which EDCA is allowed
      STAs can contend using EDCA during these time intervals
      STAs are not allowed to contend outside of these intervals

## Slide 6: Controlled EDCA operation
Access point controls the EDCA access of each STA (e.g. by setting AIFSN = 0 in EDCA Parameter Set Element)
EDCA control could be based on (a) a window as shown in the figure above, or (b) could be applicable for the entire operation
  Needs further discussion to decide the preferable option for 11ax
EDCA everywhere else
AP
Non-AP STA
No EDCA

## Slide 7: Transmit Power Control
TPC service provides for the following:
  Association of STAs with an AP based on the STAs’ power capability
  Specification of regulatory and local max transmit power (TP) levels for current channel
  Selection of TP for each TX within constraints imposed by regulatory requirements
  Adaptation of TP based on a range of info., including path loss and link margin estimates
We propose TPC be preserved as mandatory for all 6 GHz STAs
  Inherit main TPC functionalities to the 6 GHz domain to achieve, among other things:
    Compliance: Satisfy regulatory requirements, if any (de-facto adaptation of existing rules)
    Performance: TP selection and adaptation to control BSS range, mitigate interference, etc.
A STA informs an AP of its min/max transmit power capabilities when (re-)associating
  Power Capability IE present in (Re-)Association Request frames transmitted by the STA
An AP might use the TP capabilities received from the STAs to:
  Determine the local transmit power constraint for any BSS that it maintains
  Determine if the association request should be rejected due to unacceptable levels of min/max transmit power capabilities of the STA

## Slide 8: Transmit Power Control (contd.)
AP declares the local maximum transmit power in the Power Constraint IE
  This is the maximum transmit power allowed for the current channel of the 6G BSS
  The Power Constraint element is included in Beacons, Probe Responses, etc.
    Can be provided by AP in MGMT frames transmitted in 2.4/5 GHz
Pre-association: Unassociated STA receive power control info. from
  Co-located 2.4/5 GHz AP, 6 GHz AP or 2.4/5/6 GHz neighbor AP
Post-association: STAs transmissions in the channel are subject to the following:
  Shall determine the regulatory max TP and local max TP for a channel in the current regulatory domain before transmitting in the channel
  An AP shall use a TP less than or equal to the regulatory max TP level for the channel
  A non-AP STA shall use a TP less than or equal to the local max TP level for the channel
  A STA may use any criteria, and in particular any path loss and link margin estimates, to dynamically adapt the transmission power for transmission to another STA