## Slide 1: 60GHz LOSNLOS test
Date: 2018-07-05
Authors:

## Slide 2: Abstract
In this contribution we propose a protocol to enable determining whether a transmission is LOS or NLOS based on transmitting and receiving through different polarization.
PHY support was implemented in 11ay

## Slide 3: How it should work
The ISTA sends a frame with TRN subfields. In every TRN subfield it switches polarization while maintaining the same AWV.
The RSTA receives this while switching polarization on every TRN subfield
  The RSTA performs measurements of amplitude and phase on all these fields.
The RSTA sends a frame with TRN subfields. It switches Polarization on every subfield.
The ISTA switches polarization on every received TRN subfield
The RSTA sends measurements results (on the first frame) to the ISTA

## Slide 4: How Does It work (cont.)
How does the RSTA knows that the packet contains TRN subfields that require polarization switching:
  A field in the PHY header indicates that.
  Another field in the header indicates that the TRN field
Does the response need to be immediate?
  In the FTM process we separate the request and response to two separate medium accesses.
Can it work in DMG
  We cannot indicate the required fields in the DMG header, only in the EDMG
    Will complicate the protocol.

## Slide 5: What we propose?
A new exchange:
  FTM with LOS test request/ACK
  FTM with LOS test response/ACK
These new type of exchanges
  The FTM LOS Text request is identified by a new trigger value
    PHY can analyze required actions from the EDMG PHY-header
  The FTM response is a regular FTM frame with results + EDMG/DMG Channel Measurement Response
    Paired with the request using the dialog token

## Slide 6: Required Changes
Add a field to DMGz/EDMGz direction measurement parameter element indicating that LOS test may happen before or between the FTM bursts.
Add a new trigger value to the FTM trigger indicating the start of an FTM LOS test exchange
Allow transmission of EDMG/DMG channel measurement feedback element in an FTM (LOS test response) frame.
  Response frame with trigger set to 0.
  Paired with request by the dialog token.

## Slide 7: Straw Poll
Do you agree to the changes proposed in slide 6.

## Slide 8: Backup

## Slide 9: Justification
At odd TRN subfields indices
STA A transmits in Polarization 1 + 90°
STA B receives in polarization 1 + 90°
In LOS the power remains the same as the difference in TX and RX polarization remains the same
In NLOS, the reflection may have different power change for different polarizations, and also the phase may change.
Comparing the power, the device that has the power measurement can determine that the measurement is based on reflection(s).
At even TRN subfields indices
STA A transmits in Polarization 1 (can be either H or V in its point of view)
STA B receives in Polarization 1
The power is measured