## Slide 1: LMR AoA Feedback
Date: 2018-07-10
Authors:

## Slide 2: Background
Angular in Tgaz
  Subsection for sub 7 GHz angular removed from SFD
  Now only specific support for AoD/AoA in DMG/eDMG
Existing Angular
  Sub 7 GHz AoA already implemented using proprietary receive array processing
  Does not need specific protocol support
  Usually at APs, can be used in network-centric localization
  Would be beneficial also in client-centric localization
There is a need to share AoA Measurements from AP with STA
  RSTA-ISTA LMR is an obvious place to feed back per packet (NDP) AoA measurements

## Slide 3: AoA Feeback in LMR
Angle-of-Arrival (AoA)
  Can be measured on each NDP
  Could be fed back in LMR
Format
  2 octets Azimuth/Elevation
  2 octets for accuracy

## Slide 4: Format New or Reuse?
Alternative Format
  Reuse AoA Results Field
  Created for DMG/eDMG
  5 octets

## Slide 5: Addition to Location Civic Report
Angular Measurements Need a Reference Orientation
  “True North”
  Spherical coordinates can be transformed/rotated to include orientation
    Many receive arrays only measure partial spherical coordinates, e.g., azimuth only
    Or accuracy is not uniform
  Easier to let AP specify it’s own coordinate system

## Slide 6: Strawpoll 1
Do you support to include optional Angle-of-Arrival (AoA) feedback in the Fine Timing Measurement Report field of the VHTz and HEz LMR (RSTA-ISTA)?
  Yes: No: Abstain:

## Slide 7: Motion 1
We agree to include optional Angle-of-Arrival (AoA) feedback in the Fine Timing Measurement Report field of the VHTz and HEz LMR (RSTA-ISTA)
  Yes: No: Abstain: