## Slide 1: 60GHz Passive Location Justification
Date: 2018-07-05
Authors:

## Slide 2: Abstract
We discuss the justification of 60GHz passive location protocols. We examine whether passive location would provide lower power consumption on mobile 60HGz stations and medium time used for location.

## Slide 3: Case I: 60GHz passive location in stadium
Location APs stationed above stadium.
3APs stationed above each block of 50x50 meters, 20m above seats
In each block of 50x50 meters there are ~2500 seats
30-50 users need location service concurrently.
They need location computation every 1s.
Using active location they will use 3ms (each) to do that (sector sweep + BRP).
20 users per AP - 60ms. 6% of AP time. Some contention issues.
Passive location - 3ms per 1s - 0.3% of AP time - however, occasionally STAs may want to acquire passive location schedule. Not clear whether it is optimal to do it using <6GHz band.

## Slide 4: Case II – 60GHz passive location in a mall
Accurate location in shopping mall
Area of mall 12x50m, 2 floors.
3 APs located on ceiling above second floor, 10m apart.
10 users need location service
Using active location they will use 3ms each to do that (sector sweep+BRP)
5 users per AP - 15ms - 1.5% of AP time.
Passive location, 3ms per 1s - 0.3of AP time.

## Slide 5: References