## Slide 1: Agenda for IEEE 802.11 Coexistence SC meeting in Hawaii in Sept 2018
12 Sept 2018
Authors:
Name | Company | Phone | email
Andrew Myles | Cisco | +61 418 656587 | amyles@cisco.com

## Slide 2: Welcome to the 8th F2F meeting of the Coexistence Standing Committee in Hawaii in Sept 2018
  The IEEE 802.11 PDED ad hoc was formed in September 2016 at the Warsaw interim meeting
    To discuss issues related to the 3GPP RAN1 request to IEEE 802.11 WG to adopt an ED of -72dBm
  The IEEE 802.11 PDED ad hoc met in San Antonio (Nov 2016), Atlanta (Jan 2017), Vancouver (Mar 2017) and Daejeon (May 2017)
  In Daejeon in May 2017 it was decided to convert the IEEE 802.11 PDED ad hoc into the IEEE 802.11 Coexistence SC
  The IEEE 802.11 Coexistence SC met in Berlin (July 2017), Hawaii (Sept 2017), Orlando (Nov 2017), Irvine (Jan 2018), Chicago (Mar 2018), Warsaw (May 2018), San Diego (July 2018) and will meet twice this week
    Wed PM1
    Thu PM1

## Slide 3: The first task for the Coexistence SC today is not to appoint a secretary
  It is important to keep proper minutes of all Coexistence SC meetings
  Fortunately, Guido Hiertz (Ericsson) agreed in Berlin to be appointed the IEEE 802.11 Coexistence SC’s permanent Secretary …

## Slide 4: The Coexistence SC will review the official IEEE-SA patent material for pre-PAR groups

## Slide 5: The Coexistence SC hoc will operate using accepted principles of meeting etiquette
  IEEE 802 is a world-wide professional technical organization
  Meetings shall be conducted in an orderly and professional manner in accordance with the policies and procedures governed by the organization
  Individuals shall address the “technical” content of the subject under consideration and refrain from making “personal” comments to or about others

## Slide 6: The Coexistence SC will review the modified “Participation in IEEE 802 Meetings” slide
Participation in any IEEE 802 meeting (Sponsor, Sponsor subgroup, Working Group, Working Group subgroup, etc.) is on an individual basis
  Participants in the IEEE standards development individual process shall act based on their qualifications and experience (IEEE-SA By-Laws section 5.2.1)
  IEEE 802 Working Group membership is by individual; “Working Group members shall participate in the consensus process in a manner consistent with their professional expert opinion as individuals, and not as organizational representatives”. (sub-clause 4.2.1 “Establishment”, of the IEEE 802 LMSC Working Group Policies and Procedures)
  Participants have an obligation to act and vote as an individual and not under the direction of any other individual or group. A Participant’s obligation to act and vote as an individual applies in all cases, regardless of any external commitments, agreements, contracts, or orders
  Participants shall not direct the actions or votes of any other member of an IEEE 802 Working Group or retaliate against any other member for their actions or votes within IEEE 802 Working Group meetings, (IEEE-SA By-Laws section 5.2.1.3 and the IEEE 802 LMSC Working Group Policies and Procedures, subclause 3.4.1 “Chair”, list item x)
By participating in IEEE 802 meetings, you accept these requirements. If you do not agree to these policies then you shall not participate

## Slide 7: The Coexistence SC will consider a proposed agenda for Hawaii
Proposed Agenda
  Bureaucratic stuff, including approving minutes
  What is happening this week? (in no particular order)
    Scope of IEEE 802.11 Coexistence SC (a reminder)
    Relationships
      Review upcoming ETSI BRAN meeting agenda & submissions
      Discuss response from 3GPP RAN to workshop invitation
      Discuss response from 3GPP RAN4 to LS
      Review recent 3GPP RAN1 activities
      …
    Technical issues
      Adaptivity in EN 301 893
      Blocking energy in ETSI BRAN
      “Paused COT” interpretation in EN 301 893
      Greenfield coexistence
      …
Additional agenda items are requested from all interested stakeholders

## Slide 8: The Coexistence SC will consider a proposed agenda for Hawaii
Proposed Agenda
    …
    Other issues
      …
  Other business
Additional agenda items are requested from all interested stakeholders

## Slide 9
  Scope of IEEE 802.11 Coexistence SC

## Slide 10: The agreed Coexistence SC scope focuses on ensuring 802.11ax has fair access to global unlicensed spectrum
Discuss the use of PD, ED or other 802.11 coexistence mechanisms with the goal of promoting “fair” use of unlicensed spectrum
Promote an environment that allow IEEE 802.11ax “fair access” to global unlicensed spectrum
Will initially focus on liaising with 3GPP RAN/RAN1/RAN4 but may also lead to interactions with regulators and other stakeholders
Will probably not conclude at least until RAN4’s 802.11/LAA coexistence testing is defined and successfully executed
May require the SC to consider other simulations and results of tests of potential LAA/802.11 coexistence mechanisms
Will initially focus on encouraging a “technology neutral” solution in the next revision of EN 301 893 that allows IEEE 802.11ax fair access to unlicensed spectrum in Europe (noting the European approach is likely to have global impact)
The effort will also focus on allowing 802.11ax to use innovative mechanisms for frequency reuse without compromising the goal of fair access

## Slide 11: Coexistence SC will close when determined by the 802.11 WG or 802.11ax is ratified
IEEE 802.11 Coexistence SC close down criteria
  The SC is closed by the IEEE 802.11 WG
    … after it is determined that the SC is unlikely to make further progress towards its goals
  IEEE 802.11ax completes Sponsor Ballot
    … noting that the Coexistence SC ad hoc is unlikely to be relevant at that point anyway

## Slide 12
  Minutes

## Slide 13: The Coexistence SC will consider approval of the meeting minutes from San Diego
  The minutes for the Coexistence SC at the San Diego meeting in July 2018 are available on Mentor:
    11-18-1333-00
  Motion:
    The IEEE 802 Coex SC approves 11-18-1333-00 as minutes of its meeting in San Diego in July 2018
    Moved:
    Seconded:
    Result:

## Slide 14
  Agenda items
  Review of next ETSI BRAN meeting

## Slide 15: The Coex SC will discuss the ETSI BRAN meeting to held next week
  The next meeting of ETSI BRAN will be held next week
    Dates: 18-21 Sept 2018
    Location: Sophia Antipolis
  The Coex SC will hear a full report of the meeting agenda & submission particularly on issues related to:
    Timeline
    Adaptivity
    Paused “COT” feature
    Editorial issues
    Blocking energy
    …

## Slide 16: The ETSI BRAN agenda will focus on EN 301 893 topics next week, including adaptivity
  The ETSI BRAN agenda next week will focus on EN 301 893
  The ETSI BRAN Chair notes:
    For this standard we have been concentrating mainly on Adaptivity so far, but we need now also to focus on the other parts.
  He has therefore put forward an agenda in three parts:
    Adaptivity
    RX Requirements to be revised and/or included
    How to include the 5.8 GHz UK frequencies into EN 301 893
  The Coexistence SC is mostly interested in the adaptivity aspects but we can consider other aspects if desired

## Slide 17: It is important for ETSI BRAN to move past the adaptivity aspects of EN 301 893
  BRAN (18)099004 (Cisco) makes the case that ETSI BRAN needs to complete EN 301 893 ASAP …
  … and not just the adaptivity part
  While the Coexistence SC should continue to assist ETSI BRAN to refine adaptivity in EN 301 893 …
  … we should also be aware of the risk of too much delay …
  … which is the long term use of Notified Bodies by vendors

## Slide 18: The long term use of Notified Bodies has cost and delay impacts on the industry
  Notified bodies can undertake conformance assessments against European legislation with using a Harmonised Standard
    Such as EN 301 893
  The main problem with using a Notified Body without a Harmonised Standard is that it is a slow & very expensive process
    It requires the Notified Body determine & test conformance without the benefit of a Harmonised Standard
What is a Notified Body?
A notified body is an organisation designated by an EU country to assess the conformity of certain products before being placed on the market
These bodies carry out tasks related to conformity assessment procedures set out in the applicable legislation, when a third party is required.
The European Commission publishes a list of such notified bodies.
Source: ec.europa.eu

## Slide 19: ETSI BRAN is considering the inclusion of 5.8 GHz into EN 301 893
  The current ETSI BRAN 5GHz WI includes the incorporation of 5.8 GHz frequencies into EN 301 893
  There have been concerns raised during the past few meetings on how this actually should be done.
  ETSI BRAN is likely to discuss a number of options:
    Including the 5.8 GHz frequencies in the main part of the document (as it is done in the current draft)
    Including the 5.8 GHz frequencies into a normative annex
    …
  This is probably a topic more applicable for consideration by IEEE 802.18 …

## Slide 20: ETSI BRAN is discussing the inclusion of Receiver Sensitivity parameters in EN 301 893
  There is a proposal from the ETSI BRAN Chair on how they could include Receiver Sensitivity into EN 301 893
  The ETSI BRAN Chair asks for contributions from those who believe RX requirements, should be included in EN 301 893
  Additionally, he notes that for those receiver requirements (from the ETSI Guide) which will NOT be in EN 301 893, ETSI BRAN will need to develop a justification for why each parameter should not be included

## Slide 21: Why is EN 301 893 so important? It provides a basis for fair sharing among all technologies
  This SC has spent a lot of time considering the activities in ETSI BRAN, particularly the development of adaptivity rules for 5GHz in Europe
  BRAN(18)0990023r1 provides one perspective based on coexistence testing of actual LAA deployments of LAA
    It also provides an update of the known deployment status of LAA
    The bottom line is that EN 301 893 provides a basis for ensuring fair sharing among all technologies
  The SC may discuss BRAN(18)0990023r1 after presentation

## Slide 22: The following slides summarise adaptivity submissions to ETSI BRAN for discussion by the SC
  The following slides summarise the submissions that have been made to ETSI BRAN of relevance to 802.11 on the topic of coexistence
  The purpose of discussing them in the SC today is to:
    Make 802.11 stakeholders aware of issues of potential importance
    Allow 802.11 stakeholders to discuss and possibly come to consensus on the best way forward
  The conclusions of today’s discussion will be recorded in the minutes and will assist 802.11 stakeholders that participate in ETSI BRAN
  However, these conclusions do not represent the position of the IEEE 802.11 WG unless they are approved by the WG (on Friday)
  Anyone who would like a formal WG position to be established on any matter is requested to submit a recommendation for consideration by the SC on Thursday

## Slide 23: ETSI BRAN will consider submissions on potential editorial ambiguities in EN 301 893
Submissions
  BRAN(18)099002r1: Clarifications of adaptivity ambiguities in EN 301 893
    Authors: Cisco, Intel, Broadcom
    Suggests various clarifications to ambiguities related to adaptivity
      The same threshold must be used in all channels … whereas each channel should use an independently determined threshold
      The use of a -62 dBm threshold is conditional on finding a preamble … whereas it should depend on the existence of a process to detect preambles
      The threshold is integrated over multiple channels … whereas the threshold should be integrated over each 20 MHz channel
  BRAN(18)099018: Response to BRAN(18)099002
    Author: Ericsson
    Objects to suggestion that the threshold should be integrated over each 20 MHz channel, preferring the integration occur over the 20/40/80/… channel
    Asserts that such a change will severely impact existing & upcoming IEEE 802.11 products
File link

## Slide 24: ETSI BRAN will consider submissions on potential editorial ambiguities in EN 301 893
Discussion
  It turns out that the disagreement highlighted by the two presentations was the result a misreading/understanding of the proposed text (ie Guido was right!)
  Refined text is now proposed:
    Equipment shall consider a channel to be occupied as long as other RLAN transmissions are detected at a level greater than the ED Threshold Level (TL). The received power ED Threshold Level (TL) is integrated over the total Nominal Channel Bandwidth of all Operating Channels used by the equipment, then normalized to per MHz power and compared against the ED Threshold Level (TL).
  Is there any discussion?

## Slide 25: ETSI BRAN will consider a proposal to refine the “paused COT” requirements
Submission
  BRAN(18)099003r1: Paused COT in EN 301 893
    Authors: Cisco, Intel, Broadcom
    Proposes refining the “paused COT” feature requirements to:
      Account for the revised adaptivity clause (as agreed at the last ETSI BRAN meeting)
      Ensure that a system using the “paused COT” feature cannot interfere with another COT during a 16 µs gap
Discussion
  ETSI BRAN has not received any objection to this proposal
  Is there any discussion from the SC?

## Slide 26: ETSI BRAN will consider a proposal (again) to deal with blocking energy
Submissions
  BRAN(18)099005r1 - Blocking energy update
    Author: Cisco
    Proposes that ETSI BRAN notify 3GPP RAN1 that the use of blocking energy by some LAA implementations is not allowed
  BRAN(18)099007 - Clarifications on blocking energy
    Author: BMWi
    Clarifies that German regulations do not disallow the use of blocking energy as used by LAA
Discussion
  There is a more detailed item on blocking energy later in the agenda

## Slide 27: ETSI BRAN will consider a proposal to revise the Channel Occupancy Time definition
Submissions
  BRAN(18)099013r1 – Definition of COT for EN 301 893
    Author: Broadcom
    Proposes a revised Channel Occupancy Time definition
Discussion
  ETSI BRAN has not received any objection to this proposal
  Is there any discussion from the SC?
    It does not seem to allow for a paused COT
    It loses the restriction that a Channel Occupancy must be complete with 20ms

## Slide 28: ETSI BRAN will consider a proposal to avoid a responding device obtaining unfair access
Submissions
  BRAN(18)099014 - SharingCOT_for_EN 301 893
    Author: Broadcom
    Notes that a device using a low max tx power (and thus a high ED threshold) to gain access to the medium could pass control of the COT to device using a much higher max tx power – and this would provide unfair access to the high mx tx power device
    Proposes that the responding device use a max tx power no higher than the initiating device that gained control of the medium
Discussion
  ETSI BRAN has not received any objection to this proposal
  Is there any discussion from the SC?

## Slide 29: ETSI BRAN will consider a proposal to restrict a initiating devices from restarting after a “pause”
Submissions
  BRAN(18)099015 - Multiple UL DL Switching for EN 301 893
    Author: Broadcom
    Observes that RAN1 is discussing the possibility of multiple “paused” UL/DL transitions (each with only a 25us LBT) contrary to the intent of the “paused COT”
    Proposes making it clear that an initiating device cannot regain control of the medium after a pause in a COT
Discussion
  ETSI BRAN has not received any objection to this proposal
  Is there any discussion from the SC?
    This is an example of a feature (paused COT) that was agreed to as a concession, but has been misused by some in RAN1

## Slide 30: ETSI BRAN will consider a proposal to remove the test by declaration options
Submissions
  BRAN(18)099017 – Removal of declaration option
    Author: Ericsson
    Proposes removing the option to “test” the channel access mechanism and the maximum channel occupancy time by “declaration”
    Justifies on basis that:
      Test equipment vendors and test labs are prepared to certify products under version 2.1.1 of EN 301 893
      An option to declare compliance is prone to be questioned during the EC’s review
File link

## Slide 31: ETSI BRAN will consider a proposal to remove the test by declaration options
Discussion
  ETSI BRAN has not received any objection to this proposal
  Is there any discussion from the SC?
    Less testing is better for cost reasons and so imposing tests only makes sense from a vendor perspective if the EC will really object; will they?
    Are we confident the tests actually test what we think they test? Have they been tested against multiple devices?

## Slide 32: ETSI BRAN will consider a proposal to define use of PD by referring to 802.11-2016 clause 17.3.6
Submissions
  BRAN(18)099019 – Modification of the ED clause in EN 301 893
    Author: Ericsson
    Suggests specifying the PD mechanism by reference to clause 17.3.6 in 802.11-2016, rather than clause 17.3
Discussion
  ETSI BRAN has not received any objection to this proposal
  Is there any discussion from the SC?
    Is there any benefit from referring to 17.3.6 rather than 17.3?
    The second attached Word file contain material that does not seem to relate to the ppt explanation, including language to make the use of PD an “exception”; this seems to be contrary the agreement at the last ETSI BRAN meeting
File link

## Slide 33: ETSI BRAN will consider a proposal to test the use of PD
Submissions
  BRAN(18)099020 – Details on PD testing
    Author: Ericsson
    Suggests specifying a test for the use of the PD mechanism at -82dBm
Discussion
  ETSI BRAN has not received any objection to this proposal
  Is there any discussion from the SC?
    Less testing is better for cost reasons and so imposing tests only makes sense from a vendor perspective if they can’t be avoided
    Does the test actually test what it claims to test?
    Does there need to be some wiggle room in -82 dBm and -62 dBm parameters used in the test?
File link

## Slide 34: ETSI BRAN will consider a proposal to inject noise during ED tests
Submissions
  BRAN(18)099021 – Modification to ED threshold test
    Author: Ericsson
    Proposes the injection of noise at -92dBm when undertaking ED tests to simulate “real world conditions”
Discussion
  ETSI BRAN has not received any objection to this proposal
  Is there any discussion from the SC?
    Less testing is better for cost reasons and so imposing tests only makes sense from a vendor perspective if they can’t be avoided
    Does the test actually test what it claims to test?
    Does the test have much value?
File link

## Slide 35: ETSI BRAN will consider a proposal related to editorial issues
Submissions
  BRAN(18)099022 – Editorial modifications to EN 301 893
    Author: Ericsson
    Highlights various editorial issues
Discussion
  ETSI BRAN has not received any objection to this proposal
  Is there any discussion from the SC?
    These are really issues for ETSI BRAN
File link

## Slide 36
  3GPP NR-U
  Status report on the most recent 3GPP RAN1 meeting

## Slide 37: The Coex SC will hear an update on coexistence relevant activities at the recent 3GPP RAN1 meeting
  The Coex SC may hear a status update … focused on coexistence issues of course!
    Sindhu Verma (Broadcom) & Shubho Adhikari (Broadcom) have provided a report that will be presented by David Boldy (Broadcom)
  The report is in 11-18-1642-00 but will be split into different topics during the remainder of the agenda
    Slides 4-5: use of no LBT or short LBT for control messages
    Slide 7: sharing in 6Ghz of relevance to Workshop discussion
    Slides 8-10: RAN4 LS reply
  We can start with other slides now …

## Slide 38
  3GPP NR-U
  Sharing issue

## Slide 39: A report from RAN1 meeting highlighted a RAN1 misunderstanding …
A report from recent RAN 1 meeting
  Almost all NR-U proponents prefer no-LBT or 25us LBT for transmission of high priority control messages
  In LAA, only DRS can be transmitted with 25us LBT which itself was based on the incorrect assumption that Wi-Fi too transmits high priority control messages with 25us LBT
  However, the airtime of control messages in NR-U will be much higher than that of LAA DRS since NR-U will be designed to work in standalone or dual connectivity mode
  If these messages are allowed to use no-LBT or only 25us LBT, they will be much more unfair to Wi-Fi than LAA DRS.

## Slide 40: … that is now being extended unfair access for all NR-U control frames
Commentary
  The issue of DRS access using short LBT has been raised before by IEEE 802 in a LS to RAN1
    We previously asked that it be limited to 1%
    The answer was non committal, but highlighted DRS can use Cat 4 LBT
  It now appears that the basis of using a short LBT for DRS was a misunderstanding of the way Beacons get access in 802.11
  This same misunderstanding is now being extrapolated to all control frames with a significant adverse affect on sharing
  Maybe it is time to ask ETSI BRAN to limit short or no LBT control frame accesses to < 1%
    It is currently set at (roughly) 5% in EN 309 893

## Slide 41: … that is now being extended unfair access for all NR-U control frames
Discussion
  Does anyone have a view on the topic raised
  See 11-18-1642-00 (slides 4-5) for more information

## Slide 42
  3GPP NR-U
  Response to LS to RAN4

## Slide 43: The SC sent an LS to 3GPP RAN4 out of San Diego
  During San Diego’s session, an apparent contradiction between RAN1/2 and RAN4 specs was highlighted, with a potential adverse affect on 802.11 operation
  A proposal to send a LS was approved
    The IEEE 802 Coex SC recommends to IEEE 802.11 WG that the contents of 18-11-1305r0 be sent to 3GPP RAN4 as a Liaison Statement
    Moved: Sindhu
    Seconded: Jim P
    22/0/8
  Ultimately the following was sent
    See embedded

## Slide 44: The SC may discuss any response to the LS to RAN4
  A reply was received
    See 11-18-1561-00
  Some discussion of this in 11-18-1642-00 (slides 8-10)

## Slide 45
  Agenda items
  Update on LS from RAN4

## Slide 46: RAN has withdrawn the LS sent to IEEE 802 by RAN4
  Previously IEEE 802.11 WG sent a LS (18-11-1305-00) to RAN4 related to an apparent contradiction between RAN1/2 and RAN4 specs, and a reply was subsequently received (11-18-1561-00)
  It now appears that RAN has withdrawn the reply based on objections by Nokia (supported by Huawei & T-Mobile)
    See LS from RAN (note: it has not yet been official received)
    The RAN Chair ruled, “RAN chairman: approving a REL-13 CR where company have different views of what the CR means is not a good idea, have further offline discussion”
  …

## Slide 47: RAN has withdrawn the LS sent to IEEE 802 by RAN4
  …
  The text of the RAN reply is
    3GPP TSG RAN understands that 3GPP RAN WG4 had sent RP-181526 (R4-1811880) to IEEE in response to IEEE’s LS in R4-1809644 titled “IEEE 802.11 Working Group Liaison Statement to 3GPP RAN4 on certain channel combinations for LAA in 5GHz”.
    Subsequent to RP-181526 (R4-1811880) there have been additional discussions in 3GPP TSG RAN.
    Consequently, 3GPP TSG RAN humbly requests IEEE to await an update following TSG-RAN#82 (10-13 Dec 2018).
  So we will probably have another reply to consider in Jan 2019

## Slide 48
  Agenda items
  A workshop?

## Slide 49: 802.11 WG will probably need to work with 3GPP RAN1 on “fair” access in 6GHz
  It was noted in Chicago that 3GPP is treating 802.11 as an incumbent in the 5GHz band, which they have agreed to protect with a “one way definition”
    ie, the addition of an LAA systems will not cause any more loss of performance on a Wi-Fi system that the addition of a Wi-Fi system will cause
    ie, there is no expectation that Wi-Fi (with possible exception of 802.11ax) will do the same to LAA
  It was also noted that 3GPP consider 6 GHz to be greenfield spectrum and so Wi-Fi should expect no “incumbency” based protection
  This highlighted the need for 3GPP RAN1 and IEEE 802.11 to engage with the goal of agreeing on how fair access between all technologies can be maintained in the 6GHz band … hopefully avoiding any public battles (like those that occurred with LTE-U)

## Slide 50: The SC discussed the possibility of a workshop to engage with 3GPP RAN1 on sharing of 5/6GHz
  In Chicago, it was suggested that IEEE 802.11 WG be proactive about engaging with 3GPP on “fair” sharing mechanisms for 6GHz
  It was further suggested that IEEE 802 could invite 3GPP RAN1 to participate in a workshop on this topic (as well as 5GHz)
    Possibly at the IEEE 802.11 interim in Sept 2018 or the plenary in Nov 2018 (with invitation in July 2018)
  There has been some positive feedback to the suggestion for a workshop but no one has really stepped up … until San Diego!
  In San Diego, Lili Hervieu (Cablelabs) proposed a Workshop with 3GPP RAN
    See 11-18-1139-01
  Ultimately a Workshop invitation was sent
    See embedded

## Slide 51: The Coex SC will discuss the draft response to the Workshop invitation
  The Workshop invitation was discussed this week at the RAN plenary on the Gold Coast (Australia)
  It is reported that
    With regard to the LS from IEEE on the organization of a potential workshop on NR-U coexistence with IEEE technologies there was an almost unanimous approach from the speakers on the floor that such a workshop may be useful. There was clear support for organizing such a workshop …
  A draft reply has been posted
    See embedded document
  The main open issue seems to be the location
    RAN want it located at a RAN meeting
    IEEE 802 proposed it be located at an IEEE 802 meeting

## Slide 52: There is at least some support for coexistence discussions between IEEE 802 & 3GPP
  The RAN plenary on the Gold Coast discussed a submission from AT&T (RP-181537) in relation to Wi-Fi/NR-U coexistence
  The relevant proposals include:
    Proposal 1: The pros and cons of adopting a preamble and ED/PD mechanism should be studied for 5 GHz bands
      IEEE 802 has previously suggested this
      They note in a proposal 2 that a preamble may have some advantages for intra unlicensed LTE sharing
      Note: the explanation of this proposal does incorrectly assert that sharing will always favour Wi-Fi because it uses ED = -62 dBm whereas unlicensed LTE uses ED = -72 dBm; this assertion ignores that Wi-Fi also uses a PD of -82 dBm and is based on faulty simulation assumptions; wouldn’t it be much easier if everyone used the same mechanism?
    …

## Slide 53: There is at least some support for coexistence discussions between IEEE 802 & 3GPP
    …
    Proposal 3: A new fairness criterion and sharing framework should be studied for new unlicensed bands 7 GHz and below
      In particular AT&T suggest the joint workshop may be an opportunity to foster common understanding on spectrum sharing even though regulations and availability of these bands is not clear as yet ; it has been noted that a new criterion carries risks too!
  There is some discussion of the proposals and related matters in 11-18-1642-00 (slide 7)

## Slide 54: Contributions and idea are sought for the potential Workshop
  We will probably officially hear from RAN after this meeting …
  … the SC Chair will notify the WG as soon as a reply is received
  Assuming it is still positive …
    there will be a Workshop in Jan 2019 (in St Louis, USA) or Mar 2019 (in Vancouver, Canada)
    Or somewhere else
  This means we may need to plan the Workshop in November 2019 (in Bangkok, Thailand)
    Ideas and contributions will be demanded … …
    … the SC Chair is not writing everything!
  How do we resolve the location issue?
  Are there any concerns about the Workshop?

## Slide 55
  Agenda items
  Review of recent ETSI BRAN meeting
  Blocking energy

## Slide 56: IEEE 802 has a long standing position relating to the use of blocking energy
  IEEE 802 has expressed concern to 3GPP RAN/RAN1 about the use of blocking energy by some implementations of LAA for a number of years
    Via various LS’s approved by both IEEE 802.19 and 802.11
  Blocking energy as used by some LAA implementations is the energy transmitted in the time between when the LBT mechanism gives it access and the time it is ready to use the medium
    Blocking energy is also known as reservation signals
  The primary purpose of blocking energy for LAA is to stop other systems gaining access to the medium in the meantime
  The concern expressed by IEEE 802 in various Liaison Statements regarding the use of blocking energy by LAA was that it was unnecessary use of the medium and, as such, it represented inappropriate harmful interference to other devices

## Slide 57: IEEE 802’s discussions with 3GPP related to blocking energy ultimately went nowhere
  The position expressed by IEEE 802 to 3GPP RAN/RAN1 was that the use of blocking energy should be limited to a level less than currently used by some LAA implementations
    Currently blocking energy is used up to 0.5ms or 1ms per COT (up to ~8ms)
  3GPP RAN/RAN1 agreed that the use of blocking energy is undesirable
    They noted it is unnecessary for good performance
    They noted it is so unnecessary that the LAA spec did even not define it
  3GPP RAN/RAN1 agreed at one point to limit the need for blocking energy by LAA by defining additional starting positions to the LAA spec
    This would reduce the length of any blocking energy
  IEEE 802 agreed at the time that this approach might be a reasonable compromise, subject to testing with real systems
  Unfortunately, 3GPP RAN1 later reneged on their commitment to define additional starting positions in LAA

## Slide 58: There was not consensus in Dec 2107 in ETSI BRAN on restricting the use of blocking energy
  There has been a series of discussions about blocking energy in ETSI BRAN over a number of years, without consensus
  In Dec 2017, Cisco made a compromise proposal that any use of blocking energy be limited to 100µs
    This would have the effect of limiting the use of blocking energy by LAA implementations to no longer than the time before the next symbol
    It recognised that some use of blocking energy is reasonable/acceptable
  There were many objections to this proposal from both the Wi-Fi & LTE communities
    Some objections were self interested because of a desire not to change LAA implementations in the pipeline
      Note: it believed this is why 3GPP couldn’t agree on adding new starting positions
    Some objected on the basis it was not fair to pick on blocking energy when there were many other examples of inefficient use of the medium
      eg padding, use of low data rate, etc
      Some in Wi-Fi community were concerned some 802.11ax features might be impacted

## Slide 59: There is not consensus in ETSI BRAN in Mar 2018 on a methodology being applied to blocking energy in LAA
  Before the March 2018 ETSI BRAN meeting, Cisco (Andrew Myles) facilitated an e-mail discussion on a new approach to dealing with blocking energy
  The discussion and conclusions are summarised in BRAN(18)097010, which was presented to ETSI BRAN in March 2018
    BRAN(18)097010 documented a methodology for dealing with “blindingly obvious” cases
    The BRAN(18)097010 methodology applied to blocking energy means it should be disallowed for LAA
    BRAN(18)097010 did not propose a mechanism for disallowing blocking energy for LAA
  Despite this work, there is still not consensus in ETSI BRAN on the question of blocking energy

## Slide 60: The new methodology in Mar 2018 applied to blocking energy means it should be disallowed for LAA
Summary of BRAN(18)097010 methodology applied to LAA
  3GPP RAN1 is an authoritative source on LAA matters
    Particularly on the use of blocking energy (also known as reservation signals)
  3GPP RAN1 has explicitly stated in LS’s to IEEE 802.11 WG that the use of blocking energy is unnecessary for good performance
  3GPP RAN1 has also stated blocking energy is not defined in the LAA specification
    Suggesting blocking energy is so unnecessary that it is not even defined
  There is thus a “blindingly obvious” case that blocking energy should not be allowed in the very specific case of LAA
    Note: this conclusion creates no precedent for any other situation because it depends on the existence of an authoritative source (3GPP RAN1 in this case) to judge the particular facts

## Slide 61: Ericsson used an access method taxonomy in Mar 2018 to justify the use of blocking energy
  There was a presentation from Ericsson in March 2018 that was related to blocking energy
  It provided a taxonomy of access methods in BRAN(18)0000001
    The main purpose was not to make a proposal for a change in the standard, but to bring discussion on mechanism to a technical matter (the purpose these mechanisms serve)
  BRAN(18)0000001 listed various mechanisms for devices to share the medium with other devices using the same & different technologies
    At both PHY and MAC levels
  It highlighted that many PHY based synchronisation methods need to use padding of various types, ie padding can be necessary
    Pre-pending, appending or inserted into a transmission
  The implication of the presentation was that blocking energy (as a PHY synchronisation mechanism) is also justified
File link

## Slide 62: There was no consensus in Mar 2018 on the conclusions that can be drawn from the access method taxonomy
  There was limited discussion of in BRAN(18)0000001 at the time of presentation in Mar 2018; it was discussed in more detail as part of the blocking energy discussion
  Cisco asserted BRAN(18)0000001 cannot be used to justify the use of blocking energy by some implementations of LAA; he noted that:
    BRAN(18)0000001 highlighted the inclusion of a mechanism in the taxonomy does not mean it is appropriate for use
      eg PCF is in the taxonomy and yet its use is not allowed under EN 301 893 rules because it does not enable sharing
    There is agreement that many PHY sync methods are indeed necessary, whereas even 3GPP RAN1 agrees the use of blocking energy with LAA is unnecessary

## Slide 63: The Coex SC will hear an update on discussions about blocking energy at ESTI BRAN in June 2018
  There was further discussion of the blocking energy issue at the ETSI BRAN meeting in June 2018
    See BRAN(18)098008
  BRAN(18)098008 from Cisco asked for agreement on the principle that:
    Transmissions that are agreed to be unnecessary or transmissions whose sole purpose is preventing other devices using the spectrum are not allowed
  While there was not consensus on the question of blocking energy, comments from a representative of the German regulator seemed to suggest (the suggestion was later withdrawn) that blocking energy is already not allowed by regulation in Germany
    He later provided a translation of rules for 2.4GHz and 5GHz
    Translation: “Emissions that intentionally disturb or prevent the intended use of WLANs, such as emissions of radio signals and/or data packets that have the intention to log off or influence the WLAN connections of other users against their will, are prohibited”

## Slide 64: The Coex SC will hear an update on likely blocking energy discussions at ESTI BRAN in Sept 2018
  Cisco has made another contribution to the upcoming ETSI BRAN meeting related to blocking energy
    See BRAN(18)099005r1
  The contribution makes the case that the use of blocking energy by LAA is a blindingly obvious violation of Article 3.2 of the RE-D
  It makes this claim based on 3GPP RAN1’s statement to IEEE 802 that:
    Reservation signals are not required for good LAA performance
    Not using reservation signals is a viable implementation option for LAA
  The implication of these statements from 3GPP RAN1 is that the use of reservation signals with LAA represent unnecessary interference
  BRAN(18)099005r1 proposes that ETSI BRAN notify 3GPP RAN1 that the use of reservation signals in Europe, as apparently used by some LAA implementations, is not allowed

## Slide 65: The blocking energy discussions in Sept 2018 will not rely on recent German regulator comments
  The original version of BRAN(18)099005r1 strengthened its case by citing the translation from the German regulator representative as meaning blocking energy was not allowed in Germany
  However, the representative subsequently stated (BRAN(18)099007) that the translation only applied to deauthers and not blocking energy
  He also stated that blocking energy is not contrary to Article 3.2, and should not be discussed further, because it:
    Does not represent harmful interference
    Does not have a sole purpose of excluding other users
  Of course, this view contradicts the 3GPP RAN1 statement that that the use of blocking energy is unnecessary, and the subsequent implication:
    That it does represents harmful interference
    With a sole purpose of excluding other users

## Slide 66: The WG may consider a LS to ESTI BRAN asking they consider discouraging or limiting blocking energy
  It is proposed that IEEE 802.11 WG consider a LS to ETSI BRAN asking they consider discouraging or limiting blocking energy
    The complete proposed LS is in 11-18-0706r2
  This would be consistent with IEEE 802’s position expressed in previous LS’s to 3GPP RAN/RAN1 related to blocking energy
  A possible motion (for Thu PM1) is:
    The IEEE 802.11 Coex SC recommends that the material in 11-18-0706r2 be sent to ETSI BRAN, expressing support for discouraging or limiting the use of blocking energy
    Moved:
    Seconded:

## Slide 67: The SC may consider motion to re-establish the WG position on blocking energy
  If the previous motion does not pass it is probably important to re-establish the IEEE 802.11 WG’s current position on blocking energy
  One possibility to re-establish its position is the following motion
    The IEEE 802.11 Coexistence SC recommends that it should be the position of the IEEE 802.11 WG that the use of up to 1 ms of blocking energy (aka reservation signals) before a data transmission, as used by some implementations of LAA, is acceptable, despite the liaised view of 3GPP RAN1 that such use of blocking energy is unnecessary for the good performance of LAA
    Moved:
    Seconded:

## Slide 68
  Agenda items
  Plans for next meeting

## Slide 69: The Coex SC will discuss plans for the next session in Bangkok, Thailand in November 2018
  Possible items include
    Discussion of results of ETSI BRAN meeting
    Review of 3GPP RAN1 activities
      Focus on NR-U
    Preparation for Workshop?
      If confirmed by 3GPP RAN1
    … <other suggestions?>
Bottom line: do not rely on a few people/companies to drive good coexistence between 802.11 and other technologies – they can’t do it by themselves

## Slide 70: The IEEE 802.11 Coexistence SC meeting in Hawaii in September 2018 is adjourned!