## Slide 1: Discussions on Multi-AP Coordination
Date: 2018-08-22
Authors:
Name | Affiliations | Address | Phone | Email
Jianhan Liu | Mediatek |  |  | jianhan.liu@mediatek.com
Yongho Seok |  |  |  | 
Gabor Bajko |  |  |  | 
Thomas Pare |  |  |  | 
James Yee |  |  |  | 
James Wang |  |  |  | 
Chao-Chun Wang |  |  |  | 

## Slide 2: Introduction
Multi-AP coordination has been proposed in EHT TIG in multiple contributions [1] [2] [3] [4].
Multi-AP coordination is a wide topic and can be achieved in different methods.
This contribution is target to
  Make sure that Multi-AP coordination in EHT has no contradiction and has least overlaps with the multi-AP task from WiFi alliance
  Clarify the terminology in Multi-AP Coordination
  Categorize the methods of Joint transmission of Multi-AP based on complexity and requirements.

## Slide 3: Multi-AP Coordination in EHT
Multi-AP effort in WiFi Alliance
  Network architecture, system level functionality
  MAC level coordination of APs’ operation, such as channels, BW, Security, etc.
  Each STA is associated with one AP.
  Transmission among APs is one-to-one transmission.
Multi-AP Coordination in EHT
  The goal is to achieve higher efficiency and higher throughput for Multi-AP systems.
  We want to enable joint transmission/reception by multiple APs within a single packet.

## Slide 4: Modes of Multi-AP Coordination
 | Mode (Terminology) | Description | Complexity | Benefit
1 | Coordinated OFDMA | Each groups of RUs is used by one AP only (On each RU, BF or MU-MIMO is allowed). Only CSI between the STA and the AP is needed. *Multiple APs to one STA on different RUs (not a useful mode.) | Low/Medium | Reduce overhead for short packets; Higher MCSs
2 | Coordinated Nulling | One AP applies pre-coding to suppress the interferences CSI of multiple STAs and the nulling AP is needed at the nulling AP. | Medium | Improved spatial reuse

## Slide 5: Modes of Multi-AP Coordination (cont’s)
 | Mode (Terminology) | Description | Complexity | Benefit
3 | Coordinated SU Beamforming | Multiple APs transmit to a STA on one RU. Joint Processing: the data for the STAs must be available at multiple APs. CSI of multiple STAs and multiple APs. | High | Better coverage Higher MCSs
4 | Constrained Coordinated MU-MIMO | Multiple Aps transmit/receive data from multiple STAs on one RU. Joint processing: the data for the STA must be available at multiple APs. CSI of multiple STAs and multiple APs. Reduced requirements on Frequency and Phase Synchronization accuracy (need to check its feasibility). | Similar to Mode 3. | Highest efficiency More spatial streams
5 | Coordinated MU-MIMO | Multiple Aps transmit/receive data from multiple STAs on one RU. Joint processing: the data for the STA must be available at multiple APs. CSI of multiple STAs and multiple APs. Frequency and Phase Synchronization accuracy. | Very High | Highest efficiency More spatial streams

## Slide 6: AP Coordination Modes in EHT
We need to decide what the AP coordination modes will be enabled in EHT.
  Do we need more detailed analysis on hardware requirements and performance benefits to make the decision?
  We also need to consider the time it takes to enable the different modes.

## Slide 7: References
Jianhan Liu, “Multi-AP Enhancement and Multi-Band Operations’, IEEE 802.11-18/1155.
Hongyuan Zhang, “EHT technology candidate discussions”, IEEE 802.11-18/1161.
Ron Porat, “Multi-AP and HARQ for EHT”, IEEE 802.11-18/1116.
David Yang, “Discussion on EHT Study Group Formation”, IEEE 802.11-18/1180.