## Slide 1: View on EHT Candidate Features
Date: 2018-09-10
Authors:
Name | Company | Address | Phone | Email
Yusuke Tanaka | Sony Corporation |  |  | Yusuke.YT.Tanaka@sony.com
Kosuke Aio |  |  |  | Kosuke.Aio@sony.com
Sho Furuichi |  |  |  | Sho.Furuichi@sony.com
Naotaka Sato |  |  |  | naotaka.sato@ieee.org
William Carney | Sony Electronics |  |  | William.Carney@sony.com

## Slide 2: Background
This is the first meeting following the approval of EHT SG establishment during the July meeting [1].
According to [1], the scope of EHT SG is to develop a Project Authorization Request (PAR) and a Criteria for Standards Development (CSD) for a new 802.11 amendment for operating in the bands between 1 to 7.125 GHz, with the primary objectives;
  To increase peak throughput and improve efficiency
  To support high throughput and low latency applications such as video-over-WLAN, gaming, AR and VR

## Slide 3: Introduction
Since kicking-off EHT discussion, several candidate features have been proposed.
  6 GHz support, 320 MHz, 16 Spatial Streams, Multi Band Operation, Multi-AP Coordination, etc. (See details in [2-14])
  Current status is that the only thing captured is “6 GHz band” as a part of the scope of PAR/CSD that is to be developed in EHT SG.
This submission shows our views on the following features and proposes some way forwards to develop PAR/CSD towards new 802.11 amendment.
  Multi-AP Coordination
  6 GHz band support

## Slide 4: Views on Multi-AP Coordination

## Slide 5: Views on Multi-AP Coordination
Coordination among Multiple APs (i.e. Multi-AP Coordination) can contribute to achieve primary objectives of new 802.11 amendment.
  Potential to mitigate mutual interference among multiple APs
  Potential to avoid low spectrum utilization efficiency due to autonomous behavior of conventional WLANs.
Some technologies can be candidate means to mitigate the mutual interference among multiple APs, and to improve spectrum utilization efficiency in Multi-AP Coordination context.
  Coordinated Beamforming, Distributed MU-MIMO, Null-steering etc.
  Resource (time/frequency) sharing, enhancement of Spatial Reuse etc.

## Slide 6: Views on Multi-AP Coordination (Cont’d)
It is important to consider decision making topologies applicable to Multi-AP Coordination.
  Distributed decision making
    Each AP makes its decision in coordination with other APs.
  Centralized decision making
    One AP relegates its decisions to another AP; or
    All APs relegates their decisions to central entity
Which decision making topologies is applied depends on use cases.
  Example use case of distributed decision making
    Coordination between APs belonging to different networks (i.e. no common central entity exists).
  Example use case of centralized decision making
    Administration and management of enterprise network.

## Slide 7: Proposed Way Forwards concerning Multi-AP Coordination
Multi-AP Coordination should be captured in the PAR/CSD for new 802.11 amendment as one of potential means to achieve the primary objectives.
Multi-AP Coordination should consider all the applicable decision making topologies in order to realize various use cases.

## Slide 8: Views on 6 GHz Band Support

## Slide 9: Views on 6 GHz Band Support
New 802.11 amendment should support 6 GHz band.
  It is obvious that available channels for WLAN can be increased by supporting new frequency band.
  Availability of lots of channels enables us to achieve wider channel bonding, more effective Multi Band Operation, and congestion reduction.
  Therefore, it is beneficial for new 802.11 amendment to support 6 GHz band.
One the other hand, new 802.11 amendment should not ignore possible regulatory constraints to use this band.
  There are some incumbent systems in this band [2].
    Fixed Systems (FS), Fixed Satellite Systems (FSS) (earth-to-space), etc...
  Incumbent protection mechanism is still under discussion at the regulatory authorities such as FCC and CEPT.
  Some constraints might be imposed on a New 802.11 amendment supporting 6 GHz as a result of the sharing and compatibility study.

## Slide 10: Views on 6 GHz Band Support (Cont’d)
Database-aided RLAN coordination is emerging as a leading candidate approach for incumbent protection for this new 802.11 amendment.
  Fixed Wireless Communications Coalition (FWCC), an incumbent stakeholder group using FS, urged the FCC to use databases that correctly reflect all of the FS receivers in operation or successfully coordinated [15].
  Some companies jointly proposed FCC to adopt Automated Frequency Coordination (AFC), which is similar to White Space Database (WSDB) used in TV band White Space [16].
In new 802.11 amendment development, IEEE 802.11af (i.e. WLAN for TVWS) could be a good basis to support 6 GHz band under (possible) regulatory constraints.
  11af = 11ac PHY/MAC + Operation under geolocation database (GDB), and is already a part of IEEE 802.11-2016.
  We can extend the functions of “Operation under GDB” with a consideration of (possible) 6 GHz regulatory constraints while developing PHY/MAC for EHT.
  Even if any regulatory authority does not adopt database-aided RLAN coordination for 6 GHz use, we can continue to develop PHY/MAC for new 802.11 amendment with closing the functional extension of “Operation under GDB”.
  Less spec impacts and shorter development time than when creating from the scratch.

## Slide 11: Proposed Way Forward concerning 6 GHz
6 GHz band support should be captured in the PAR/CSD for a new 802.11 amendment, continuously.
IEEE 802.11af should be considered as a basis to support 6 GHz band under (possible) regulatory constraints for new 802.11 amendment development.

## Slide 12: Summary
This submission showed our views on 6 GHz band support and Multi-AP Coordination.
This submission proposed way forwards to develop PAR/CSD concerning 6 GHz band support and Multi-AP Coordination.

## Slide 13: Reference
    [1] 11-18-1059-06-0000-july-2018-wg-motions
    [2] 11-18-0789-06-0wng-extreme-throughput-802-11
    [3] 11-18-0818-03-0wng-16-spatial-stream-support-in-next-generation-wlan
    [4] 11-18-0846-00-0wng-next-generation-phy-mac-in-sub-7ghz
    [5] 11-18-0857-00-0wng-beyond-802-11ax-throughput-enhancement-utilizing-multi-bands-across-2-4-5-6ghz-bands
    [6] 11-18-0903-01-0wng-next-generation-home-use-case
    [7] 11-18-1116-00-0eht-multi-ap-harq-for-eht
    [8] 11-18-1155-01-0eht-multi-ap-enhancement-and-multi-band-operations
    [9] 11-18-1161-00-0eht-eht-technology-candidate-discussions
    [10] 11-18-1171-00-0eht-view-on-eht-objectives-and-technologies
    [11] 11-18-1180-00-0eht-discussion-on-eht-study-group-formation
    [12] 11-18-1184-01-0eht-eht-discussions-on-throughput-enhancement
    [13] 11-18-1190-01-0eht-discussion-on-eht-timeline-and-scope
    [14] 11-18-1191-00-0eht-mu-sounding-improvements
    [15] FWCC, “Re: GN Docket No. 17-183, Expanding Flexible Use in Mid-Band Spectrum Between 3.7 and 24 GHz Ex Parte Communication”, August 28, 2018
    [16] Apple Inc., et al, “Re: Expanding Flexible Use in Mid-Band Spectrum between 3.7 and 24 GHz, GN Docket No. 17-183”, August 23, 2018