## Slide 1: Multi-WID Addressed WUR Frame
Date: 2018-09-02
Authors:
Name | Affiliation | Address | Email
Li Nan | ZTE Corporation | No.9 Wu Xing Section Xi Feng Road Xi’an, Shaanxi Province P.R.China | li.nan25@zte.com.cn
Lv Kaiying |  |  | lv.kaiying@zte.com.cn
Sun Bo |  |  | sun.bo1@zte.com.cn
Wei Ning |  |  | wei.ning@zte.com.cn

## Slide 2: Abstract
As defined in Draft D0.4, the Address field of the WUR Wake-up frame is set to
  The WUR ID when the frame is individually addressed
  The group ID when the frame is group addressed
  The transmit ID when the frame is broadcast addressed
  0 when multiple WIDs are included in the Frame Body field of the frame.
A WUR frame with group ID in the Address field is a group addressed WUR frame that is addressed to all the WUR STAs identified by that group ID.
A WUR frame with 0 in the Address field is a WUR Wake-up frame that has a list of identifiers in the Frame Body field where one of the identifiers identifies the non-AP STA. However all WUR STAs need to decode the multi-WID address WUR frame.
A method about multiple WID addressed WUR frame with more power saving consideration is proposed in this proposal.

## Slide 3: Proposal
AP uses block granularity parameters to divide WUR STA addressing space into blocks. Block granularity parameter means how many WUR STAs with contiguous WIDs in WUR addressing space are contained in one block.
  AP signals block granularity parameters to WUR STAs in WUR Operation element.
  AP implicitly signals block IDs by mapping the WUR ID space with granularity parameters
The WUR STAs are grouped based on the block granularity parameters, and each block is identified the block ID.
  Eg. block granularity parameter may be set to 2 octets, 4 octets, 8 octets and 16 octets, respectively.
  A specific WUR STA can belong to multiple blocks with different block granularity.

## Slide 4: Block ID Allocation Scheme
As an example shown above, one WUR STA can belong to multiple blocks based on the block granularity.
  WUR STAs of range 1 to 16 belong to block ID #1 and STAs of range of 17 to 32 belongs to block ID #2 respectively when block granularity is x
  WUR STAs of range of 1 to 32 belong to block ID #m+1 when block granularity is 2x
When ONLY STAs within range 1 to 16 are to be waken up, the AP can send a multi-WID addressed wake-up frame with block ID #1 for example.
When STAs within range of 1 to 32 are to be waken up, the AP can send a multi-WID addressed wake-up frame with block ID #m+1 for example.
IDs for WUR STA(WID)
block granularity x
block granularity 2x
#1
Block ID numbering
#2
…
…
#3
#4
# m
# m+1
# n
STA 1 to 16
STA 17 to 32
STA 1 to 32

## Slide 5: Multi-WID addressed WUR frame format
A Multi-WID addressed WUR frame is a WUR frame with the proposed definition of the subfields as below.
  Frame Control field:
    the Length Present field is set to 0 to indicate the Length/Misc field contains the Length field
    the Length field contains the length of the Frame Body field as defined in 9.10.2.4
  Address filed: The address field is set to block ID
  Frame Body field: contains the list of WIDs

## Slide 6: Conclusion
We discussed flexible Block ID allocation scheme in this proposal.
  AP notifies block granularity parameters to WUR STAs.
  By knowing block granularity, a WUR STA could determine which block(s) it belongs, and its position in the block(s).
  AP signals a multi-WID WUR frame using the address and length field.
By using this scheme,
  AP does not need to explicitly signal the specific block IDs which the WUR STA belongs to.
  Only WUR STAs belonging to a block indicated in the address field of the WUR frame will decode the frame body of a multi-WID addressed wake-up frame so that more power saving can be achieved

## Slide 7: Straw Poll 1
Do you agree the Block ID Allocation Scheme in slide 3?

## Slide 8: Straw Poll
Do you agree the multi-WID addressed WUR frame format in slide 5?

## Slide 9: References
[1]Draft P802.11ba D0.4