## Slide 1: Time-Aware Traffic Shaping over 802.11
Date: 2018-09-10
Authors:

## Slide 2: Abstract
In a previous presentation (doc#: 802.11-18/1160r0) we showed that 802.11 latency can be very low, but predictability (reliability) can be improved
  - This would enable 802.11 to address many time sensitive applications (gaming, robotics, industrial automation, etc.)
Many issues raised with current products can be resolved with optimized implementations, or by implementing features already defined in 802.11.
802.11 could go further on congestion control solutions to address worst cast latency predictability to ensure 802.11 competitiveness
  Extend 802.1 TSN features: Time-Aware shaping (802.1Qbv) over 802.11
In this presentation we discuss the Time-Aware shaping (802.1Qbv) concept and how it can be used to control congestion in 802.11
We also provide preliminary performance results in a single BSS case

## Slide 3: Outline
Time sensitive application examples
Latency challenges
802.1 TSN overview
Time-Aware (802.1Qbv) traffic shaping
Time-Aware traffic shaping over 802.11
Performance evaluation
Conclusions

## Slide 4: Time Sensitive Applications Examples
Real-time mobile gaming
Wireless control system
Limiting worst case latency (also over the Wi-Fi link) is the main issue
Latency/jitter cause lagging/bad user experience
Latency/jitter may cause instability of the system

## Slide 5: Requirements for the Wi-Fi Network
Application | Worst Case Latency | Application PER | Throughput Requirement
*Mobile gaming | 10 ms | 0.1% | Low (0.5-1Mbps)
**Wireless control, robotics, AGVs | Class A: 10-50ms Class B: 1-10ms Class C: <1ms | 0.1 – 0.0001% (depend on specific application) | Low
Wireless VR | 5 ms | 0.1% | High
*Doc#: 802.11-18/1419r4
**Doc#: 802.11-18/1160r0
Predictable worst case latency with high probability is major improvement area for Wi-Fi.

## Slide 6: Latency Challenges
802.11 latency can be very low without congestion
  Basic sequence: EDCA+DATA+ACK (~100’s µs for 100 bytes)
  This enables a wider range of very low latency use cases (mobile gaming, industrial Class A/B under managed networks)
Congestion is the main challenge in enabling more predictability of worst case latency
  Congestion within BSS is easier to address with congestion control solutions
  Congestion with managed OBSSs can also be addressed
  Congestion with unmanaged OBSSs is very hard to control
Time-aware traffic shaping can enable better congestion control
  802.1Qbv defines a solution for Ethernet-based TSN (Time-Sensitive Networking)
  As with other 802.1 capabilities, similar concept can be extended to 802.11
  This also enables better integration of 802.11 with Ethernet-based TSN

## Slide 7: IEEE 802.1 Time-Sensitive Networking (TSN)
TSN Components Common Standards
Latency
Reliability
Standard Ethernet with Synchronization, small and/or fixed latency, and extremely low packet loss
Reliability
Ultra reliability: Frame Replication and Elimination (P802.1CB) Path Control and Reservation (802.1Qca) Per-Stream Filtering and Policing (802.1Qci) Reliability for time sync (P802.1AS-Rev)
Synchronization
Time synchronization: Time Synchronization (802.1AS)
Resource Mgmt
Dedicated resources & API Stream Reservation Protocol (802.1Qat) TSN configuration (P802.1Qcc) YANG (P802.1Qcp) Link-local Registration Protocol (P802.1CS)
Bounded low latency: Time-Aware traffic shaping (802.1Qbv) Preemption (802.1Qbu/802.3br) Cyclic Scheduling (802.1Qch) Asynchronous Scheduling (802.1Qcr)
Zero congestion loss
Credit: János Farkas, Ericsson
TSNA Conference 2017, http://www.tsnaconference.com/
√ 802.1AS over 802.11
Timing Measurement (TM)
Fine Timing Measurements (FTM)
√ 802.11aa (SRP over 802.11 for AV)
√ 802.11ak (802.11 links in an 802.1Q network)
Time-Aware shaping (802.1qbv) over 802.11 (extension to address latency)

## Slide 8: Time-Aware Traffic Shaping
Scheduling time-critical frame transmissions while avoiding contention with lower priority frames can give low jitter and guarantee worst case latency
  802.1Qbv defines Time-Aware shaper for Ethernet switches
frame selection
T
T
T
T
T
T
T
T
Multiple queues are controlled based on a repeating schedule (time, gate open/closed), time reference is provided by 802.1AS
Queues/Traffic classes
Qbv can be very effective, especially for predictable, periodic traffic
gate open
gate closed
gate open
gate closed
gate open
Transmission time

## Slide 9: Time-Aware Shaping over Wireless
Time-Aware shaping sitting on top of 802.11 MAC can resolve contention within each device and across multiple STAs/AP that share the medium
  Within the BSS, existing 802.11 MAC/PHY protocols can be used to ensure that the STAs will have time to complete their transmission during the period when the gate is open: EDCA, UL OFDMA, TWT, …
STA 1
T
T
T
T
T
T
T
T
T
T
T
T
Shared medium
AP
STA 2
Other Traffic
Time-Sensitive Traffic
AP
STA 1
STA 2
…
gates closed
gates closed
gate open
gate open
gate open
gate open
All gates open
(Normal Operation)
gates closed
Example Scenario
The Qbv schedule defines when the gates open/close (implementation specific)
The schedule can take into account the 802.11 MAC/PHY mode (e.g. EDCA, 11ax DL/UL OFDMA, TWT, …)

## Slide 10: Simplified TSN Reference Stack
IEEE 802.1 Network
TSN Capabilities: time sync, time-aware, reservations, and many others …
Application
Transport
IP
IEEE 802.3
(Ethernet)
IEEE 802.11
(Wi-Fi)
3GPP/5G
(new)
MAC/PHY
Direct L2 access
IP Encapsulation
Link Layer
Media Specific Support required for TSN Capabilities
  Exchange the 802.1Qbv schedule between managed STAs
  Rules to certify the release of frames from the 802.11 queues according to the 802.1Qbv defined times
802.11 requirements for Time-Aware (Qbv) capability:

## Slide 11: Performance Evaluation
Single BSS gaming scenario
  Single AP, 80 MHz channel BW, 2 NSS
  16 Gaming STAs: Time-Sensitive traffic
    Bi-directional periodic streams: 500B UDP packets (worst case packet size according to 802.11-18/1419r4) every 30ms;
    DL and UL streams are independent
  20 Video STAs: BE traffic
    DL traffic: ~6MB DL packets generated periodically every 4s (models 1080P DASH video streaming application)
Goal: evaluate the latency performance of with and without Qbv over different access mechanisms

## Slide 12: Simulation configurations
With Qbv:
AP and STAs know the Qbv schedule
Gaming traffic is prioritized
Other traffic is blocked before and within the period
Access within the period:
  DL: MU OFDMA
  UL: EDCA, Trigger-Based, or TB (no gaming) + EDCA (gaming)
Without Qbv: no prioritization and no reserved period (gaming uses VO, and Video uses VI)
Trigger-based access:
EDCA access:

## Slide 13: Results
Worst case latency is under 10ms with high reliability with Qbv in this scenario

## Slide 14: Conclusions
Worst case latency is an important requirement for many time-sensitive applications (gaming, automation, robotics, …)
The Time-Aware traffic shaping concept (802.1Qbv) has been used to control congestion and worst case latency in 802.1 TSN over Ethernet
Extending Qbv over 802.11 can help control congestion in managed networks and improve latency for time-sensitive traffic
  Few MAC changes are required to enable the exchange of the Qbv schedule within a BSS and rules to ensure interfering traffic can be blocked during certain periods

## Slide 15: References
Doc#: 802.11-18/1419r4
Doc#: 802.11-18/1160r0

## Slide 16: Simple Experiment: Admission control and Time-Aware Scheduling over the 802.11 MAC
STA
AP
d
DL
UL
DL
…
Slot Duration = 10 ms
Packet arrivals according to a schedule
Application packet size = 100 Bytes
Busy/Office hours
Overnight hours
PER= Packet is considered lost if not delivered within the slot duration (10 ms)
802.11ac 2.4 GHz, d=10 m range (NLOS)
Application layer latency and PER (office environment)
STA and AP are time synchronized through 802.1AS over 802.11
Time-Aware Schedule: STA and AP hold the packet into the application queue until the scheduled release time (same concept as in 802.1Qbv)
Dave Cavalcanti, Intel

## Slide 17: DL latency results