## Slide 1: RTA Optimization proposal Sep Kona Meeting
Date: 2018-09-12
Author:

## Slide 2
This presentation contains technical discussion of RTA TIG.
Abstract

## Slide 3: Outline
Problem flashback
Problem analysis
Optimization direction and desirable features

## Slide 4: Problem flashback
◆ High latency
  ➣ High latency will cause packets delay
  ➣ It can be causes of signal quality, interference, loading or geolocation (not in scope)
◆ Jitter/Spike/Worst case latency
  ➣ The average latency is acceptable
  ➣ The jitter is the problem to solve
  ➣ The jitter between STA and AP have considerable correlation with lagging

## Slide 5: Problem flashback
◆ Traffic characteristics
  ➣ average 30ms / packet
  ➣ size 30-500Bytes
◆ Traffic model
  ➣ Frame sync
  ➣ Status sync
Please refer to IEEE 802.11-18/1419r5 for more details
An effective mechanism to identify real-time gaming traffic by the packet characteristics of different gaming stages is under research

## Slide 6: Latency breakdown from client to game server
Client
AP
Game server
latency<100ms to ensure good game experience
100-200ms for acceptable game experience
Worst case latency can go up to 100+ ms
latency varies from 30ms to 200ms per geolocation
Latency/ms | Game experience
<100 | No lagging
100-200 | Lagging expected
>200 | Bad experience
460 | Disconnection
Relatively stable
Random spike
latency spike cause the supposed satisfied game experience not acceptable 

## Slide 7: Quadrant of jitter and latency between STA and AP
Quadrant A: Network status between STA and AP is good. This is best scenario.
Quadrant B: Network status between STA and AP might impact the game experience.
Quadrant C: Network status between STA and AP impact game experience.
Quadrant D: Network status between STA and AP impact game experience negatively.
Latency is from STA to AP RTT. Jitter is standard deviation of latency.
Game experience of point X and Y shall be enhanced by the trade-off of latency and stability

## Slide 8: Network Requirements between STA and AP
Specification | Value
Average latency | <10ms
Packet loss | <0.1%
Jitter | <5ms
High latency packet(>30ms) | <1%
The average latency between STA to AP is 7ms.
To control worst case spike, the average latency can go up to 25ms for stability.
When latency between STA and AP reach 30ms, it will start to impact gaming experience severely.

## Slide 9: To wrap things up
Real-time mobile gaming usually low throughput, small packets (30-500Bytes)
Sometimes the experience of RTA is non reversible
Satisfying user experience requests consistent stable latency, preferable low
The latency request is not a problem in theory, but in practice
The tradeoff between latency/throughput to stability should be considered

## Slide 10: Optimization direction
Concurrent dual link transmission
  Most AP and STA support dual band
  2.4GHz is congested, but it is used by most wi-fi users
  5GHz is fast but have coverage issue
  Random spike appear at both 2.4GHz and 5GHz, but less likely concurrently
  Dual link transmissions are recommended for stability

## Slide 11: Traffic flow
2.4GHz
5GHz
MAC
Management entity
2.4GHz
5GHz
MAC
Management entity
Dual band connections are simultaneously at both ends
The duplication is done before frame transmission
A sequence number is generated for duplication detection at peer end
Frame at each band shall be sent out whenever the channel is clear
Management entity will decide when and how duplication/de-duplication is done
Duplication
Sequence generation
Sequence check
Duplication
Removal
Sequence check
Duplication
Removal
Duplication
Sequence generation
2.4GHz
5GHz
2.4GHz
5GHz
STA
AP

## Slide 12: Dual link use case in RTA
John is playing real-time mobile game with his phone connected to dual-band router in his home.
While John is within the range of both 2.4GHz ,5GHz range of his router and he is very sensitive to game experience, he does not want any lagging during game. So he enabled dual link function on his phone before he starts the game.
Based on signaling from the AP and phone, each packet, both UL and DL during the game is replicated. The process manner at each end is based on first come, first serve. Only the 1st packet is accepted, while the 2nd is dropped directly at Phone and AP.
Duplicated data transmission
1st transfer, 2nd drop
2.4GHz
5GHz
Dual link enabled
Dual link enabled
Simultaneous dual band
Simultaneous dual band

## Slide 13: Current solutions…
SU-MIMO
  multiple streams of data to be simultaneously transmitted or received between two Wi-Fi devices using multiple antennas and beamforming technology
Fast BSS Transfer
  2nd AP association can be done before 1st AP disassociation
FST
  Different streams can be sent over different bands to/from same STA, transparently or non-transparently to higher layers
To send same stream over different band between AP and STA
- A mechanism to identify the specific traffic which requests this feature
A mechanism for STA to associate two bands concurrently
A mechanism to replicate and de-duplicate frames from different bands is requested
Hardware and OS compatibility are needed. Ex. More antennas