## Slide 1: TX Requirement – Spectral flatness
Date: 2018-08-16
Authors:

## Slide 2: Spectral flatness/bandwidth - Background
The spectral flatness in 802.11-16 is a test of the transmitter HW. The test is done using a BPSK signal
In 11ba, because the signal waveform is not defined in the spec., the test is rather concerned with the signal properties in the frequency domain

## Slide 3: Thoughts
A lot of work has been done related making the TX spectrum flat in order to allow for as high total TX power as possible if PSD limited [1]-[4]
The problem of being allowed to send with high TX power when PSD limited is very similar to requiring a flat spectrum
=> A certain flatness can be ensured by requiring a that a minimum TX power can be used

## Slide 4: Thoughts, cont’d
In [1] it is shown that for the three provided examples for LDR and HDR, the allowed TX powers under a 10 dBm/MHz requirement are
  LDR: 15.6,14.5, and 15.7 dBm, respectively
  HDR:15.5, 14.4, and 15.5 dBm, respectively
The idea is therefore to test the flatness by requiring that a minimum TX power can be used under the constraint of 10 dBm/MHz
The idea is also to do this in a way similar to how the 10 dBm/MHz is tested

## Slide 5: Suggestion for test
Perform the test using the same methodology as is used in [5] 5.4.3.2 & 4.3.2.3 to test maximum PSD by searching over 1 MHz segments, the core steps illustrated below
Step 5:
Starting from the first sample PSamplecorr(n) (lowest frequency), add up the power (in mW) of the following samples
representing a 1 MHz segment and record the results for power and position (i.e. sample #1 to sample #100). This is the
Power Spectral Density (e.i.r.p.) for the first 1 MHz segment which shall be recorded.
Step 6:
Shift the start point of the samples added up in step 5 by one sample and repeat the procedure in step 5 (i.e. sample #2 to
sample #101).
Step 7:
Repeat step 6 until the end of the data set and record the Power Spectral Density values for each of the 1 MHz
segments.
From all the recorded results, the highest value is the maximum Power Spectral Density (PSD) for the UUT. This value,
which shall comply with the limit given in clause 4.3.2.3.3, shall be recorded in the test report.

## Slide 6: Suggestion for test, cont’d
Identify the sample correpsonding to the lowest frequency and the highest frequency. These will be denoted sample #1 and #401, respectively. The lowest and highest frequency are found by defining #201 to coinside with the center frequency of the channel.
Starting from the first sample (lowest frequency), add up the power (in mW) of the following samples representing the 4.010 MHz segment and record the result for power (i.e. sample #1 to sample #401). This is the total power for the 4 MHz channel.
Find the maximum PSD as described in 300.328, Section 5.4.3.2.1.
Calculate the difference in dBm between the total power found in 2 and the maximum PSD in 3. The difference shall be at least 3 dBm.

## Slide 7: Straw Poll 1
Do you believe Spectral flatness should be a requirement for 11ba?
Y/N/A

## Slide 8: Straw Poll 2
Do you believe the Spectral flatness requirement for 11ba should be specified along the lines described in this contribution and that we should prepeare this text for D1.0?
Y/N/A

## Slide 9: References
[1] Tuning Symbol Randomization, IEEE 802.11-18/1529r0, M. López et al.
[2] Spectral line suppression for MC-OOK, IEEE 802.11-18/1179r1, M. López et al.
[3] WUR Power Spectral Density, IEEE 802.11-18/0824r1, S. Shellhammer et al.
[4] WUR PSD Studies, IEEE 802.11-18/1165r1, V. Kristem et al.
[5] ETSI 300.328, V 2.1.1,