## Slide 1: Discussion on the Co-Existence of 802.11bb with the Family of 802.11 Standards
Date: 2018-09-10
Authors:

## Slide 2: Abstract
Most of the usage models of [1,2] face outage problems when a physical optical signal blockage occurs or the geometric setup of the transceiver is unfavourable.
This contribution discusses ways to address this problem by using the Fast Session Transfer (FST) mechanism of IEEE STD 802.11-2016 [3] and rely on the already available IEEE 802.11 family of standards for RF communication.
The co-existence and co-operation of IEEE 802.11bb with the rest of the family of standards of IEEE 802.11 has the potential to accelerate the penetration of LC in the general market of IEEE 802.11.

## Slide 3: Outline
Recap of the usage models of IEEE 802.11bb
Possible difficulties encountered by LC systems
Possible countermeasures and solutions
Advantages of the co-existence and cooperation of 802.11bb with the rest of the 802.11 standards
Multi-band Operation and the Fast Session Transfer Mechanism (FST) as a way forward
Conclusion

## Slide 4: Recap of the Usage Models of IEEE 802.11bb
In IEEE 802.11bb, the following usage models are considered [1]:
  Industrial wireless (10 Mbps-1 Gbps; latency <1 ms; 99.9 % reliability)
  Wireless access in medical environments (10 Mbps-3 Gbps, latency<1 ms)
  Enterprise networks wireless (10 Mbps-1 Gbps; latency <ms)
  Home networks wireless (10 Mbps-5Gbps; latency<1 ms)
Also, the following secondary usage models are considered [2]:
  Backhaul
  V2V, V2I, and I2V communication
  Underwater communication
  Gas Pipeline communication

## Slide 5: Possible Difficulties Encountered by LC Systems
In LC and especially in the visible light spectrum:
  The optical wireless spectrum is highly dependent on the geometric setup of the (MIMO) transceiver [4,5,6]. This means that an inconvenient geometric setup results in the rapid decrease of the receive optical SINR
  Physical signal blockage causes connectivity problems
In particular, almost all considered usage models of IEEE 802.11bb are susceptible to the previous events

## Slide 6: An Optical Solutions (1)
A solely optical solution requires the careful deployment of multiple optical transmitters, in different spatial positions and with different orientations, and multiple photo-detectors in the receiver with different orientations. Ideally, the multiple photo-detectors have also different spatial positions.
  Problems:
    The densification of the optical transmitter might cause undesired optical interference.
    Additional backhauling is required.
    On-the-fly system adaption is difficult.

## Slide 7: An Alternative Solutions (2)
An alternative solution can be based on the co-existence and cooperation of LC and RF communication systems.
  Operating principle:
    In the event of blockage or low values of receive SINR, LC is terminated and data transmission is direct to the existing RF wireless network. Once LC is possible, data transmission is redirected to the existing LC wireless network.
  Main advantage:
    As 802.11bb is part of the 802.11, its co-existence with the rest of the 802.11 standards can be done efficiently using already existing mechanisms and with almost negligible standard modification.

## Slide 8: Advantages of the co-existence and cooperation of 802.11bb with the rest of the 802.11 standards
  On-the-fly increased connectivity and communication robustness for: i) industrial wireless; ii) enterprise and home networks; and iii) V2V, V2I, and I2V communication.
  Indirect support of high mobility in: i) industrial wireless; enterprise and home networks; and ii) V2V, V2I, and I2V communication.
  Coverage extension in: i) industrial wireless; ii) enterprise and home networks; and iii) V2V, V2I, and I2V communication.
  Cross-room connectivity in i) industrial wireless; and ii) enterprise and home networks.
  Enable the formation of on-the-fly unstructured LC networks in: i) industrial wireless; ii) enterprise and home networks; and iii) V2V, V2I, and I2V communication.

## Slide 9: Multi-band Operation and the Fast Session Transfer Mechanism (FST) as Way Forward
  Based on IEEE STD 802.11-2016 [3], a multiband capable device is able to:
    manage operations in more than one band/channel in a simultaneous manner or not.
    support multiple MAC sublayers.
  In IEEE 802.11, the FST mechanism presented in IEEE STD 802.11-2016 [3], is the mechanism which enables multiband operations.
  A FST mechanism from IEEE STD 802.11-2016 [3] could be also be used by IEEE 802.11bb for enabling its co-existence and smooth cooperation with rest of the RF IEEE 802.11 standards.
  Result: faster and smoother penetration of LC in the wide market of IEEE 802.11

## Slide 10: Conclusions
  Most of the considered usage models of [1,2] are susceptible to optical signal blockages and poor performance in unfavourable geometric setups of the involved transceivers.
  An optical solution might increase the system interference, requires additional backhauling, and is not adaptable.
  An alternative solution can be approached by enabling the co-existence and co-operation of IEEE 802.11bb with the rest of the IEEE 802.11 standards.
  This can be achieved using the FST mechanism of IEEE STD 802.11-2016 [3] with marginal standards modification.
  The discussed solution could accelerate the spread of IEEE 802.11bb in the general ecosystem of IEEE 802.11

## Slide 11: Straw Polls
Do you believe that the effective co-existence and co-operation of IEEE 802.11bb with the rest of the IEEE 802.11 family of standard is beneficial for IEEE 802.11bb?
Y/N/A:
Do you believe that IEEE 802.11bb needs to consider a mechanism for enabling the effective co-existence and co-operation of IEEE 802.11bb with the rest of the IEEE 802.11 family of standard?
Y/N/A:

## Slide 12: References
[1] 11-18/1109r5, “LC Usage Model Document”, Oliver Pengfei Luo, et al.
[2] 802.11-18/1109r2, “LC Usage Model Document”, Oliver Pengfei Luo, et al.
[3] IEEE Standard for Information technology--Telecommunications and information exchange between systems Local and metropolitan area networks--Specific requirements - Part 11: Wireless LAN Medium Access Control (MAC) and Physical Layer (PHY) Specifications," in IEEE Std 802.11-2016 (Revision of IEEE Std 802.11-2012) , vol., no., pp.1-3534, 14 Dec. 2016
[4] J. M. Kahn and J. R. Barry, "Wireless infrared communications," in Proceedings of the IEEE, vol. 85, no. 2, pp. 265-298, Feb. 1997.
[5] A. Stavridis and H. Haas, "Performance evaluation of space modulation techniques in VLC systems," 2015 IEEE International Conference on Communication Workshop (ICCW), London, 2015, pp. 1356-1361.
[6] M. Uysal, F. Miramirkhani, O. Narmanlioglu, T. Baykas and E. Panayirci, "IEEE 802.15.7r1 Reference Channel Models for Visible Light Communications," in IEEE Communications Magazine, vol. 55, no. 1, pp. 212-217, January 2017.