## Slide 1: Recommended Direction for EHT
Date: 2018-09-09
Authors:

## Slide 2: 802.11 (+WFA) has a remarkable history of standardizing valuable technologies …
Mandatory Headline Feature
Optional Headline Feature
Amendment
AP: 2SS MIMO
AMPDU
5 GHz
3-4SS
40 MHz
11n (HT)
5 GHz
40 MHz
80 MHz
3-8SS
DL-MU-MIMO
160 MHz
256QAM
11ac (VHT)
4SS AP: DL-MU-MIMO
UL/DL-OFDMA
MU-EDCA
3-8SS
UL-MU-MIMO
160 MHz
256 & 1024QAM
11ax (HE)
Cumulative*
*With some minor exceptions:
5GHz not mandatory in 11ax but eco-system direction now well-established
Exception for IoT-class 20MHz-only HE STAs
Some novel features jump straight to mandatory, and some evolve from optional to mandatory

## Slide 3: EHT Should Follow that Successful Path, with the Following Headline Features
Mandatory
Optional
Amendment
4SS AP: DL-MU-MIMO
UL/DL-OFDMA
MU-EDCA
3-8SS
UL-MU-MIMO
160 MHz
256 & 1024QAM
11ax (HE)
6 GHz
Multiband 80+80 MHz
4SS AP: UL-MU-MIMO
Non-AP: UL/DL Simul MU-MIMO + OFDMA
160 MHz
HARQ
Explicit sounding to 16SS Implicit sounding
Low throughput PHY
3-16SS
320 MHz, 80+160 MHz
256QAM, 1024QAM
EHT
Cumulative*
Why these features?
See following slides

## Slide 4: 9.6 Channels Per Band is the Right Number Considering 320 MHz As a Mandatory Headline Feature[1-3,5,7,8,10]
Some enterprise customers share their WLAN configs with their vendor for help on optimizing / troubleshooting their deployments
Anonymous data from one vendor database of >30k configs and >900k 160MHz capable APs across 6 countries indicates:
Take-aways:
  Highest data rates enabled by widest bandwidths are not the driving factor
  2-3 channels is certainly too few channels; 3-5 channels is little favored too
  The mean of the preferred number of channels per deployment is 9.6
160MHz (1-2ch@160 + 1ch@80M)
80MHz (3-5ch)
40MHz (6-12ch)
20MHz (13-25ch)
Auto
0.02%
11%
64%
25%
0.02%
17%
59%
23%
Human Expert selection
Human + SW Expert selection
Manual
2GHz (11ad, 3-4ch)
0%
0%
Geometric mean of #ch ranges from 5.6 to 13 with 9.6ch as the mean
+ + + + +

## Slide 5: … so 320 MHz Doesn’t Make Sense As a Mandatory Headline Feature, but 160 MHz Could Be
When 11ac added 160 MHz, it needed new spectrum to make sense:
  11ac anticipated access to 5.35-5.47 GHz and 5.875-5.925 GHz, yielding 775 MHz of contiguous spectrum, and 3ch@160 + 3ch@80 MHz
  That spectrum didn’t eventuate, and 2ch@160 + 1-2ch@80M isn’t viable [slide-1]
There is much 11a/n/ac/ax legacy that supports 5 GHz but not 6 GHz
  Then 6 GHz cannot be considered “more 5 GHz channels”
  Instead 6 GHz is a third band, and must either be aggregated with 5 GHz or have sufficient channels
6-7.125 GHz opens up:
  7 new 160 MHz channels, which is close to the industry sweet spot
  3ch@320M + 1ch@160M, which is much below the industry sweet spot
  Strongly points to 320 MHz being a little used feature, and then optional
    Also 320MHz on an AP will severely impact power and size until a major process node shrink
  But 160 MHz makes enough sense for it to be mandatory
  And also non-contiguous 20/40/80M@5GHz + 20/40/80/160M@6GHz is very interesting
Open up 2.3 GHz, and let’s talk

## Slide 6: 16SS will Only Affect a Subset of Customers Considering 16SS As a Mandatory Headline Feature[1-3,5,7-10]
Mobile hotspot (1-2),
Lo end client
Lo end AP, hi end client
Hi end AP
Very hi end AP
Ultra hi end AP
Vendors progressively add antennas to APs, at a regular cadence
  Which is highly dependent on process node (and, closely related, power consumption and cost)
There continues to be a range of products, and the highest number of antennas are only found on the premium products
Based on historical patterns, 16SS is a 2024 technology
1
1
1
1
1
2-3
2-3
2-3
2-3
4
4
4
8
8
16
2000+
2007
2011
2019?
2024?
Key: Max spatial streams

## Slide 7: … so 16SS MHz Doesn’t Make Sense As a Mandatory Headline Feature, but Should Be Optional; And Needs Complementary Features
Since there are negligible 4+SS clients, this mandates
  UL+DL MU-MIMO STA support
  And practically simul OFDMA+MU-MIMO too, given likely adoption of 160 MHz
Sounding overheads increase 2x wrt 8SS: we need to bound the sounding overhead in order to achieve real gains:
  Continue explicit sounding but also add implicit sounding
  Let’s assume that the AP performs self calibration (avoid the 11n complexity)
  AP can compel non-AP STAs to transmit efficient implicit sounding on demand
    Requested via a field in the Trigger frame
    The STA shall add Extension LTFs / midamble / postamble / other that sounds all TX antennas, at the triggered bandwidth
    If a STA has RX antennas not associated with a soundable TX antenna, then the STA shall be able to detect and tolerate MU interference on the unsounded RX antennas
MDPU
Preamble
CTS
MU-RTS
Pad
BAs
Aggressive MU needed for efficiency

## Slide 8
But this style of thinking is a bit of a trap, because the overarching datum is
Customers want reliability and more client devices/AP
Higher speeds are secondary

## Slide 9: Obstacles to Higher Reliability
ISM users (microwave ovens, hoppers, etc)
Contention and collisions from 802.11 STAs, due to
  Active scanning
  Pre-11ax non-AP STAs that cannot be changed
  11ax STAs transmitting SU PPDUs
    Mitigated via MU EDCA parameters, BSR polling, and random access RUs
  Contention between APs
    Less impactful, and more feasible to address
A (partially) clean-sheet design for 6 GHz avoids some of this and can significantly mitigate the rest
  Recall, unlicensed spectrum means we’re stuck with original choices for 20 years.
  We should revisit our implicit and explicit design choices to decide if they’re right for 6 GHz for the next 20 years

## Slide 10: Moreover, We’re Missing a Mandatory Headline Feature … Mandatory 6 GHz will be Most Impactful
Adding 211% more channel bandwidth triples system capacity
  (3+25)=28x 20MHz channels today, plus 59x 20MHz channels
This, more than anything, is the most impactful way to improve 802.11 customer experience
  … and we should spend it wisely
802.11ac was a 5 GHz only standard, and ushered in widespread adoption of 5 GHz
  After 10 years of laggardly 5 GHz adoption
  EHT should do the same thing for 6 GHz
Mandatory 6 GHz proliferates 802.11 in that band, and quickly
  By comparison, 802.11 did not embrace 3.5 GHz, and that is now a de facto cellular band
  An early and widespread 802.11 presence maintains practical access to the band

## Slide 11: Multi-band Integrates 6 GHz into Existing Networks With Options for Reliability or Peak Data Rate[3-5,7,11]
Standalone BSS
P40/80M; NonContig 40/80M@5G+80/160M@6G
Classic concurrent multi-band BSSs
  No increase in peak data rate
Standalone BSS at 6 GHz
Standalone BSS at 5 GHz
Standalone BSS at 2.4 GHz
Standalone BSS
P40/80M; NonContig 40/80M@5G+80/160M@6G
Standalone BSS at 2.4 GHz
Beacons sent on each bands, with dual primaries
  Legacy STAs use the 5 GHz primary
  (EHT) STAs steered akin to ROMI parking; STAs needing highest QoS steered to 6 GHz primary
APs send MU and solicit TB PPDUs that are non-contiguous across two bands for higher data rates
  20/40/80/160MHz@5GHz + 20/40/80/160MHz@6GHz
AP/non-AP STA PPDU requirements are:
  M: Contiguous: TX, RX
  M: Non-contiguous dual band: TX+TX, TX1+TX2, RX+RX, RX1+RX2
    i.e. non-AP STAs can TX or RX on both bands simultaneously
BSS at 5/6 GHz with independent contention at 5/6 GHz
Standalone BSS at 2.4 GHz
BSS at 5/6 GHz with independent contention at 5/6 GHz
HD
HD
HD
Double Headed HD AP
HD
Non-contiguous HD + FDD
HD
Optional: Same as Double Headed HD AP but now the AP and some STAs support frequency-division duplex
  O: FDD: TX1+RX2, RX1+TX2
For lower latency communications
Natural extension to 2.4GHz but secondary importance
Notes: TX1+TX2 indicates transmission of two different PPDUs, one on 5GHz, one on 6 GHz.
RX1+RX2 indicates reception of two different PPDUs, one on 5GHz, one on 6 GHz.
TX1+RX2 indicates transmission of one PPDU at 5GHz plus reception of one PPDU on 6GHz
RX1+TX2 indicates reception of one PPDU at 5GHz plus transmission of one PPDU on 6GHz

## Slide 12: Clean-sheet 6 GHz Design (1/2)[5-7]
E.g. 10% of power
Broadcast Probe response (P20=5)
Beacon
Broadcast Probe response (P20=5)
Broadcast Probe response (P20=5)
First issue: 11ax is permitting 6 GHz usage already: at 11ax we propose to encourage 11ax towards:
  Preclude HT/VHT PHY formats at 6 GHz, no active scanning at 6GHz
  An 11ax AP at 6GHz must vacate a channel upon request by a cochannel neighboring EHT AP
  Otherwise EHT has no ability to make a clean-sheet design
Actively probing when there are 59 channels is suboptimal. Hurts QoS and burdensome for non-AP STAs
  a) Mandate every 6 GHz AP has a colocated or nearby companion 2.4/5 GHz AP or an application-specific discovery mechanism, b) mandate neighbor reports with TSF offset across bands to help with discovery, c) prohibit active scanning at 6 GHz
  Also, more frequent mini-Beacons and “Multi-channel Beacons” to help with passive scanning
  Multichannel Beacon = FDM of 20 MHz PPDUs, with Beacon sent on P20 and “Broadcast Probe Response” that includes the channel number of P20 sent on the other 20MHz subchannels; with power allocation to minimize range loss of the Beacon
E.g. 10% of power
E.g. 70% of power
E.g. 10% of power
ch13
ch9
ch5
ch1

## Slide 13: Clean-sheet 6 GHz Design (2/2)
Should we disallow 20 MHz channels?
  Some loss of Beacon range
  Some loss with nearby Primary spectrum services, since we lose spectrum in 40 MHz chunks
Should we redefine a TU to be 1000us at 6 GHz, to assist with coexistence with other technologies?
  We lean against – too awkward for 802.11, but the question bears raising
Should we prevent contention by non-AP STAs?
  Exclusively use random access RUs, TWT, BSR polling, MU/TB PPDUs instead
Should we add EVM in every CTS/Ack/BA frame / PPDU?
  Built-in rather than a Control Wrapper
Should we replace 11a format by a “Low Throughput” PHY format
  Next 2 slides …

## Slide 14: Issues with 11a in 6 GHz
Bandwidth indication is a kludge
  Doesn’t easily extend to 320MHz
  Never addressed non-contiguous
Doesn’t support higher MCSs, wider bandwidths or LDPC
Duplication at end of TXOP to avoid EIFS is inefficient
No future proofing
  E.g. no ability to insert an EVM
But EHT at 6 GHz still needs something for control frames and short data frames

## Slide 15: Low Throughput (LT) PHY Design
Summary:
Synthesis of:
  11a: limited to 1SS max, no xSTF, xLTF nor SIGB
  HTGF: 90deg rot at LTSIG
  HE: extra training around LTSIG (deferred from LLTF so preamble processing common for 20M and >20M)
Mandatory in 6GHz, replaces 11a PHY; prohibited in 2.4/5 GHz
48-56 LTSIG bits via 2 OFDM symbols or 40MHz raster (TBD)
8b CRC in LTSIG, 14-18b reserved bits available for future growth
  Fixed XOR mask in place of scrambler due to high count of reserved bits
MCS predefined up to 64KQAM
BW predefined up to 2560 MHz; could indicate non-contiguous too
Data field can be duplicated (RTS/CTS) or not (Ack/BA/short data/short mgmt.).
  Add a LTSIG bit “Last PPDU in TXOP” in lieu of duplicated-20MHz Ack/BA to avoid EIFS
LSTF
LSTF
LLTF
LLTF
LTSIG
LTSIG
LSTF
LSTF
LLTF
LLTF
LTSIG
LTSIG
Dup Data field
Dup Data field
Dup Data field
Dup Data field
LSTF
LSTF
LLTF
LLTF
LTSIG
LTSIG
LSTF
LSTF
LLTF
LLTF
LTSIG
LTSIG
Data field

## Slide 16: HARQ[2,5,6]
Promising direction for 802.11, targeted directly at increased reliability
Unlicensed noise model is collision-dominated, with uncontrolled and highly variable interference power per PPDU
  Not noise or controlled interference
  Have to avoid averaging good + trashed soft bits
  Often unclear when a PPDU is even directed to a STA
  Therefore we should limit HARQ to positively identified PPDUs
Recommend that HARQ only be allowed when the TA is predictable: i.e. MU/TB PPDUs
  Then AP knows own limitations, so only non-AP STAs negotiate buffer depth, etc

## Slide 17: Misc
We always see demand for the following, which should be permitted by the PAR:
  Client power saving
  Coexistence / regulatory

## Slide 18: Summary
Mandatory
Optional
Amendment
6 GHz
Multiband 80+80 MHz
4SS AP: UL-MU-MIMO
Non-AP: UL/DL Simul MU-MIMO + OFDMA
160 MHz
HARQ
Explicit sounding to 16SS Implicit sounding
Low throughput PHY
3-16SS
320 MHz, 80+160 MHz
256QAM, 1024QAM
EHT

## Slide 19: References
[1] 11-18-0789-10-0wng-extreme-throughput-802-11
[2] 11-18-1116-00-0eht-multi-ap-harq-for-eht (1)
[3] 11-18-1155-01-0eht-multi-ap-enhancement-and-multi-band-operations
[4] 11-18-1161-00-0eht-eht-technology-candidate-discussions
[5] 11-18-1171-00-0eht-view-on-eht-objectives-and-technologies
[6] 11-18-1180-00-0eht-discussion-on-eht-study-group-formation
[7] 11-18-1184-01-0eht-eht-discussions-on-throughput-enhancement
[8] 11-18-1190-01-0eht-discussion-on-eht-timeline-and-scope
[9] 11-18-1191-00-0eht-mu-sounding-improvements
[10] 11-18-1263-03-0eht-eht-subgroup-formation-motion
[11] 11-18-1271-00-0eht-eht-802-11-study-group-creation
[12] 11-18-1316-02-0eht-eht-802-11-way-forward
;