## Slide 1: Doppler Impact on OFDM Numerology for NGV
Date: 2018-09-10
Authors:

## Slide 2: Introduction
NGV can leverage existing 802.11 technology advances to enhance the communication reliability and throughput [1].
802.11n/ac/ax tone numerology with corresponding downclock rates can be good candidates for NGV.
Doppler induces channel variation and inter-subcarrier-interference (ICI), which limit the tone spacing choices.
In this contribution, we analyze the impact of Doppler on the design of NGV tone numerology.

## Slide 3: OFDM Numerology
For the same NGV signal bandwidth, different OFDM tone numerology can be designed.
  Smaller tone spacing (TS) can achieve better OFDM efficiency, (same cyclic-prefix (CP) duration).
  But observes worse ICI, and larger channel variation across OFDM symbols.
OFDM numerology candidates:
  TS=156.25kHz, FFTsize=64
    11ac 20MHz with 2x Downclock, and max CP of 1.6us
  TS=78.125kHz, FFTsize=128
    11ac 40MHz with 4x Downclock, and max CP of 3.2us
  TS=39.0625kHz, FFTsize=256
    11ax 20MHz with 2x Downclock or 11ac 80MHz with 8x Downclock
    Max CP of 6.4us

## Slide 4: Impact of Doppler
Doppler is common in vehicular communications, causing channel variation.
  Channel variation from symbol to symbol can be partially resolved by channel tracking techniques: midamble, traveling pilots, and etc.
  Channel variation within symbol causes unresolvable inter subcarrier interference (ICI).
ICI compensation is not practical in WiFi design.
  Degrades channel estimation accuracy.
  Affects data detection performance, especially high modulation order
For the same Doppler, the smaller tone spacing, the larger ICI shows up in the received signal.
  Need to control the ICI level for the largest Doppler speed.

## Slide 5: Consideration of ICI with Highest Speed
The design of OFDM numerology needs to consider the ICI from the highest speed.
C2C channel model is proposed for NGV studies [1, 4].
  Zero Doppler shift and spread are assumed for the LOS path.
  Assume that CFO loop tracks the LOS Doppler frequency shift.
  The impact of LOS Doppler will not show up in the link simulations.
In real vehicular environments, the LOS Doppler shift may not be fully compensated through the CFO tracking loop.
  Multiple path Doppler, rich reflections in high-traffic environments, especially non-line-of-sight scenarios.
  Only average Doppler shift can be tracked and compensated
  The residual ICI from LOS path can be dominating due to large power of LOS component.

## Slide 6: Numerical Simulations
Speed: 500km/h
10MHz signal bandwidth
Four different OFDM numerology:
  TS=156.25kHz, FFTsize=64
  TS=78.125kHz, FFTsize=128
  TS=39.0625kHz, FFTsize=256
  C-V2X: 15kHz TS
Evaluation metric: signal-to-interference ratio (SIR)
  Compute the average SIR for different OFDM numerology [2]

## Slide 7: Numerical Results: AWGN
  The average SIR for all four TS are: 73.0dB, 61.0dB, 48.9dB and 31.9dB.

## Slide 8: Numerical Results: Fading Channel (C2C4)

## Slide 9: Discussions
In fading channels (C2C4), the SIR on the deep faded tones can be even worse, due to the interference from adjacent strong tones.
The 11ac MCS 9 (256QAM-5/6) has sensitivity SNR @10%PER of ~27dB.
  Budget 10dB for all impairments. The needed SNR is ~37dB.
Observe from the average and per-tone SIR values:
  156kHz and 78kHz can support 256QAM-5/6 with good margin.
  39kHz can support 256QAM-5/6 in AWGN, but may have difficulty in fading channels
  15kHz can NOT support 256QAM-5/6
Tone spacing | 156kHz | 78kHz | 39kHz | 15kHz
Ave. SIR (dB) | 73.0 | 61.0 | 48.9 | 31.9
C2C4 minSIR(dB) | 59.0 | 52.2 | 35.4 | 31.8

## Slide 10: Summary
NGV can reuse 802.11n/ac/ax OFDM numerology with corresponding downclock rates.
The smaller the tone spacing is, the more ICI effect is observed from Doppler effect.
The SIR limits the effective SNR, which provides the guideline to choose the appropriate tone spacing.
SIR analyses show that TS=156kHz (20MHz 11n/ac 2xDC) and 78kHz (40MHz 11n/ac 4xDC) provide good ICI tolerance in both AWGN and fading channels.
When choosing the proper OFDM tone spacing, other system errors may also need to be taken into consideration, such as CFO/CPE estimation errors.

## Slide 11: Reference
[1] Hongyuan Zhang and etc., “802.11 For Next Generation V2X Communications”, IEEE 802.11-18/0513r2.
[2] URL: http://www.wirelesscommunication.nl/reference/chaptr05/ofdm/doppler/doppler1.htm
[3] Table 21-25, Draft P802.11REVmd_D1.0
[4] Jianhan Liu and etc., “11-18-0821-00-0ngv-ngv-channel-models”