## Slide 1: Further Discussion on Content of BPSK Mark
Date: 2018-09-06
Authors:

## Slide 2: Introduction
During the July meeting, the group discussed that BPSK Mark should be BCC ½ coded OFDM symbol to be utilized in future 802.11 specification (e.g. EHT)
  In 11-18-1156-01 [1], this discussion was brought up and the motion for a similar proposal was approved in 11-18-1068-08 [2]
In this presentation, we discuss a proposal for defining the content of BPSK Mark in TGba to allow a future 802.11 specification to utilize BPSK Mark
  If left to vendors’ choices and WUR is deployed in the market sooner than EHT for example, then EHT devices will not be able to classify a TGba wake-up packet.

## Slide 3: Content of BPSK Mark
BPSK Mark is not useful for WUR devices
BPSK Mark is not decodable by legacy 802.11 devices (based on the current draft of 11ax and previous amendments)
Content of BPSK Mark should be defined in TGba for future standard devices to classify Wake-up packet and the exact content of BPSK Mark should be defined in a future standard (e.g. EHT)

## Slide 4: Options for BPSK Mark Definition
Option 1
  Type: 2 bits
    Example: 0 = 1st gen. WUR deployed prior to EHT, 1=2nd gen. WUR deployed after EHT, etc.
  CRC: 8 bits
  Tail : 6 bits
  The rest bits are reserved and will be define in a future spec
Option 2
  Flipped RL-SIG
    All devices (legacy, 11ax, EHT) will classify it as 11a
  Later future spec can define a new content
Option 3
  RL-SIG, Mod (Length,3) = 0

## Slide 5: Straw Poll 1
Do you agree to make BPSK Mark classifiable by future amendments?
  Y/N/Abstain

## Slide 6: Straw Poll 2
Which of the following options do you support for BPSK Mark?
  Option A – Define a simple structure in TGba (Option 1 in Slide 4)
  Option B – Reuse RL-SIG (Option 2 and Option 3 in Slide 4)

## Slide 7: Straw Poll 3
Do you support BPSK Mark to be defined as follows ?
  Type – 2bits
  Tail – 6 bits
  CRC - 8 bits
  The rest bits are reserved

## Slide 8: Straw Poll 4
Which of the following options (as defined in slide #4) do you support for the content of BPSK Mark?
  Option A: Flipped RL-SIG (Option 2 in slide #4)
  Option B: L-SIG/RL-SIG with Length divisible by 3 (Option 3 in slide #4)

## Slide 9: Straw Poll 5
Do you support to define BPSK Mark as L-SIG/RL-SIG with Length divisible by 3?

## Slide 10: References
[1] Alphan Sahin, et. al., “11-18-1156-01-00ba-a-comparison-of-bpsk-mark-options”, July 2018
[2] Alphan Sahin, et. al., “11-18-1068-08-00ba-proposed-spec-text-on-the-construction-of-the-bpsk-mark”, July 2018