## Slide 1: TDD-SP Coexistence
Date: 2018-09-12
Name | Affiliation | Address | Phone | Email
Mohamed Abouelseoud | Sony | 1730 N. First Street, San Jose CA 95112 | +1-408-352-4027 | Mohamed.Abouelseoud(at)sony.com
Kazuyuki Sakoda | Sony | 1730 N. First Street, San Jose CA 95112 | +1-408-352-4405 | kazuyuki.sakoda(at)sony.com

## Slide 2: Problem Statement
Devices operating TDD SP can access the channel without sensing the channel
TDD-SP is not enforcing listen before talk to access the channel for transmission
There are concerns from 11ay members of TDD-SP Coexisting with SRDs and even other TDD-SP devices
Other devices operating CBAP might struggle to access the channel and suffer from severe interference or even completely blocked if collocated with TDD-SP devices

## Slide 3: Proposed Approach
TDD-SP devices should announce its existence and channel usage (time allocation and spatial allocation) so other devices can take actions

## Slide 4: Actions taken by STAs detecting TDD-SP devices (1)
STAs might switch to another channel knowing that there is a TDD SP device
STAs might try to access the same channel if the TDD-SP device is lightly scheduled
STAs might try to access the same channel at time when the TDD-SP device TX/RX slots are unassigned

## Slide 5: Actions taken by STAs detecting TDD-SP devices (2)
STAs might access the channel if TDD-SP is lightly scheduled in its direction

## Slide 6: Actions taken by STAs detecting TDD-SP devices (3)
STAs might access the channel in a different direction that is not affected by the TDD-SP device

## Slide 7: Possible TDD-SP Announcement
  TDD-SP shall transmit a frame in the direction of the scheduled TDD-SP transmission
    Announce TDD-SP channel occupancy (Extended Schedule element)
    Announce TDD-SP Scheduling information ( TDD Slot Schedule and TDD Slot Structure elements)
    Announce TX beam direction used by TDD-SP devices for each TDD Slot Schedule element

## Slide 8: TDD-SP Coexistence Example
TDD-SP devices should send a beacon in each direction where there is a scheduled TDD-SP transmission
The beacon should contain:
  Extended schedule element
  TDD Slot Structure element
  TDD Slot Schedule elements with TX Beam ID of the scheduled transmission
  TRN fields

## Slide 9: TDD-SP Coexistence Example (2)
A STA trying to access the channel compares the beacon TX beam ID with the TX beam ID of TDD Slot Schedule elements, when matching:
  A TDD SP device is active
  STA can switch channel or try to access the channel if possible
STA can decide based on the TDD-SP Slot Schedule element if and when to access the channel

## Slide 10: TDD-SP Coexistence Example (3)
TDD-SP device sends TRN fields with the beacon for other STAs to determine direction of potential interference
STA performs RX beam training to determine the RX beams affected by the TDD-SP device
STA can access the channel in directions other those affected by the TDD-SP device

## Slide 11: Straw Poll (1)
Do you support the following approach for TDD-SP coexistence?
“A STA employing TDD-SP shall transmit periodic beacon frame in the direction of each scheduled TDD-SP transmission to announce TDD-SP channel occupancy, scheduling information and spatial directional information so other STAs can take actions”
  Yes
  No
  Abstain