## Slide 1: Discussion on the Frame Body in VL Wake-up frame
Date: 2018-09-11
Authors:

## Slide 2: Introduction
If the Length Present field of a Wake-up frame is set to 1, the Frame Body field is present
  The Frame Body field may contain multiple Paged STAs
  The units and the maximum size of Frame Body are 2 octets and 16 octets respectively [1]
In this contribution, we discuss the encoding of the Frame Body field

## Slide 3: Encoding of the Frame Body field
The Frame Body field may consist of multiple Wake-up STA Info field
  Each Wake-up STA Info field should identify a WUR STA
Since the length of WUR ID (12 bits) is not octet-aligned, proper encoding of the Wake-up STA Info field must be considered
  In terms of identification, efficiency or functionality
The length of the Wake-up STA Info fields can either:
    Option 1) 12 bits
    Option 2) 8 bits
    Option 3) 16 bits
 | Type (Wake-Up) | Length Present (1) | Length | Address | TD Control | Frame Body | FCS
Wake-up STA Info | Wake-up STA Info | Wake-up STA Info
TBD | TBD | TBD

## Slide 4: Option 1) 12-bit Wake-up STA Info field
Wake-up STA Info field contains a 12-bit WUR ID
Pros:
  Simple
  No ambiguity on identification
Cons:
  Not octet-aligned
  The number of Wake-up STA Info fields may not be indicated by the Length field
  Padding with variable length occurs depending on the number of target WUR STAs
    In case of 12-bit padding, the padding must be distinguished from WUR identifiers
      Any 12-bit value can be assigned to WUR STA as a WUR identifier
WUR ID
12
L | FB size (bits) | # of WIDs | Padding (bits)
0 | 16 | 1 | 4
1 | 32 | 2 | 8
2 | 48 | 3 or 4 | 12 or 0
3 | 64 | 5 | 4
4 | 80 | 6 | 8
5 | 96 | 7 or 8 | 12 or 0
6 | 112 | 9 | 4
7 | 128 | 10 | 8
 | Type (Wake-Up) | Length Present (1) | Length (2) | Address | TD Control | Frame Body | FCS
Wake-up STA Info | Wake-up STA Info | Wake-up STA Info
12 | 12 | 12
Padding
12

## Slide 5: Option 2) 8-bit Wake-up STA Info field
Wake-up STA Info field contains a partial WUR ID
Pros:
  Most efficient
  Octet-aligned
Cons:
  The partial WUR ID may not identify the whole WUR STAs in the BSS
    Additional rules need to be defined to avoid ambiguity
  The number of Wake-up STA Info fields may not be indicated by the Length field
  Padding occurs depending when odd number of Wake-up STA Info fields are present
    The padding must be distinguished from the partial WUR IDs
partial WID
8
L | FB size (bits) | # of WIDs | Padding (bits)
0 | 16 | 1 or 2 | 8 or 0
1 | 32 | 3 or 4 | 8 or 0
2 | 48 | 5 or 6 | 8 or 0
3 | 64 | 7 or 8 | 8 or 0
4 | 80 | 9 or 10 | 8 or 0
5 | 96 | 11 or 12 | 8 or 0
6 | 112 | 13 or 14 | 8 or 0
7 | 128 | 15 or 16 | 8 or 0
 | Type (Wake-Up) | Length Present (1) | Length (2) | Address | TD Control | Frame Body | FCS
Wake-up STA Info | Wake-up STA Info | Wake-up STA Info
8 | 8 | 8
Wake-up STA Info | Wake-up STA Info | Padding
8 | 8 | 8

## Slide 6: Option 3) 16-bit Wake-up STA Info field
Wake-up STA Info field contains a WUR ID and additional 4-bit Wake-up Control subfield
Pros:
  Octet-aligned
  No ambiguity on identification
  The Length field directly indicates the number of Wake-up STA Info field
  The remaining 4-bit can be used for additional control information for each WUR STA
Cons:
  Less efficient
WUR ID | Wake-up control
12 | 4
L | FB size (bits) | # of WIDs | Padding (bits)
0 | 16 | 1 | 0
1 | 32 | 2 | 0
2 | 48 | 3 | 0
3 | 64 | 4 | 0
4 | 80 | 5 | 0
5 | 96 | 6 | 0
6 | 112 | 7 | 0
7 | 128 | 8 | 0
 | Type (Wake-Up) | Length Present (1) | Length (2) | Address | TD Control | Frame Body | FCS
Wake-up STA Info | Wake-up STA Info | Wake-up STA Info
16 | 16 | 16

## Slide 7: Considerations
We prefer option 3) 16-bit Wake-up STA Info field
  11ba already defines several ways to wake-up multiple STAs simultaneously
    E.g., group-addressed wake-up, FDMA wake-up
  In terms of efficiency, using VL Wake-up frame doesn’t have much benefit compared to other schemes
  Allowing additional control information for each STA will effectively differentiate the usage of VL Wake-up frame from other schemes
The usage of the 4-bit Wake-up Control subfield needs further discussion

## Slide 8: Possible candidate for the Wake-up Control subfield
Scheduled wake-up
  Increasing the channel utilization and reducing the power consumption of WUR STA
  WUR STA addressed by a Wake-up STA Info field wakes up its PCR after a certain amount of time indicated by the Wake-up Control subfield
    E.g., 4-bit Wake-up Control subfield can indicate 16 levels of delay time
    The unit of the delay time can be negotiated via PCR
  AP can schedule the expected wake-up timings of multiple WUR STAs subject to:
    The size of the buffered BUs of each STA
    The PCR transition delay of each STA
Scheduled wake-up in VL Wake-up frame can also benefit when AP operates the WUR channel different from the PCR primary channel
  Whenever AP switches between the WUR channel and PCR channel, it performs NAV synchronization

## Slide 9: AP Operation Examples
PCR channel
WUR channel
NS
ML
CA
NAV Sync.
ML Wake-up Frame
Channel Access
GA Wake-up Frame
NS
DL BU (STA1)
NS
ML
CA
NS
DL BU (STA2)
NS
ML
CA
NS
DL BU (STA3)
Channel switch
Channel switch
PCR channel
WUR channel
NS
GA
CA
NS
DL BU (STA1)
DL BU (STA2)
DL BU (STA3)
Channel switch
Channel switch
VL Wake-up Frame
PCR channel
WUR channel
NS
VL
CA
NS
DL BU (STA1)
DL BU (STA2)
DL BU (STA3)
Channel switch
STA1 Awake
STA2 Awake
STA3 Awake
STA1 Awake
STA3 Awake
STA1 Awake
STA2 Awake
Individually addressed wake-up
Group addressed wake-up
Multiple addressed
scheduled wake-up
STA3 Awake
STA2 Awake
Scheduled Wake-up Time (STA1)
Scheduled Wake-up Time (STA2)
Scheduled Wake-up Time (STA3)

## Slide 10: Conclusion
The Frame Body field in VL Wake-up frame consists of multiple Wake-up STA Info fields
  The Wake-up STA Info field contains:
    12-bit WUR ID
    4-bit Wake-up Control information
Scheduled Wake-up using VL Wake-up frame
  WUR STA addressed by a Wake-up STA Info field wakes up its PCR after a certain amount of time indicated by the Wake-up Control subfield
    Increasing the channel utilization and reducing the power consumption of WUR STA

## Slide 11: Strawpoll 1
Do you agree the following?
  When the Frame Body field is present in the WUR Wake-up frame, the Frame Body field contains one or more Wake-up STA Info field
  The size of the Wake-up STA Info field is 2 octets
  The Wake-up STA Info field consists of:
    12-bit WUR ID subfield
    4-bit Reserved
Y/N/A

## Slide 12: Strawpoll 2
Do you agree the concept of scheduled wake-up in slide 8-9?
Y/N/A