## Slide 1: Discovery Channels For 6 GHz Band
Name | Affiliation | Address | Phone | Email
Alfred Asterjadhi | Qualcomm Inc. |  |  | aasterja@qti.qualcomm.com
George Cherian | Qualcomm Inc. |  |  | 
Abhishek Patil | Qualcomm Inc. |  |  | 
Date: 2018-08-20

## Slide 2: Introduction
TGax PAR has opened the 6 GHz band to be used by 11ax STAs
  Regulatory discussions for access rules, and restrictions are still ongoing
Discovery/scanning were discussed in [1] under these assumptions
  Dual Radio AP (2.4/5GHz plus 6 GHz)
    Anchored in 2.4/5 GHz band to perform discovery/scanning functions
    Allows discovery/scanning/roaming in 6 GHz only under certain conditions
  Non-AP STA discovers 6 GHz APs in the 2.4/5 GHz bands and optionally
    Passively scan the 6 GHz bands for the presence of APs
    Actively scan if the STA already knows the AP that it is probing
In this presentation we discuss the following
  Enable discovery of 6 GHz-only APs (infrastructure and soft APs)
  Limit channel pollution due to scanning in the 6 GHz band
  Reduce scanning latency for 6 GHz operations

## Slide 3: Problem Statement
Up to 1280 MHz of spectrum are expected to be available in 6 GHz
  Which can be split in to up to 64 channels of 20 MHz each,
    Each of these channels are greenfield (i.e., no incumbent dot11 devices)
Without defining any rules all 64 channels need to be scanned
  Increases scanning latency for non-AP STA scanning for 6 GHz APs
    Total scan time of up to 1.2 s (if MinChannelTime=20 ms (more in other cases))
    Leads to increased power consumption, and increased connectivity outage
  Impacts systems’ performance of those STAs already operating in these channels
    Due to probe storming effect, reduced access opportunities, increased collisions, etc.
Affecting especially certain applications with stringed QoS requirements
  Augmented reality (AR)/virtual reality (VR), real-time voice, video, gaming, etc.

## Slide 4: Proposed Solution
Define 6 GHz channelization for discovery purposes
  Reducing scanning times and improving its efficiency
    For passive, active scanning, and roaming
  Improve system’s efficiency of 6 GHz compared to 2.4/5 GHz
Allocate a subset of channels as discovery channels
  Option 1: Subset located in a contiguous portion of 6 GHz band
    E.g., scanning concentrated only in the lower portion of the band
  Option 2: Subset consists of equally spaced 20 MHz channels
    E.g., scanning concentrated in channels 1, 5, …, 13, etc.
    We describe this option in more detail in subsequent slides
Similar to what has been proposed in [2] for 11ba

## Slide 5: Discovery Channels (DC)
DCs are equally spaced with locations defined in the standard
  DC spacing is of nonunitary periodicity (e.g., every 4, 8, 16, …, channels)
  The higher the DC periodicity the better since
    Scanning latency reduces with reduced number of DC channels
    System efficiency increases with increased number of non-DC channels
A DC periodicity requires AP to satisfy any of the following
  Operating with enough BW to cover one DC
    E.g., 80 MHz for 4C, 160 MHz for 8C, 320 MHz for 16C
  Delegating its advertisement to neighboring APs that cover a DC
    E.g., using Neighbor Report IEs with AP’s information

## Slide 6: DC Periodicity: Evaluation
Definitions:
  SYS Ratio – Percentage of channels where no scanning activity exists
  Max Scan Time – Maximum scanning time to detect AP in the 6 GHz band
    MinChanTime is equal to 20 ms
Recommend the definition of DCs with 8-C periodicity
  Good SYS ratio, and sufficient number of DC channels
  Reduced scanning latency, and one DC can easily be covered in a 160 MHz BSS
DC periodicity | # of DCs | Max Scan Time | SYS Ratio
1 channel (base) | 64 | 1280 ms | 0 %
4 channels | 16 | 320 ms | 75 %
8 channels | 8 | 160 ms | 87.5 %
16 channels | 4 | 80 ms | 93.5 %
32 channels | 2 | 40 ms | 98.3 %

## Slide 7: HE BSS Setup with 8-C DCs
AP 1 sets up 160 MHz BSS (at least one DC will fall in BSS BW)
  Select BSS’s primary channel to coincide with the discovery channel
    Preferred option for HE BSS due to its simplicity, and minimal spec changes
    BSSs with independence of PC and DC can be considered as part of EHT
AP 2 and AP 3 set up 80 MHz BSS (i.e., with narrower BW)
  Possible e.g., when including DC (AP1) or delegating neighbor AP (AP3)
… | CH9 | CH10 | CH11 | CH12 | CH13 | CH14 | CH15 | CH16 | CH17 | …
… | DC | SYS | SYS | SYS | SYS | SYS | SYS | SYS | DC | …
S20
P20
AP 1
S40
S80
S20
P20
AP 2
S40
AP 3
S20
P20
S40

## Slide 8: Scanning in Discovery Channels
Scanning is same as baseline except that
  Scanning (active and passive) limited to discovery channels (DC) only
Fast Passive scanning (inherit .11ai functionalities)
  FILS Discovery frames should be generated at least every MinChanTime
Active scanning (inherit .11ai functionalities)
  STAs wait for at least MinChanTime before sending Probe Request frame
    FD frame indicates whether AP allows EDCA-based pre-association frames
      May include power control and other information in carried elements
  If nothing is detected then move to next DC or send directed Probe Request

## Slide 9: Conclusion
We discussed discovery channels for 6 GHz band that
  Reduce scanning latency
  Improve scanning efficiency
  Increase systems’ performance
Compared to baseline all-channel scanning access

## Slide 10: Spec text
A 6G STA may perform active and passive scanning and send pre-association frames only in discovery channels, which are indexed as c = (n-1)*8, where n varies between 1 to 8. The STA shall not send pre-association frames in channels that are not discovery channels.

## Slide 11: References
[1] G. Cherian (Qualcomm Inc.) et. al., “11-18/1256r0 11ax operation in 6 GHz”
[2] G. Li (Apple) et. al., “11-17/1608/r7 WUR discovery-frame for smart scanning”