## Slide 1: HEz Passive Ranging Schedule Announcement
Date: 2018-09-12
Authors:

## Slide 2: Introduction
The purpose of this presentation is to propose mechanism and formats for announcement of the availability window for HEz Passive Ranging to ‘passive’ clients that desire to use the signal exchange to estimate their location.

## Slide 3: HEz-Ranging Sequence for Passive Location
DL
NDP
UL
NDP
TF
Responder
Initiator iSTA 1
Initiator
iSTA 2
UL
NDP
UL
NDP
DL
NDPA
Poll
TF
PR
PR
iSTA to rSTA
LMR
TF
rSTA to
iSTA
LMR
UL
NDP
TF
iSTA to rSTA
LMR
LCI, DL LMR
UL LMR
iSTA to rSTA
LMR
LCI/LMR broadcasting frames
TOD
UL LMRs
Responder LMRs
HE SU NDP PPDU
Example contents
HE SU NDP PPDU

## Slide 4
Passive Location built on HEz Passive Ranging
AP (RSTA)
AP
AP
AS
AS
AS
AS
AS
AS (ASTA/ISTA)
The client to be located need to be able to find out when and on what channel and BW each AP is scheduling its Hez Passive Ranging with its client anchor stations (AS – ASTA/ISTA).
Cross ranging
Client to be located
APs nominally on different channels
AS - Client Anchor Station

## Slide 5: Proposal for HEz Passive Ranging Announcement
Signal the required parameters for the HEz Passive Ranging availability window in each of the AP’s beacon.
Parameters to include:
Partial TFS [10TU] – Time to start of next HEz Passive Ranging availability window
Duration [10TU] – Time duration of next Hez Passive Ranging availability window
Periodicity [10TU] – Current periodicity of Hez Passive Ranging availability window
BW [unit TBD] – Bandwidth used for next HEz Passive Ranging window
Notes:   Report circle also enables to increase the MCS and reduce the broadcast time, since the chances of the client being close to at least one ASTA in the NW is much higher.

## Slide 6: Number of Nsts in HEz Passive Ranging
Propose to limit the max number of Nsts in HEz Passive Ranging to 4.
Notes:   Report circle also enables to increase the MCS and reduce the broadcast time, since the chances of the client being close to at least one ASTA in the NW is much higher.

## Slide 7: Straw Poll
Should the schedule announcement for HE Passive Ranging be specified as in slide 5?
Y: N: A:

## Slide 8: Straw Poll
Should the max number of Nsts in Passive HEz Ranging be limited to 4?
Y: N: A:

## Slide 9
Thank You!