## Slide 1: LMR and LCI Reporting For Passive Location
Date: 2018-09-12
Authors:

## Slide 2: Introduction
The purpose of this presentation is to propose mechanisms and formats for LMR and LCI reporting in the HEz Passive Ranging exchange for the purpose of passive location.

## Slide 3: HEz-Ranging Sequence for Passive Location
DL
NDP
UL
NDP
TF
Responder
Initiator iSTA 1
Initiator
iSTA 2
UL
NDP
UL
NDP
DL
NDPA
Poll
TF
PR
PR
iSTA to rSTA
LMR
TF
rSTA to
iSTA
LMR
UL
NDP
TF
iSTA to rSTA
LMR
LCI, DL LMR
UL LMR
iSTA to rSTA
LMR
LCI/LMR broadcasting frames
TOD
UL LMRs
Responder LMRs
HE SU NDP PPDU
Example contents
HE SU NDP PPDU

## Slide 4: Passive Location HEz iSTA to rSTA LMR
Dialog Token
CFO to Responder
TOD error
TOA error
Per time-stamp:
  Type – TOD or TOA
  Time stamp validity – Valid or Not
  Time-stamp
  RID of transmitter
Notes:   Report circle also enables to increase the MCS and reduce the broadcast time, since the chances of the client being close to at least one ASTA in the NW is much higher.

## Slide 5: HEz LCI/LMR Broadcast Frame 1 Content
LCI table element
DL LMR:
  Dialog Token
  TOD error
  TOA error
  Per time-stamp:
    Type – TOD or TOA
    Time stamp validity – Valid or Not
    RID of transmitter (RID=0 for RSTA)
    Time-stamp
Notes:   Report circle also enables to increase the MCS and reduce the broadcast time, since the chances of the client being close to at least one ASTA in the NW is much higher.

## Slide 6: HEz LCI/LMR Broadcast Frame 2 Content
Per iSTA device:
  Dialog Token
  CFO to Responder
  TOD error
  TOA error
  Per time-stamp:
    Type – TOD or TOA
    Time stamp validity – Valid or Not
    Time-stamp
    RID of transmitter
Copy of the LMR report from each ASTA/Initiator
Notes:   Report circle also enables to increase the MCS and reduce the broadcast time, since the chances of the client being close to at least one ASTA in the NW is much higher.

## Slide 7: LCI Table
For LCI Table:
  Content option bit
  Content option bit = 0:
    Current LCI table number
    Countdown to opportunity planned to contain LCI table
  Content option bit = 1:
    LCI table
    LCI table number
    Responder LCI info
    RIDs, MAC addresses and LCI info for participating ISTAs
    Report LCI for ISTAs in relation to Responder location in order to save bits (3x16 bits enough)

## Slide 8: Straw Poll
Should the Passive Location HEz iSTA to rSTA LMR have the content described in slide 4?
Y: N: A:

## Slide 9: Straw Poll
Should the HEz LCI/LMR Broadcast frames have the content described in slides 5 and 6?
Y: N: A:

## Slide 10: Straw Poll
Should the LCI Table have the content described in slide 7?
Y: N: A:

## Slide 11
Thank You!