## Slide 1: Sounding-only Support During Ranging
Date: 8/7/2018
Authors:

## Slide 2: Abstract
Current az ranging protocol
  VHTz or HEz based on sounding frames
  Timing estimation through LMR feedback
Current explicit MU sounding has high overhead
  Majority of the airtime overhead is due to the feedback frame
Adding implicit BF support to existing ranging protocol can allow low overhead sounding
  Allow the ranging protocol to skip LMR
  Allow a trigger based sounding
  Minimal changes to existing ranging protocol and optional feature

## Slide 3: Background for CIDs 102, 103
102: “The ranging protocol should support to not include the LMR at the end of the measurement phase. This option can be used to do bidirectional implicit beamforming with a smaller airtime overhead. When a STA includes the "only sounding mode supported" flag in its ranging capabilities, RSTA shall not send the LMR to this ISTA.”
103: “Measurement sessions should be able to indicate a sounding only session by including a flag during the sounding negotiation.”

## Slide 4: Current Ranging
VHTz
HEz
NDPA
NDP
NDP
RSTA
ISTA
SIFS
SIFS
HEz Polling
HEz Measurement Sounding
SIFS
SIFS
RSTA to ISTA
LMR
LMR
SIFS

## Slide 5: Observation on Current Ranging
As a side benefit of current ranging protocol
  Allows for implicit channel estimation using NDPs
  Both directions
Possibility of supporting an efficient sounding for non-ranging use cases
  Allow to skip the LMR feedback stage
  Allow to trigger STAs to periodically range without expecting LMR (invalid or low resolution)

## Slide 6: Current Sounding
MU precoding requires CSI [1]
  11ac and 11ax define only explicit feedback to learn CSI
Most airtime taken up by CSI feedback (Compressed Beamforming Frame)
  Length of CBF will grow further with increasing number of streams

## Slide 7: Updates to Ranging Parameter
Add new field to the existing IE [2]
  Ranging parameters element
  Sounding capable – depends on the trigger frame
  Sounding-only capable – support only sounding mode

## Slide 8: HEz mode: Trigger based Sounding
Trigger frame [2]
  Trigger type
  Location trigger subtype
HEz sounding-only example
HEz Polling
TF
(sounding)
SIFS
UL NDP
UL NDP
TF
(sounding)
UL NDP
DL NDP
SIFS
SIFS
SIFS

## Slide 9: Updates to Ranging NDPA
Add flag to ranging NDPA [2]
  Feedback type
  STA Info
VHTz sounding-only example
NDPA
NDP
NDP
RSTA
ISTA
SIFS
SIFS

## Slide 10: Summary
As part of the scope of Ranging, supporting a sounding-only mode should be considered
  Indication in the capabilities
    Flag added to the Ranging parameters element
  Sounding and Sounding-only without feedback mode to be supported
  STAs can trigger a sounding-only session with capable peers using a flag during HEz polling or Ranging NDPA in VHTz mode
  Alternatively, allow a trigger mechanism for STAs to trigger ranging even if LMR is invalid or of low resolution

## Slide 11: References
[1] MU sounding improvements, IEEE 802.11-18/1191
[2] Draft standard, ammendment 8: Enhancements for positioning, IEEE P802.11az D0.4