## Slide 1: Use Cases, Requirements and Potential Wireless Approaches for Industrial Automation Applications
Date: 2018-11-01
Author:

## Slide 2: Abstract
This presentation addresses requirements and use cases commonly experienced by R3 Communications in the industrial automation sector. Apart from discussing these use cases and their requirement implications, we also address potential approaches to realize the latency requirements typically seen in industrial automation use cases. We finally present some results of measurement campaigns that highlight the potential of the discussed approaches.

## Slide 3: Shift to Smart Factory
TODAY:
STATIC PRODUCTION SETUP
Inflexible, centralized production flow, labor intensive processes.
TOMORROW:
SMART MANUFACTURING SYSTEMS
Flexible, smart, mobile and adapting
systems that support even lot size “1”
Product 1
Product 2
Product 1
Product 2

## Slide 4: Architecture of Industrial Automation Systems
Master PLC
Unit Control
(PLCs)
Control Level
Field
Level
Production Cell
Module
Module
Module
Devices (Sensors, Actuators, Primary Technology )

## Slide 5: Relevant Performance Metrics in Industrial Automation Systems
Cycle time: Elapsed time from writing of sensor reading into memory until reading actuation command from memory.
Reliability: Packet error rate per individual communication component in the loop.
Coverage: Range spanned between loop components.
Density: Amount of loops per unit (production cell).
Raw payload: Size of the sensor reading or actuation command (additional protocol overhead might apply).
Roaming: Necessity for handover functionality.

## Slide 6: Illustration Cycle Time and Components
Sensor
Actuator
PLC
Tx
Rx
Rx
Tx
Ttransfer
Ttransfer
Twireless
Ttransfer
Ttransfer
Twireless
Tcompute

## Slide 7: Typical Use Cases
automation of transport (AGVs, monorails, AS/RS)
LOGISTICS
(LAM)
MACHINE
TOOLS
Instantaneous adaptation of shop floor machinery
closed loop control between PLC and field devices (I/Os)
FIELD-LEVEL
CONTROL
PLC-2-PLC
COMMUNICATION
fixed-group PLC master/slave set-up (multiple hierarchies)
same as field-level control, but safety-oriented
SAFE FIELD-
LEVEL CONTROL
HUMAN IN THE
LOOP (HMI)
wireless control for humans (integrated in safety control)
wireless edge control of / collaboration between robots
COORDINATED
ROBOTS
HUMAN-ROBOT
COEXISTENCE
wireless control / worker safety in dynamic production cells
SAFETY

## Slide 8: Use Case Requirements
Cycle Time
Reliability
Coverage
<50 ms
10 ms
<1 ms
10-3
10-6
10-9
< 5
10-20
> 50
10 m
100 m
Field-Level Control
PLC-2-PLC Communication
Safe Field-Level Control
Human in the Loop (HMI)
Cycle Time
Reliability
Coverage
Density
<50 ms
10 ms
<1 ms
10-3
10-6
10-9
< 5
10-20
> 50
10 m
100 m
Logistics (LAM)
Machine Tools
Coordinated Robots
Human-Robot Coexistence
Density
Use cases with large packet size (> 50 Byte)
Use cases with small packet size (< 50 Byte)

## Slide 9: Contemporary Wireless Capabilities
100ms
50ms
20ms
10ms
1ms
10-9
10-6
10-3
Latency (sensor-to-controller-to-actor)
Reliability (error/success transmission ratio)1
Remote
Control
Wireless
HART
Bluetooth
ZigBee
802.11p
Standard
WLAN
DETERMINISTIC
REQUIRMENTS
SIEMENS IWLAN
LTE/4G

## Slide 10: Token-Passing Principle & Cooperation
logical token ring
wireless channel
deterministic
behavior with
low latencies
failure recogni-
tion and auto-
matic reaction
cooperative re-
transmission of
lost data packets
fault
tolerance
wireless channel
wireless channel
physical token ring
ARCHITECTURE
COOPERATION
cable based
IEEE 802.5 Token
Ring Standard as
basis for EchoRing
immediate relaying
transmission failure
fault
reaction

## Slide 11: Performance Studies
Scenario:
5 stations
Indoor, low mobility
5 GHz band, no interference
.11g physical layer (10 MHz)
100 Byte packet size
~108 transmitted packets
Schemes:
  Basic ring
  CSMA
  Recovery ring
  EchoRing (token-passing + cooperative communications)
~10 x 20 meters

## Slide 12: Experimental Evaluation
OVERALL PERFORMANCE
LATENCY BEHAVIOUR
COOPERATION GAIN
Data Packet Loss Rate above layer 2 for all stations
Packet Delay Distribution at Station
Station 2’s PLRs for various ring sizes

## Slide 13: Conclusions
Low-latency, low-rate requirements generally encountered in industrial automation applications
Useful categorization along safety/non-safety applications and/or payload sizes.
R3 Communications observes somewhat similar requirements for automation applications as Intel (Ref Missing) and NIST (IEEE 802.11-14/1784r0) – difference mainly with our emphasis on cycle times.
Token-passing is a powerful approach to guaranteeing low latencies

## Slide 14: References
C. Dombrowski and J. Gross (R3 Communications) “EchoRing: A Low-Latency, Reliable Token-passing MAC Protocol for Wireless Industrial Networks” European Wireless Conference, 2015 .
Richard Candell (NIST), “Reliable, High Performance Wireless System for Factory Automation,” IEEE 802.11 RTA TIG contribution, IEEE 802.11-14/1784r0, October 2018.