## Slide 1: EHT should adopt a single, technology neutral PAR & CSD
6 November 2018
Authors:
Name | Company | Phone | email
Brian Hart | Cisco (US) |  | brianh@cisco.com
David Kloper |  |  | dakloper@cisco.com
Peter Ecclesine |  |  | pecclesi@cisco.com
Pooya Monajemi |  |  | pmonajem@cisco.com
Mukesh Taneja | Cisco (India) |  | mutaneja@cisco.com
Andrew Myles | Cisco (Australia) | +61 418 656587 | amyles@cisco.com

## Slide 2: EHT should use the old model of one technology-neutral PAR, just like 802.11g/n/ac/ax!
Situation
Complication
Solution
There is a desire by some stakeholders for 802.11 to transition to a two-year cadence for PHY/MAC standards
Two mechanisms (with one & two PAR/CSDs respectively) are proposed to implement the two-year cadence concept
The use of technology-specific PAR/CSDs by both mechanisms is unsatisfactory
The 2nd PAR/CSD in the 2nd mechanism is likely to be unsuccessful or may cause both PAR/CSDs to fail
EHT should be developed using the old model of one technology-neutral PAR, just like 802.11g/n/ac/ax!

## Slide 3: There is a desire by some stakeholders for 802.11 to transition to a two-year cadence for PHY/MAC standards
  There is a perception by some stakeholders that the traditional approach of utilising technology neutral PAR/CSDs is inappropriate for the next 802.11 PHY/MAC generation
  The basic concern is the open nature of technology neutral PAR/CSDs means that a new PHY/MAC generation standards is only completed every 5 years or so …
  … whereas some stakeholders would prefer a two year cadence of smaller and more focused PHY/MAC standards to:
    Drive more frequent Wi-Fi product improvements & turnover
    Enable Wi-Fi to respond in a more timely manner to competition from other technologies, including 3GPP defined NR-U

## Slide 4: Two mechanisms (with one & two PAR/CSDs) are proposed to implement the two-year cadence concept
Technology-specific PAR/CSD
Multiple PAR/CSDs
A first PAR/CSD for standardisation of specific technologies in the next two years or so
A second PAR/CSD for more complicated features requiring further study in the longer term
One PAR/CSD constrained to specific technologies that are more likely to be suitable for standardisation in the next two years
eg 320 MHz, 16SS & possibly others (multi-band?) for the generation beyond 11ax
1
2
Refined “compromise” proposal that allows for additional & more complex features to be developed in a second PAR/CSD for the longer term
Original proposal focused on short term goal of a new PHY/MAC standard in the next two years or so

## Slide 5: The use of technology-specific PAR/CSDs by both mechanisms is unsatisfactory
Technology-specific PAR/CSD
Multiple PAR/CSDs
A first PAR/CSD for standardisation of specific technologies in the next two years or so
A second PAR/CSD for more complicated features requiring further study in the longer term
One PAR/CSD constrained to specific technologies that are more likely to be suitable for standardisation in the next two years
eg 320 MHz, 16SS & possibly others (multi-band?) for the generation beyond 11ax
1
2
More technical discussion is required before forcing EHT into a direction that is unlikely to be changed
16SS is an example of a proposed EHT1 feature that has been clearly inadequately discussed
802.11aa is an historic example showing that PAR changes are unlikely

## Slide 6: More technical discussion is required before forcing EHT into a direction that is unlikely to be changed
  The nature of technology-specific PAR/CSDs with a two year horizon, as proposed for EHT, is that they constrain work to features predicted to be ready for standardisation within two years
  This choice is problematic because:
    The SG has not yet had the benefit of technical presentations & discussions to inform any choice or prediction
      Such discussions typically occur during the TG phase; they could occur during the SG phase but the EHT SG Chair has deprioritised technical presentations this week
    Constraining the features means the TG is unable to take advantage of exciting or valuable new ideas as they emerge over the coming years
      It is possible to change the PAR/CSD but this is a rare & difficult/slow process
    Specifying required features now means the TG will be forced to complete features whose technical merit or feasibility is known to be diminishing
      It is possible to change the PAR/CSD but this is a rare & difficult/slow process

## Slide 7: 16SS is an example of a proposed EHT1 feature that has clearly been inadequately discussed
  One of the features that has been proposed for the first technology-specific PAR/CSD (EHT1) is 16SS
  16SS has some obvious benefits if high throughput is the goal
  However, it is not really suitable or applicable as a technology for an EHT1 standard to be finished within two or so years
    Based on historical patterns, 16 SS is a feature probably only suitable for the ultra high end in about 2024 (see 11-18-1539-00)
    16SS will be complex to standardise with two years in manner that is useful
      Explicit sounding overheads scale with antenna count and so …
      … we need greater compression of explicit sounding
      … we need hooks for implicit sounding
  There has been some discussion of these issues but more is needed to understand & potentially mitigate these issues before specifying 16SS as suitable as a standard feature in two years time

## Slide 8: 802.11aa is an historic example showing that PAR changes are unlikely
  The 802.11aa PAR defined 5 work areas, with HW changes implicitly precluded:
    Graceful degradation of audio video streams when there is insufficient channel capacity, by enabling packet discarding, without deep packet inspection
    Increased robustness in overlapping BSS environments, without the requirement for a centralised management entity
    Intra-Access Category prioritization of transport streams by modifying EDCA timing and parameter selection, without deep packet inspection,
    Improved link reliability & low jitter characteristics for multicast/broadcast audio video streams,
    Interworking with relevant 802.1AVB mechanisms (802.1Qat/Qav/AS)
  Partway through the project, TGaa realized it could address 3-4 of these items well; but could not “move the needle” on another 1-2 items
  However, TGaa found it was easier to put something in the 802.11aa draft, however weak or pointless, rather than change the PAR

## Slide 9: The 2nd PAR/CSD in the 2nd mechanism is likely to be unsuccessful or may cause both PAR/CSDs to fail
Technology-specific PAR/CSD
Multiple PAR/CSDs
A first PAR/CSD for standardisation of specific technologies in the next two years or so
A second PAR/CSD for more complicated features requiring further study in the longer term
One PAR/CSD constrained to specific technologies that are more likely to be suitable for standardisation in the next two years
eg 320 MHz, 16SS & possibly others (multi-band?) for the generation beyond 11ax
1
2
Technical issue: two EHT TGs are likely to waste preambles
Process issue: it is unlikely two TGs working on very similar topics can successfully amend 802.11 in parallel
Ecosystem issue: insignificant minor amendments puts 802.11’s inter-generational success at risk

## Slide 10: Technical issue: two EHT TGs are likely to waste preambles
  Suppose two parallel TGs (EHT1 & EHT2) are formed, as proposed, to develop amendments with short term & long term time horizons
  It is likely that EHT1 will need a new preamble optimized for the short term features
  It is also likely that EHT2 will need another new preamble optimized for the long term features
  Each new preamble increases the false alarm rate and adds overheads and (HT/VHT carry 8us of overheads; HE carries 12us of overheads)
  A critical prerequisite for 802.11’s long term evolution in existing bands is to have an extremely high bar before a new preamble is allocated

## Slide 11: Process issue: it is unlikely two TGs working on very similar topics can successfully amend 802.11 in parallel
  A key question is whether the 802.11 WG processes will enable two parallel TGs (EHT1 & EHT2) on very similar topics to both succeed?
  The likely answer is that either both TGs will fail to make progress or only the EHT1 will make progress
    EHT1 & EHT2 will compete for human resources & meeting slots; in similar situations, the usual outcome is that the short term project starves the longer term project of resources
    Even if both TGs manage to obtain sufficient resources, there will a significant coordination burden because they are likely to be making changes to the same clauses; parallel sessions will make the burden even worse
    There is a high likelihood that EHT1 will dump “difficult” issues into EHT2 causing it to accumulate a negative perception as the “never-never project”; and this is likely to become reality
  The former outcome is clearly unsatisfactory; the latter outcome has the same issues as the first proposed mechanism

## Slide 12: Ecosystem issue: insignificant minor amendments puts 802.11’s inter-generational success at risk
  802.11’s major MAC/PHY standards generations (11b/g/n/ac) have succeeded (at least partially) because each new amendment has:
    Remained backward compatible with the previous generation
    Enabled a significant increase in capability, driving an upgrade cycle
    Incorporated both peak rate improvements (for the excitement), as well as a range of other background features (to actually enhance users’ experiences)
      eg aggregation, multi-user operation, improved power save mechanisms, deleting low MCSs, …
    Avoided “Osborning” the previous generation
      Note: you need to know 1983 technology to understand this! 
  Splitting EHT into two PAR/CSDs only two years apart, with limited differentiating or value adding features, …
  … is likely to put 802.11’s well established history of success across multiple generations at risk

## Slide 13: EHT should be developed using the old model of one technology-neutral PAR, just like 802.11g/n/ac/ax!
  IEEE 802.11 WG already has a proven, successful development model
    One “5 year” next generation project at a time, delivering a massive increase in capability on many fronts for 802.11’s multitudinous customers and use cases
    … which enables the Wi-Fi Alliance to develop appropriate certifications of high profile features and efficiency enhancements
    … in a manner that is timely to satisfy market needs
    … and does not require the IEEE 802.11 WG to make impossible predictions long into the future
  There is one obvious choice for EHT …
    One, technology-neutral PAR …
    … that will probably take five or so years to ratification
  … just like 802.11g, 802.11n, 802.11ac, 802.11ax!