## Slide 1: EHT Channel Modeling
Date: 2018-10-22
Authors:
Name | Affiliations | Address | Phone | Email
Jianhan Liu | Mediatek |  |  | jianhan.liu@mediatek.com
Alireza Ghaderipoor |  |  |  | 
Thomas Pare |  |  |  | 

## Slide 2: Introduction
Some well accepted features for EHT are listed as follows
  Multi-AP Coordination
  320MHz bandwidth (including operations in 6GHz band)
  16 Spatial Streams
Technical proposal selection requires a more precise channel model for link level simulations and PHY abstractions for system level simulation in EHT.
  Channel models for 6GHz band and 320MHz BW need to be added for EHT.
  To enable 16 spatial streams, the correlations among the antennas must be taken into account due to the foot size of an AP and large number of antennas;

## Slide 3: Channel models for 6GHz band and 320MHz BW
Given that 6GHz band is close to 5GHz band, we suggest that the channel models for 6GHz band use the same model as in 5GHz band.
Generation of 320MHz Channel:
  Using the channel generation method described in [1]:
System Bandwidth W | Channel Sampling Rate Expansion Factor | PDP Tap Spacing
W ≤ 40 MHz | 1 | 10 ns
40 MHz < W ≤ 80 MHz | 2 | 5 ns
80 MHz < W ≤ 160 MHz | 4 | 2.5 ns
160 MHz < W ≤ 320 MHz | 8 | 1.25 ns
320 MHz < W ≤ 640 MHz | 16 | 0.625ns
Table 1: Channel sampling rate expansion (tap spacing reduction) factors

## Slide 4: Correlations in Multiple Antennas Systems
In 11n/ac/ax, we model the correlations at AP with a correlation matrix with antenna distance and we model the correlations at the non-AP STA with a correlation matrix with antenna distance
Given that EHT is likely to introduce more antennas at the AP and the foot-size of EHT AP may be different, we suggest to add the following correlation parameters to EHT.
  Three correlation matrices at the AP.
    Low correlations: with antenna distance
    Medium correlations: with antenna distance
    High correlations: with antenna distance
  The correlation parameter at the Non-AP STA keeps antenna distance
In 11n/ac/ax, each channel tap has a different correlation matrix realization [2][3], EHT should follow the same method.

## Slide 5: Possible Antenna Array Configurations
There are multiple possible antenna array configurations for 16 antenna systems:
  Circular
  Polarized
  3D
Do we need to introduce the correlation modelling for the most likely configurations too?

## Slide 6: Channel Models for Multiple AP Systems
is the channel between AP #m and non-AP STA #n with infinity antenna distance.
Base on the assumption is the antenna distances between two APs and two non-AP STAs are large, we have

## Slide 7: References
[1] “TGac Channel Model Addendum”, IEEE 802.11-09/0308r12, Greg Breit, etc.
[2] “Tgax channel model document”, IEEE 802.11-14/0882r4, Jianhan Liu, etc.
[3] “TGn Channel Models”, IEEE 802.11-03/0940r4, Vinko Erceg, etc.