## Slide 1: Proposed resolution of CID 3518
Date: 2018-11-14
Name | Affiliation | Address | Phone | Email
Mohamed Abouelseoud | Sony | 1730 N. First Street, San Jose CA 95112 |  | Mohamed.Abouelseoud(at)sony.com
Kazuyuki Sakoda |  |  |  | kazuyuki.sakoda(at)sony.com

## Slide 2
CID | PP.LL | Comment | Proposed Change
3518 | 11.31.6 | Multi-band discovery assistance allows discovery of an AP or PCP that this STA is connected to however this is not enough. For some use cases, the STA might need to talk to a non-AP/PCP STAs in the same BSS or even in other BSSs . A STA should find other non-AP in that BSS and other BSS | The standard should define a mechanism to allow new STA to find neighbor STAs in an on-demand fashion. Commenter is willing to provide resolution text.

## Slide 3: Overview
Latency is critical for consumer devices use cases
Multi-band discovery assistance is included in 802.11ay D2.0 to allow a new STA to trigger on-demand sector sweeping instead of the continuous exhaustive sector sweeping all the time by AP
(Multi-band
capable AP)
New STA
(Multi-band
capable STA)
Established sub-6GHz link
AP
Potential mmW link
However, new STA might not be in the mmW range of the multi-band capable AP to form a mmW link
New STA needs to find other neighbor STAs that might not be multi-band capable in an on-demand fashion
New STA needs to establish a STA-to-STA link at the time of joining the BSS

## Slide 4: Example
New STA can use multi-band capability to trigger on-demand SSW (Multi-band Discovery Assistance)
A multi-band capable AP can start on-demand SSW for the new STA
The multi-band AP should inform STA 1 about the new STA to start on-demand SSW
STA1
Multi-band capable AP
New STA
Multi-band capable STA
mmw link
Established sub-6GHz link
Potential mmW link
AP
STA1
Multi-band capable AP
New STA
Multi-band capable STA
mmw link
Established sub-6GHz link
Potential mmW link
AP
AP 1
Potential mmW link
Potential mmW link

## Slide 5: Recap: multi-band discovery assistance
New STA connects to AP using lower band signal
New STA sends DMG discovery assistance request to AP on lower band
AP responds with DMG discovery assistance response to new STA on lower band
AP starts TXSS on mmW band
DMG Discovery Asst.
Request
DMG Discovery Asst.
Response
Lower band signal
mmW band signal
DMG discovery signal to STA2 (TXSS)
AP
(multi-band)
STA2
(New STA, multi-band)
STA 2
(New STA, multi-band)
AP
(multi-band)
Joining BSS request

## Slide 6: Extending neighbor STA discovery
AP propagates a DMG discovery assistance request to STA 1 on mmW band
STA 1 responds to AP with DMG discovery assistance response if it supports discovery assistance on mmW band
AP responds to new STA with DMG discovery assistance response on lower band
STA 1 starts TXSS on mmW band
STA 2
(New STA, multi-band)
AP
(multi-band)
STA 1
(Existing STA)
Joining BSS request
Ask to perform TXSS
TXSS
DMG Discovery Asst.
Request
DMG Discovery Asst.
Response
AP
(multi-band)
Lower band signal
mmW band signal
STA2
(New STA, multi-band)
STA1
(Existing STA)
DMG discovery signal to STA2 (TXSS)
DMG Discovery Asst.
Request
DMG Discovery Asst.
Response

## Slide 7: Extending neighbor STA discovery
It would be beneficial if we can perform both discovery process altogether
STA 2
(New STA, multi-band)
AP
(multi-band)
STA 1
(Existing STA)
Joining BSS request
Ask to perform TXSS
TXSS
DMG Discovery Asst.
Request
DMG Discovery Asst.
Response
AP
(multi-band)
Lower band signal
mmW band signal
STA2
(New STA, multi-band)
STA1
(Existing STA)
DMG discovery signal to STA2 (TXSS)
DMG Discovery Asst.
Request
DMG Discovery Asst.
Response
DMG discovery signal to STA2 (TXSS)

## Slide 8: How to enable neighbor discovery
DMG Discovery Assistance element is already defined in the 802.11ay D2.0
The Information Request frame can be used to propagate the DMG Discovery Assistance element from the STA requesting discovery assistance to other STAs
The Information Response frame can be used to send the DMG Discovery Assistance element including a response to the propagated discovery assistance request
AP processes the responses and sends one response to the STA requesting discovery assistance ( FST Setup Response frame)

## Slide 9: Propagated discovery assistance request
New STA DMG Capabilities element
DMG Discovery Assistance element
Information Request frame
Element ID
Length
Discovery Assistance Control
Element ID Extension
Discovery Assistance Window Length
Sector Sweep Start Time (optional)
Discovery Assistance Request Status
Temporary AID (optional)
Dwelling Time (optional)
Discovery Assistance Type
Dwelling Time Present
Reserved

## Slide 10: Discovery assistance response
DMG Discovery Assistance element
Information Response frame
Element ID
Length
Discovery Assistance Control
Element ID Extension
Discovery Assistance Window Length
Sector Sweep Start Time (optional)
Discovery Assistance Request Status
Temporary AID (optional)
Dwelling Time (optional)
Discovery Assistance Type
Dwelling Time Present
Reserved

## Slide 11: Discovery assistance response to new STA
AP sets the discovery assistance response to the new STA as follows:
  If discovery assistance is performed through scheduling DMG beacon transmission sweeping all sectors or initiating TDD beamforming:
    Sector Sweep Start time and Discovery Assistance Window Length fields represent the discovery assistance campaign
  If the discovery assistance is performed through scheduled beamforming training period or scheduled TDD beamforming period:
    Discovery Assistance Window Length field is the time duration of the all STAs beamforming periods
* Details in document 1910r0

## Slide 12: Straw Poll
Do you support the proposed resolution of CID 3518?
  Yes
  No
  Abstain