## Slide 1
Issues on negotiating WUR mode
Date: 2018-11-12
Authors:

## Slide 2: Introduction
The WUR mode negotiation is performed by the Action frame including the WUR mode element[1]
  The duty cycle period, on duration, and starting point is set by negotiation process
The WUR Parameter field in WUR mode element can be differentiated by the type of WUR negotiation frame:
  For some negotiation types(WUR denial, Enter WUR suspend, etc), WID and WUR channel offset is not needed
  For some negotiation types(WUR denial with WUR mode response status=2), the additional parameter(e.g. Duty Cycle Period) is needed
In this contribution, we discuss about different WUR Parameter field for the type of WUR negotiation frame, which addresses CID 447, 449

## Slide 3: Recap: WUR mode element
The WUR mode setup frame, WUR mode element is included to deliver the parameters
In the WUR Parameter field:
  If it is sent by AP, it contains WUR ID, WUR channel offset, Starting Time of the WUR Duty Cycle, Group ID List(depending on WUR Parameter Control field)
  If it is sent by STA, it contains On Duration and Duty Cycle Period

## Slide 4: Modification for the WUR mode element for denial
When AP denies the WUR negotiations with 2 in WUR mode response status field, AP needs to specify the proposed value for appropriate WUR duty cycle
  With no appropriate value, STA needs to determine the appropriate value of the duty cycle period by trial and error
When AP denies, other parameters are not needed
  WUR ID, WUR channel offset, Starting Time of the WUR Duty Cycle, Group ID List

## Slide 5: Proposed structure of WUR parameter
The WUR parameter field for WUR mode response frame can be structured depending on the response type
  When the WUR mode response status field is 0 (Accept)

## Slide 6: Proposed structure of WUR parameter (continued)
  When the WUR mode response status field is 1 (Denial with unspecified reason)
  When the WUR mode response status field is 0 (Denial because of long duty cycle period)

## Slide 7: Conclusion
In this presentation, we discussed various type of WUR mode element depending on the response type
  For denial, the needed parameters are different
We suggest the various type of WUR parameter field depending on the WUR Mode response status value

## Slide 8: Reference
[1] IEEE P802.11ba D1.0