## Slide 1
Issues on WUR duty cycle scheduling
Date: 2018-11-12
Authors:

## Slide 2: Introduction
In Draft 1.0, the WUR duty cycle operation has been adopted to reduce time that WURx operates in awake state [1]
  The duty cycle period, on duration, and starting point is set by negotiation process
Because of the different duty cycle period and channel for FDMA, it is hard to deliver the broadcast wake-up frame, which indicates:
  buffered group-addressed BU
  Counter soliciting the BSS parameter update in STA
In this contribution, discussion about transmission procedure of the broadcast wake-up frame, which addresses CID 308, 985, and 986

## Slide 3: Broadcast WUR frame transmission with Duty Cycle Operation
The WURx of STA may operate based on the negotiated duty cycle schedule[2]:
  AP indicates the unit of the duty cycle period and starting point
  STA indicates the on duration and the duty cycle period
However, because of different duty cycle in each STA, it is hard to manage the schedule of WUR frame transmission, especially for the broadcast WUR frame
STA2 DC=1/16
STA3 DC=1/12
STA4 DC=1/3
STA1 DC=1/4
2T
TON_1 = ½ T
5T
3T
3T
TON_2 = ¼ T
TON_3 = ¼ T
T (e.g. 10ms)
STA4 starts from t1
t0
t1
t2
t3
t4
t5
t6
t7
STA1, STA2, STA3 starts from t0
Notes: 현재 spec 상 WID/Group ID/multiple WID 로는 individually addressed BU를 indicate,
Broadcast WUR로만 group addressed BU를 indication할 수 있음(Group ID/multiple WID로는 group address BU indication 부분이 없음)
Broadcast WUR로 group addressed BU indication->단말에서 Wake-up 이후 implicit sleep(관련 PCR 동작)

## Slide 4: Broadcast WUR frame transmission with FDMA Operation
In addition to the different duty cycle operation, the WUR FDMA operation makes even harder of the transmission of broadcast WUR frame
  Since the different STA uses different channel for receiving WUR frame, the transmission procedure of broadcast WUR frame should be performed in each channel

## Slide 5: Issues and the suggestion
The decision of on duration and the duty cycle period by STA makes the scheduling of transmission of Wake-up frame harder
Especially, the difficulty of transmitting broadcast frame may cause the long delay for transmission of the buffered BU and indication of updated BSS counter
To manage the duty cycle scheduling, AP needs to modify the parameters of duty cycle operation
  Suggest to include duty cycle period and on duration parameter in WUR parameter field transmitted by AP

## Slide 6: Additional method for transmitting broadcast Wake-up frame
If AP transmits the broadcast wake-up frame to all negotiated STA in primary 20MHz channel, the following procedure can be easily operated
  The Cascade indicator in Beacon frame may indicate that there is the following wake-up frame

## Slide 7: Conclusion
In this presentation, we discussed scheduling issues in duty cycle operation and FDMA operation
  Especially in transmitting broadcast wake-up frame
The suggestion for the management issue on WUR duty cycle operation is the inclusion of duty cycle period and on duration parameter in WUR parameter field in WUR mode element
The additional procedure for transmitting broadcast wake-up frame cascading the WUR beacon frame may help to wake all STA up or indication of updated BSS counter

## Slide 8: Reference
[1] IEEE P802.11ba D1.0
[2] 17/651r2 Indication for WUR Duty Cycle