## Slide 1: IPv6 ND Proxy - why it matters for 802.11 -
Date: 2018-11-09
Authors:
November 2018

## Slide 2: Abstract
This submission indicates a new IETF reference for the 802.11 WMN STA Proxy IPv6 Neighbor Discovery Service function
This submission also proposes 1 variations for the implementation of this proxy function, a pure routing version that does not leak the MAC addresses from the wireless side, and a L3 bridging version whereby the proxy advertises the IPv6 address of the STA together with its MAC address.

## Slide 3: IPv6 ND proxy references
https://datatracker.ietf.org/doc/draft-ietf-6lo-rfc6775-update/
https://datatracker.ietf.org/doc/draft-ietf-6lo-backbone-router/
https://datatracker.ietf.org/doc/draft-ietf-6lo-ap-nd/
Pascal Thubert
November 2018

## Slide 4: Unmet expectations
Solicited node multicast requires highly scalable L2 multicast
  IEEE does not provide it => turns everything into broadcast
  IPv6 ND appears to work with broadcast on 802.1 fabrics up to some scale ~10K nodes
IPv6 ND requires reliable and cheap broadcast
  Radios do not provide that => conserving 802.1 properties over wireless is illusory
  RFC 4862 cannot operate as designed on wireless
  Address uniqueness is an unguaranteed side effect of entropy
802.11 expects proxy operation and broadcast domain separation
  802.11 provides a registration and proxy bridging at L2
  Requires the same at L3, which does not exist (NULL ref to ND proxy)
  Implementations provide proprietary techniques based on snooping (SAVI)
  => widely imperfect
  RFC 6775 solves the problem for DAD in one BSS
  This update enables a registration for proxy and routing services across the ESS
November 2018

## Slide 5: Use AND implementation of mCast in IPv6 ND
IPv6 Discovery protocols use multicast flooding
  Assuming a lower layer multicast support
  Not just IPv6 NDP but also mDNS, etc…
Layer-2 destination set to 3333XXXXXXXX
Layer-2 fabric handles as broadcast (all nodes)
Broadcast clogs the wireless access at low access speed (typically 1Mbps) on all APs around the fabric
Broadcast self interferes on attached wireless mesh and drains the batteries on all nodes
November 2018

## Slide 6: Flooding for mobility
MAC address reachability flooded over L2 switch fabric
Device sends RS to all routers link scope mcast
Router answers RA (u or m)
Device sends mcast NS DAD to revalidate its address(es)
Device sends mcast NA(O)
An ND proxy, aka backbone router, limits the broadcast domain to the backbone
IPv6 STA moves from AP within ESS:
November 2018

## Slide 7: flooding for Neighbor Discovery
Router looks up ND cache (say this is a cache miss)
Router sends NS multicast to solicited-node multicast @;
here that is 3333 FF00 00A1
Targets answers unicast NA
Target revalidates ND cache for the router, usually unicast
Router creates ND cache entry
6TiSCH proxies at the backbone router on behalf of device
Packet comes in for 2001:db8::A1
November 2018

## Slide 8: ND proxy drafts
November 2018

## Slide 9: In a nutshell
  Provide for draft-thubert-6lo-rfc6775-update-reqs
  draft-ietf-6lo-rfc6775-update (RFC-to-be 8505)
        The Layer-3 equivalent to the wireless association by a STA
        Enables registration to both ND proxy and IPv6 routing services
  draft-ietf-6lo-ap-nd
        Protects addresses against theft (Crypto ID in registration)
  draft-ietf-6lo-backbone-router
        Federates 6lo meshes over a high speed backbone
        The Layer-3 equivalent to the bridging operation by an AP
November 2018

## Slide 10: RFC 6775 Update (RFC-to-be 8505)
P.Thubert, E. Nordmark, S. Chakrabarti, C. Perkins

## Slide 11
6LBR
6BBR
Router/Server
Bridged
Ethernet
Router/Server
Router/Server
RFC 4861/4862
RFC 6775
STA/6LN
AP/6LR
Routerver
Router/ver
Router
PIO
MTU
RA (u|mcast)
RA (u|mcast)
PIO
MTU
SLLA
November 2018
802.11

## Slide 12
6LBR
6BBR
STA/6LN
AP/6LR
NS (ARO)
SRC = 6LN LL **
DST = 6BBR LL **
TGT = 6LN
SLLA = 6LN
UID = ROVR
TID included
* Can be Anycast
Create binding state
RFC-to-be 8505
** link local
November 2018
802.11

## Slide 13
6LBR
6BBR
RFC-to-be 8505
STA/6LN
AP/6LR
NA (ARO)
SRC = 6BBR LL **
DST = 6LN LL **
TGT = 6LN
TLLA = 6LN
UID = ROVR
TID included
** link local
November 2018
802.11

## Slide 14: Status of the document
IANA steps
  https://www.iana.org/assignments/icmpv6-parameters/icmpv6-parameters.xhtml#icmpv6-parameters-codes-type-157-code-suffix
Done RFC Editor disambiguations and edition
RFC Editor state : RFC-EDITOR *
  * Awaiting final validation by authors, 2 of them pending
November 2018

## Slide 15: draft-ietf-6lo-ap-nd
P. Thubert, B. Sarikaya, M Sethi, R. Struik

## Slide 16: Expectations
First come first Serve address registration
  First registration for an address owns that address till it releases it
  The network prevents hijacking
Source address validation
  Address must be topologically correct
  Source of the packet owns the source address
First Hop Security only?
  Proxy ownership and routing advertisements not protected yet
November 2018

## Slide 17
6LR
LP Node
NS (EARO, CIPO*, Nonce and NDPSO**)
AP/6LR
STA/6LN
AP-ND
NA (EARO(status=0))
NS (EARO(ROVR=Crypto-ID))
NA (EARO(status=Validation Requested), Nonce)
* Crypto-ID Parameters Option
** NDP Signature Option
November 2018
802.11

## Slide 18: Recent changes
Published -08
René Struik joined as contributing author
Updated the computation of the Crypto-ID
  Crypto-Id in EARO is a truncated hash of the node's public-key
  Digital signature (SHA-256/NIST P-256 or SHA-512/EdDSA) in NDPSO is executed on additional material (nonces, etc…, see updated section 6.2) for proof of ownership of the private key
  Uses both nonces from the 6LN and 6LR
Removed SHA-256 for EdCSA to comply with RFC 8032.
November 2018

## Slide 19: draft-ietf-6lo-backbone-router
P. Thubert

## Slide 20: Unmet expectations
Scale an IOT subnet to the tens of thousands
  With device mobility (no renumbering)
  Controlled Latency and higher Reliability using a backbone
Deterministic Address presence
  Route towards the latest location of an address
  Remove stale addresses
November 2018

## Slide 21
6LBR
6BBR
Router/Server
Router/Server
Router/Server
STA/6LN
AP/6BBR
Router/Server
Router/Server
Router/Server
NS DAD (ARO)
NS (ARO)
SRC = UNSPEC
DST = SNMA
TGT = 6LN
UID = ROVR
TID included
SRC = 6LN LL **
DST = 6BBR LL **
TGT = 6LN
SLLA = 6LN
UID = OVR
TID included
* Can be Anycast
Create binding state
Create proxy state
Bridged
Ethernet
RFC-to-be 8505
Backbone router
* Omitted in general
** link local
November 2018
802.11
AP/6BBR

## Slide 22
6LBR
6BBR
Router/Server
Bridged
Ethernet
Router/Server
Router/Server
RFC-to-be 8505
STA/6LN
AP/
6BBR
Router/Server
Router/Server
Router/
Server
NA (O) *
NA (ARO)
SRC = 6BBR LL **
DST = 6LN LL **
TGT = 6LN
TLLA = 6LN
UID = ROVR
TID included
* Omitted in general
** link local
DAD time out
SRC = 6BBR LL **
DST = SNMA
TLLA = 2 modes
TGT = 6LN
Backbone router
November 2018
802.11
AP/6BBR

## Slide 23
6LBR
6BBR
Router/Server
Bridged
Ethernet
NA (~Override)
Proxy NS (EARO)
Router/Server
Router/Server
RFC-to-be 8505
NA (EARO)
STA/6LN
AP/6BBR
Router/Server
Router/Server
Router/
Server
NS lookup
Packet
Backbone router
802.11
November 2018

## Slide 24: 6BBR Status
Quite Stable, no recent change
WGLC is needed to make final progress

## Slide 25: Resulting flows

## Slide 26: Initial time
Routers within subnet have a connected route installed over the subnet backbone.
PCE probably has a static address in which case it also has a connected route
Connected
Route to subnet
November 2018
Wireless
Domain

## Slide 27: First advertisements from GW (RA, IGP, RPL)
Gateway to the outside participate to some IGP with external network and attracts all extra-subnet traffic via protocols over the backbone
Default
Route
In RIB
November 2018
Wireless
Domain
Wireless
Domain
Wireless
Domain
Wireless
Domain
Wireless
Domain

## Slide 28: IPv6 ND Registration to 6LR and 6LBR
Directly upon NS(ARO) or indirectly upon DAR message, the backbone router performs DAD on behalf of the wireless device.
DAR
NS
(ARO)
DAD
NS DAD
(ARO)
November 2018
Wireless
Domain

## Slide 29: IPv6 ND Registration and Proxy for NS ARO
NA(ARO) or DAC message carry succeful completion if DAD times out.
NA(Override) is optional to clean up ND cache stale states, e.g. if node moved.
DAC
NA
(ARO)
Optional NA(O)
November 2018
Wireless
Domain

## Slide 30: IPv6 ND Proxy for RPL
The BR maintains a route to the WSN node for the DAO Lifetime over instance VRF. VFR may be mapped onto a VLAN on the backbone.
RPL
DAO
Host
Route
Optional NA(O)
November 2018
Wireless
Domain

## Slide 31: RPL over the backbone
The BBR maintains a route to the WSN node for the DAO Lifetime over instance VRF that is continued with RPL over backbone.
RPL
DAO
RPL DAO
Host
Route
November 2018
Wireless
Domain

## Slide 32: Duplication
DAD option has:
Unique ID
TID (SeqNum)
Defend with NA if:
Different OUID
Newer TID
NS DAD
(ARO)
NA (ARO)
NS
(ARO)
November 2018
Wireless
Domain

## Slide 33: Duplication (2)
DAD option has:
Unique ID
TID (SeqNum)
Defend with NA if:
Different OUID
Newer TID
DAR
NA
(ARO)
DAD
November 2018
Wireless
Domain

## Slide 34: Mobility
RPL
DAO
Optional NA(ARO)
Host
Route
DAD option has:
Unique ID
TID (SeqNum)
Defend with NA if:
Different OUID
Newer TID
NA (ARO) with older TID (loses)
November 2018
Wireless
Domain

## Slide 35: Resolution
Packet
NS
lookup
NA ARO option has:
Unique ID
TID (SeqNum)
NA (ARO)
November 2018
Wireless
Domain

## Slide 36: Resolution (2)
NS
lookup
Mixed mode ND
BBR proxying over the backbone
NA (ARO)
Packet
November 2018
Wireless
Domain

## Slide 37: Conclusion
Proxy ND Service for IPv6 is complex; a real specification from the IETF was missing so far and the description in 802.11 was very high level
The IETF is finally producing a specification for IPv6 ND proxy; 802.11 might consider adding a reference to that specification as the recommended IPv6 ND proxy technique
Additionally, as 802.11 11.22.14 mentions a Layer 3 function, 802.11 might consider integrating the routing proxy function as one of the accepted ND proxy modes in addition to the bridging proxy.