## Slide 1: CR for CID 915, 1100 and 1132
Date: 2018-11-11
Authors:

## Slide 2
Abstract
In this contribution, we propose resolutions for CID 915, 1100 and 1132.

## Slide 3: CIDs
CID | Clause Number(C) | Page(C) | Line(C) | Comment | Proposed Change | Resolution
915 | 4.3.15a | 22 | 2 | A WUR non-AP STA that supports reception of WUR PPDU with High Data Rate may fail to receive the WUR frame in bad channel conditions. In such situations, it would be better for the WUR AP to switch to Low Data Rate; however currently there is no mechanism for WUR STAs to provide feedback to the WUR AP. | In the event of CRC or MIC errors during reception of WUR PPDUs carrying WUR frames with High Data Rate addressed to a WUR non-AP STA, add options for the STA to provide feedback to the AP in one of the following two ways: 1) As an Event Report e.g. "FCS Error Event" 2) As a request to switch to Low Data Rate Based on the feedback from the STA, AP can decide to use the more robust LDR for subsequent WUR frames addressed to the STA. | 
1100 | 9.4.2.273 | 31 | 38 | A non-AP STA should be able to opt to receive a WUR frame at low data rate. High and low data rates are defined in the draft, but a non-AP STA has no remedy if the AP decides to transmit to in high data rate. | add a row on "preferred data rate" in Table 9-318e and the associated procedures so that a non-AP STA can have some remedy if an AP decides to transmit to it using high data rate. Otherwise, there is no point to define a high data rate if high data rate is not being used at all. | 
1132 | 31.6.1 | 55 | 1 | A WUR non-AP should have a remedy in case the WUR AP chooses to transmit to it using HDR and if HDR doesn't work well as a part of the WUR negotiation process. | Provide a remedy in the WUR negotiation process for WUR non-AP STA to switch to a LDR if HDR doesn't work well for the current channel condition. | 

## Slide 4: Discussion (1/2)
Two data rates are defined for 11ba devices: LDR and HDR
  LDR is designed to reach all STAs in the BSS, including those on the “cell edge”
  HDR is meant to support higher spectral efficiency compared to LDR [1]
Currently there is no communications between the AP and the STA regarding which data rate to use for the wake up frames
  A STA can indicate support for the reception of a HDR wake up frame [2]
  It seems that it is up to the AP to select LDR or HDR
  A STA has no remedy to negotiate a better rate if the current rate is too high (fail to receive) or too low (low efficiency)

## Slide 5: Discussion (2/2)
This can lead to the following problems as pointed out by CID 915, 1100 and 1132
  A STA may not be woken up by a HDR WUR frame even if it can receive the WUR beacons correctly (assuming that the WUR beacons are transmitted using LDR following 802.11 convention)
  A STA may not be woken up by a HDR WUR frame on its WUR channel, since it may experience worse channel conditions on its WUR channel (dictated by the AP during WUR negotiations) than on the WUR primary channels
    Both the WUR primary channel and the WUR channel are narrow band, and can be quite far away from each other
  Even when the STA can wake up by itself after some timeout interval, it has no way to let the AP know that it needs the LDR
    Will also cause significant delays, which may not be desirable according to the PAR [3]
In addition, if the channel condition warrants a HDR WUR transmission instead of LDR, the STA is not able to notify the AP either

## Slide 6: Proposal
Add Data Rate Preference in WUR Mode element when it was transmitted by the STA
This would allow the STA and the AP to consider data rates when negotiating other WUR parameters
The detailed proposal is included in 11-18/1925r2

## Slide 7: Conclusion
To resolve CIDs 915, 1100 and 1132, we propose to add Data Rate for WUR frames in the WUR Mode element when it is transmitted by the STA as a part of the WUR negotiation process
Such additions will allow STAs and the AP to remedy a few problems pointed out by CID 915, 1100 and 1132

## Slide 8
References
[1] IEEE 802.11-18/990r0, WUR Data Rates, July 2017
[2] IEEE P802.11ba Draft 1.0, Sept. 2018
[3] IEEE 802.11-16/1045r9, A PAR Proposal WUR SG, July 2016

## Slide 9: SP 1
Do you support the proposal resolutions for CID 915, 1100 and 1132 as proposed in 11-18/1925r2?
  Y/N/A: