## Slide 1: Error Correction Message
Date: 2018-11-12
Authors:

## Slide 2: Background
During the last meeting, the concept of a dedicated message carrying outer code parity bytes was presented
  IEEE802.11-18-1307
  Based on RS codes
Several comments have been raised at the meeting
  Parity message FCS failure assurance
  Overhead
  Complexity of RS code
November 2018

## Slide 3: Parity Message FCS Failure Assurance
The group has raised the concern that a parity message would be falsely accepted
Indeed, random data may extremely rarely pretend as FCS
A single byte can be added to assure FCS failure
  N = ~FCS(7:0), calculated on first N-3 bytes
Parity bytes
N
Data for FCS calculation
3 bytes
November 2018

## Slide 4: Overhead
802.11p doesn’t support frame aggregation
As such, PHY overhead has to be accounted for each parity packet
  TPreamble + TPHY header = 96uS
Sample calculation for 300 bytes packets
  Overhead + packet length + DIFS = 96uS + 408uS + 58uS = 562uS
November 2018
Code size | Parity bytes | Overhead [uS] | Percentage
(240, 224) | 32 | 96 + 48 + 16 = 160uS | 28%
(80, 64) | 64 | 96 + 96 + 16 = 208uS | 37%
(48, 32) | 112 | 96 + 160 + 16 = 272uS | 48%

## Slide 5: Overhead – Longer Term
Frame aggregation support is desired for supporting large infrastructure messages
  For example, CRL update
Frame aggregation isn’t a trivial addition to NGV
  Frame aggregation is negotiated per link: For NGV, pre-configuration would be needed
  Legacy units presence should be detected
  Activation conditions should be determined
Frame aggregation can significantly reduce parity packet overhead
Further study is needed
November 2018

## Slide 6: Complexity of RS Code
RS is a fairly common code
  Used in storage (compact disk, DVD), bar code, communication (xDSL, space) and more
Hardware implementations are well studied and widely available
  RS(255, 239) decoder size varies between 20K gates and 60K gates at >5Gbps throughput [1]
  Software implementations are possible for low-rate
  Legacy IEEE802.11p typically operates at 6Mbps
  Decoder has to operate only on failed packets
  1Mbps decoder was demonstrated on 16MHz ARM Cortex M3[2] (20 DMIPS). Far higher capacity is available in modern ECUs
November 2018

## Slide 7: References
[1] High-Speed Low-Complexity Reed-Solomon Decoder using Pipelined Berlekamp-Massey Algorithm and Its Folded Architecture, by Jeong-In Park et al
[2] Engineering a world-class Reed Solomon Algorithm by John Peter Norair
November 2018