## Slide 1: IoT Onboarding for 802.11
Date: 2018-11-11
Authors:

## Slide 2: Abstract
This document presents challenges around IoT onboarding for 802.11, and suggests a few areas of possible cooperation between 802.11 and IETF

## Slide 3: Basic onboarding is simple
Level 1: just need the SSID / PSK
Level 1: I accept any client with the right credentials
A headless IoT device needs to be told the SSID and its associated credentials
At this basic level (“level 1”), connectivity is the main objective
Jerome Henry, Cisco
Slide 3

## Slide 4: Basic Provisioning is simple
Level 1: just need the SSID / PSK
Level 1: I accept any client with the right credentials
OOB (NFC, BT etc.) or P2P Wi-Fi
SSID, credentials
Several solutions have been developed to solve this provisioning problem
This can be seen as an “individual scale” provisioning problem
Jerome Henry, Cisco
Slide 4

## Slide 5: Provisioning at Scale is not solved yet
“individual scale” provisioning solutions are challenged for “building scale” provisioning scenarios
Jerome Henry, Cisco
Slide 5

## Slide 6: Provisioning at Scale is not solved yet
Individual P2P communication and provisioning
(times n individual devices)
“Individual scale” provisioning techniques only imperfectly solve the “building scale” case
Potential excessive airtime consumption
“Regular” 802.11 process vs “IoT” process mismatches
Jerome Henry, Cisco
Slide 6

## Slide 7: Provisioning at Scale is not solved yet
Infrastructure needs to:
Advertise “IoT friendliness”
Automate provisioning
For “building scale” provisioning, the awaking IoThing needs to detect “IoT SSIDs” through which inline automated onboarding mechanism may exist
802.11u, 802.11aq can advertise IoT support
Temporal tunnel could be used for secure provisioning (e.g. RFC 8110, EAP-TEAP-BRSKI, others)
Jerome Henry, Cisco
Slide 7

## Slide 8: Conclusion 1
802.11 messaging could be augmented to facilitate IoT onboarding at scale
Specific “IoT onboarding” values in 802.11u/aq, in beacons and probe responses
Options could be set to signal secure provisioning (e.g. RFC 8110)
Jerome Henry, Cisco
Slide 8

## Slide 9: Increased IoThing side Requirements
SSID1
SSID2
Level 2: IoT may need to determine the “correct” SSID
In multi-tenant scenarios, the IoThing needs to know the ‘right’ SSID
“Honest neighbors” also should not want to onboard the Thing
This can be achieved when the infrastructure proves that it “knows” the IoThing
Jerome Henry, Cisco
Slide 9

## Slide 10: Increased IoThing side Requirements
SSID1
SSID2
Level 2: IoT may need to determine the “correct” SSID
Requesting IoThing may position an “is it you” question in probe/association request frames
IoThing needs to add an identifier:
MAC address / serial
Vendor identifier
Public key (BRSKI, PKI)
Probe + “is it you?”
Jerome Henry, Cisco
Slide 10

## Slide 11: IoThing Side Identifier Challenges
SSID1
SSID2
Level 2: IoT may need to determine the “correct” SSID
Some verticals will only need “what is that thing” value (object category)
Other verticals will need individual thing identification (thou shalst not onboard your neighbor lightbulb even if they use the same brand as yours)
Other verticals will mandate anti-spoofing provisions
Probe + “is it you?”
These different requirements are great area of potential cooperation with the IETF BRSKI* effort
*Bootstrapping Remote Secure Key Infrastructures
Level 2: AP only accepts the right client, with the right credentials
Jerome Henry, Cisco
Slide 11

## Slide 12: Infrastructure Side knowledge proof
SSID1
SSID2
Level 2: IoT may need to determine the “correct” SSID
The AP can return a sign, or proof of knowledge, confirming that the IoThing communicates with the ‘right’ SSID:
Complementary value (e.g. serial)
Bloom filter
BRSKI Voucher, PKI
Proof that I know you
Complementary value, bloom filter are for IoThing level 2 needs,
PKI, BRSKI can fulfill infrastructure level 2 needs
No proof
Level 2: AP only accepts the right client, with the right credentials
Jerome Henry, Cisco
Slide 12

## Slide 13: Infrastructure Side knowledge proof
SSID2
Level 2: IoT may need to determine the “correct” SSID
If the proof is given at the probe phase, the AP may need to go search for an answer
This process may require a comeback phase
Is it you?
Response + comeback
Response + proof
Is it you?
Backend proof collection
Jerome Henry, Cisco
Slide 13

## Slide 14: Conclusion 2
Specific “IoT identifiers” fields could be added to probe/association requests
Identifiers may be associated with exchange type (in following slides)
AP probe/association response could include comeback values, proof IE values
Jerome Henry, Cisco
Slide 14

## Slide 15: Level 3 for Secure networks
Level 3: prove that you are allowed to onboard me
Level 3: prove that you are allowed to onboard, and were not tampered with
AAA
Registrar
MASA
Manufacturer
For higher security networks, and/or critical objects, a third level of security may be needed
IoThing may need anti-evil twin protection
Network may need anti-tempering (open boxes) measures for new IoThings
Jerome Henry, Cisco
Slide 15

## Slide 16: Level 3 for Secure networks
Level 3: prove that you are allowed to onboard me
Level 3: prove that you are allowed to onboard, and were not tampered with
IoThing provides a public cert
Cert is verified by MASA/Manufacturer and approved
Proof of ownership is returned
AAA
Registrar
MASA
Manufacturer
BRSKI allows for such level 3 requirements on both sides
Jerome Henry, Cisco
Slide 16

## Slide 17: Approaches to onboarding
 | WPS | Simple Serial # | DPP | BRSKI w/ sales integration | BRSKI no sales integration | BRSKI with POP
Correct Network Selection | Yes | Yes | Yes | Yes | No | Yes
Onboard without Internet access | Yes | Yes | Yes | No | No | Yes
Proof of ownership | No | No | No | Yes | Yes** | Yes***
Supply chain security | No | No | No | Yes | Yes*** | Partial
Hands free* | No | No | No | Yes | Yes | No
Well secured | No | Maybe | Yes | Yes | Yes | Yes
Status | Here | Not planned | Std | Partially standardized | Partially standardized | Beginning
Key type | None | Ser # | Asym. | X.509 | X.509 | X.509 + private
Manufacturing complexity | Nvram | Serial# | Public Key + label/BOM | Cert+Back End Integration | Cert | Cert+label/BOM
*Hands free = no label or BOM integration
**Assumes protection of proof of ownership
***Assumes Internet access to enterprise AAA at some point
Jerome Henry, Cisco
Slide 17

## Slide 18: Conclusion 3
IoT onboarding presents new requirements for 802.11 exchanges
Collaboration with IETF may help better refine the associated needs for 802.11
New IEs in existing or new frames may be proposed to solve the various use cases

## Slide 19: References
BRSKI over IEEE 802.11, draft-friel-anima-brski-over-802dot11-00, https://datatracker.ietf.org/doc/draft-friel-anima-brski-over-802dot11/
Proof of Possession to Devices for Onboarding, draft-lear-brski-pop-00, https://datatracker.ietf.org/doc/draft-lear-brski-pop/
Worth noting: IETF opsawg and anima mailing lists, upcoming iot-onboarding@ietf.org mailing list