## Slide 1: Experimental Study of NOMA/SOMA in Wi-Fi
Date: 2019-03-11
Authors:
Name | Affiliation | Address | Phone | Email
Evgeny Khorov | IITP RAS |  |  | khorov@iitp.ru
Alexey Kureev | IITP RAS |  |  | 
Ilya Levitsky | IITP RAS |  |  | 

## Slide 2: Outline
Motivation
NOMA and SOMA brief introduction
KPIs
Theoretical results
Testbed description
November’18 results for NOMA (and short links)
February’19 results for SOMA (and long links)

## Slide 3: Motivation
In current networks, it is a typical situation when an AP serves several devices
located at different distances from the AP (thus having different channel attenuation)
having different traffic load.
In this case, Non-orthogonal multiple access (NOMA) can be a promising solution to increase spectrum efficiency.
This presentation considers theoretical and experimental results for DOWNLINK NOMA.
[1] proposes SOMA, which is actually a specific case of NOMA (having no SIC).
[1] doc.: IEEE 802.11-18/1462r0 SOMA for EHT

## Slide 4: Basic Idea of Downlink NOMA
AP
STA 2
STA 1
Power
To STA2
To STA1
P
STA2 decodes signal to STA1 and
performs Successive Interference
Cancelation (SIC)
Power
To STA2
To STA1
P
Traditional TDMA
NOMA
Different MCSs

## Slide 5: Signal Superposition
I
Q
TX side
RX side
STA2
STA1

## Slide 6: A possible transmission process
To STA2
To STA1
ACK
ACK
SIFS
SIFS
DIFS
AP
STA1
STA2

## Slide 7: KPI
Average throughput
  Can be increased if we block the client with the worst channel conditions
Geometric Mean Throughput
  KPI, widely used in cellular networks optimization as the target utility function:
  Equals zero, if any client is blocked
  Reaches the maximum value, if all the clients share the channel fairly (the same portion of channel time)
    This is called proportional fair resource allocation
    In a scenario with N client (saturated/full buffer/ traffic), each client obtains throughput where T is the maximal throughput if the client is alone.

## Slide 8: With SOMA, no SIC is needed
I
Q
STA 2
1011
1010
1001
1000
0001
0000
0011
0010
1110
1111
1100
1101
0100
0101
0110
0111
STA 1
AP
STA 2
STA 1
Gray-mapped superposed constellation
Can be considered as multiplexing + reflection of constellations
I
Q
BPSK
QPSK
Result
I
Q
I
Q

## Slide 9: Theoretical Results for 11a
PHY | 802.11a
SNR1 | 3 dB
SNR2 | 19 dB
MCS TDMA | 0 and 6
MCS NOMA | 0 and 4
 | 0.85
PHY | 802.11a
SNR1 | 3 dB
SNR2 | 19 dB
MCS TDMA | 0 and 6
MCS NOMA | 0 and 4
 | 0.85
Payload 1K/4K to align NOMA payloads
Comments
Round Robin 1K/1K – Equal throughput for both STAs
Round Robin 1K/4K – Throughput for STA1 goes down, Throughput for STA2 is 4 times higher than for STA1
Proportional fair 1K/4K – Equal channel time. Thrp for STA1 even lower, Thrp for STA 2 even higher -> Max Geomeric Mean Thrp
NOMA 1K/4K – 92% gain in thrp for STA1, small gain in thrp for STA2, Overall gain +43%

## Slide 10: Trade-off between throughputs for STA1 & STA2
=0.85
Mix of
NOMA (STA1 and STA2)
and CSMA (STA2)
max average/total thrp is not a good target
Proportional fair operation point
Round Robin
Operation point

## Slide 11: Testbed
AP (SDR)
STA2 (SDR)
As NOMA device
STA1 (Laptop)
legacy device
Can be used with legacy
off-the-shelf device!
Full description:
E. Khorov, A. Kureev, I. Levitsky. NOMA Testbed on Wi-Fi. //In Proc. of IEEE PIMRC, Bologna, Italy, 9-12 September 2018

## Slide 12: TX Implementation
Source
Data bytes to bits
Data bytes to bits
Encoder
Encoder
Modulator
Modulator
FFT
TX IQ Processing
to RF
Data 1
Data 2
+reflection

## Slide 13: RX Implementation
weak signal is isolated here
Always trying to separate SOMA packets
If no SOMA, the following check fails:
Reserved bit, tail bits, parity bits, N_SYM1 ≥ N_SYM2
(NO additional “SOMA indication bits” used!)
Demodulator & Decoder
Bits to
data bytes
Bits to
data bytes
Destination
Data 1
Data 2
Decoder
from RF
RX IQ
Processing
Demodulator
Decoder
Demodulaor

## Slide 14: Implementation
PHY RX State machine
for weak signal
L-SIG decoding
IDLE
Signal
detected
Reserved bit, tail bits, parity check passed & N_SYM1 ≥ N_SYM2
Done
False
Frame decoding
True
extracted
FCS check passed
False
True
Frame received
Done

## Slide 15: Minimal set of changes to the standard
Capabilities IE
  Indicator that a device is able to decode a NOMA/SOMA frame
  the other of NOMA/SOMA (optional)
The way how modulations are multiplexed
  For example, Gray-mapped superposed constellation

## Slide 16: November results

## Slide 17: Testbed. Experimental Setup
AP (SDR)
STA2 (SDR)
As NOMA device
STA1 (SDR)
As legacy device
A legacy device is replaced with SDR
to simplify gathering statistics
In November experiments, we located devices in the same room, reduced TX power and used 30dB attenuators to model different channel conditions

## Slide 18: Evaluation. Reference Throughputs
STA1 Payload ~ 1kB
STA2 Payload ~ 2kB
Different payloads are needed to make multiplexed frames of the same duration

## Slide 19: Testbed. Results
STA1 Payload ~ 1kB
STA2 Payload ~ 2kB
x1.5
NOMA
Link1 MCS1
Link2 MCS3
Obtained as the average throughput of STA 1 and STA2, when each of them has 50% of channel time

## Slide 20
=0.86
Mix of
NOMA (STA1 and STA2)
and CSMA (STA2)
Balance between throughput for STA1 & STA2

## Slide 21: February results (SOMA)
March 2019

## Slide 22: Testbed. Experimental Setup
AP (SDR)
STA2 (SDR)
As NOMA device
STA1 (SDR)
As legacy device
In February experiments, we located devices in separate rooms to provide different channel conditions for STA1 and STA2.

## Slide 23: Location of devices
(AP)
STA2
STA1
Now, the devices are located in different rooms and no attenuators are used

## Slide 24: Example of stats

## Slide 25: Testbed Results
PF
Link1 MCS1
Link2 MCS5
SOMA
Link1 MCS1
Link2 MCS3
x1.4
Twice lower because of fair sharing

## Slide 26: NOMA/SOMA Properties
Backward compatibility (STA 1 can be legacy)
  Even if not standardized, any vendor can use NOMA/SOMA for transmission between its own devices, and at the same time transmit data to other devices.
Almost double throughput for the STA with poor channel (in case of fare resource allocation) OR
Manifold gain in throughput of the nearest STA (STA 2) while providing guaranteed throughput for the far STA (STA 1)
If devices are close to each other higher modulations are possible.

## Slide 27: Straw Poll
Should NOMA/SOMA be considered as a possible solution for future 802.11 standards?
Yes, for EHT
Yes, for another project
No
Need more info
Abstain