## Slide 1: 6 GHz association discussion
Name | Affiliation | Address | Phone | Email
Laurent Cariou | Intel |  |  | Laurent.cariou@intel.com
Po-Kai Huang | Intel |  |  | 
Robert Stacey | Intel |  |  | 
Date: 2018-11-11

## Slide 2: Introduction
This document intends to clarify the proposal on association to a 6GHz AP that is part of a device with other Multiband Collocated APs

## Slide 3: Association to a 6GHz AP part of a Multi-band device
3 objectives:
  1) Define an AP mode with: Access to all STAs (that have credentials) to the 2.4/5GHz APs, access to collocated 6GHz AP controlled/restricted by the AP (limit the number of STAs based on several criterias is the best tool to ensure QoS, latency, …)
  2) Define a mode where pre-association traffic is reduced as much as possible at 6GHz (in-band)
    Useful for instance if we define a specific Low-Latency TSN operating mode in EHT/RTA
  3) Allow for full coexistence between 11ax and EHT/RTA, if a new greenfield mode is designed

## Slide 4: Association to a 6GHz AP part of a Multi-band device
One solution for 3 objectives:
  Signal a mode where STAs should perform association out-of-band through the collocated APs, and should not send pre-association traffic in-band (at 6GHz)
    OCT enables probes, association to 6GHz AP through over-the-air exchanges with Collocated AP
  Solves objective 1: STAs go to 2.4/5GHz AP, attempt to associate to 6GHz AP through OCT, AP denies or allows access. STA can always associate to 2.4/5GHz AP. AP sends BTM request to STA to move the STA to the 6GHz AP.
  Solves objective 2: STAs perform entire pre-association procedure with the 6GHz AP with over-the-air transmissions at 2.4/5GHz. STA only needs to measure RSSI with the 6GHz AP (FILS DF allows this with passive scanning in 15ms)
  Solves objective 3; STAs that don’t support the new mode of operation stay associated to the Multiband Collocated APs

## Slide 5: Association to a 6GHz AP part of a Multi-band device
1 field “pre-association mode” in Multiband Element, in Reduced Neighbor Report, in Neighbor Report and in FILS DF to indicate this mode:
  Bit set to 0 for in-band association
    Likely the main mode, especially in the short term
  Bit set to 1 for out-of-band association
Out-of-band association mode:
  STA should transmit pre-association frames only to the collocated 2.4/5GHz AP (using OCT, …)
    “Should” instead of “shall” here as there is a need for flexibility (as we discussed in September):
      STAs that don’t support OCT, if the AP still wants to allow them to access 6GHz
      STAs in fast roaming from another 6GHz AP from the same ESS should be able to do re-association in-band

## Slide 6: Association to a 6GHz AP part of a Multi-band device
Define a field “pre-association mode”:
  In Neighbor report: 1 reserved bit in BSSID Info Field
  In Multiband element: 1 reserved bit in Multiband control field
  In Reduced Neighbor Report: New field included in TBTT Info Field if the “Multiband Collocated” bit is set to 1 in TBTT Info Header
  In FILS DF: 1 reserved bit in FILS DF Control subfiled