## Slide 1: Overview of PHY Features for EHT
Date: 2019-01-14
Authors:
Name | Affiliation | Address | Phone | Email
Eunsung Park | LG Electronics | 19, Yangjae-daero 11gil, Seocho-gu, Seoul 137-130, Korea |  | esung.park@lge.com
Dongguk Lim |  |  |  | dongguk.lim@lge.com
Jinmin Kim |  |  |  | jinmin1230.kim@lge.com
Sunwoong Yun |  |  |  | sunwoong.yun@lge.com
Jeongki Kim |  |  |  | jeongki.kim@lge.com
Suhwook Kim |  |  |  | suhwook.kim@lge.com
Sungjin Park |  |  |  | allean.park@lge.com
Insun Jang |  |  |  | insun.jang@lge.com
Jinsoo Choi |  |  |  | js.choi@lge.com

## Slide 2: Introduction
In order to increase throughput and improve efficiency, the following candidates have been proposed as the potential technologies for EHT
  Wider bandwidth, i.e., 320MHz [1-4]
  Increased spatial streams, i.e., 16 SS [1-8]
  Multi-AP coordination [2][3][8-16]
  HARQ [3][4][9][17][18]
  6GHz operation / Multi-band operation [1-4][6][10][11][15][18-20]
In this contribution, we discuss PHY features to be considered for enabling potential EHT candidates
  We only focus on the first four candidates since the last one may be primarily related to the MAC feature

## Slide 3: PHY Features for 320MHz
Tone plan
EHT-STF / EHT-LTF sequence
Preamble puncturing
Phase rotation for legacy part
EHT-SIGB

## Slide 4: PHY Features for 320MHz – Tone Plan
In addition to the conventional bandwidths, i.e., 20 / 40 / 80 / 160 / 80+80 MHz, we can add various bandwidths to EHT using up to 320MHz
  Contiguous / non-contiguous 240MHz and 320MHz
  Those bandwidths can be formed only within a single band as well as across multiple bands
We need to develop tone plans appropriate for those new bandwidths
  Just reusing the conventional 80MHz tone plan, i.e., repeating the 80MHz tone plan similar to the 160MHz structure in 11ax is the most simple approach
  We can also design new tone plans
    Given the introduction of a 6GHz band where many contiguous 160MHz channels exist [1], there are more chances to use the contiguous 160MHz bandwidth especially with scheduled access in 6 GHz [18][20], and thus it can be adopted as a mandatory bandwidth and its tone plan can be also modified for throughput and efficiency enhancement
Pilot location and coefficients also need to be defined
  Pilot location can be determined based on the pilots of 26-tone RUs as in 11ax
  Pilot coefficients for each RU in wide bandwidths can be obtained by reusing or repeating conventional pilot coefficients

## Slide 5: PHY Features for 320MHz – EHT-STF / EHT-LTF Sequence
EHT-STF / LTF sequences suitable for wider bandwidth need to be designed
  Basically, those sequences can be optimized in terms of PAPR / correlation performance
Various numerologies, i.e., 1/2x STF and 1/2/4x LTF have been adopted in 11ax, and those may be sufficient for EHT as well
  We need to design EHT-STF / LTF sequences in these all numerologies
Design approach for EHT-STF / LTF sequences may depend on the tone plan
  If the tone plan is designed by repeating the 80MHz tone plan, sequences can be also constructed by repeating the 80MHz HE-STF / LTF sequence
    It may need an additional phase rotation per 40 / 80 / 160 MHz for PAPR reduction
  If new tone plans are adopted for a wider bandwidth, sequences also need to be designed accordingly
    Seed sequences can be used with an additional phase rotation

## Slide 6: PHY Features for 320MHz – Preamble Puncturing
To enhance the efficiency of frequency utilization, 11ax adopted preamble puncturing which nulls secondary channels based on the 20MHz CCA
Since the preamble puncturing is more beneficial to the wide bandwidth case in terms of frequency utilization, EHT seems to necessarily use it
Preamble puncturing can be applied as in 11ax, i.e., based on 20MHz CCA, but it will introduce numerous cases especially in the 320MHz transmission which results in a severe signaling overhead in EHT-SIGA
Thus, larger granularity based CCA, i.e., 40 / 80 MHz based preamble puncturing can be considered in the wide bandwidth transmission
  Trade-off between performance and overhead should be addressed

## Slide 7: PHY Features for 320MHz – Phase Rotation for Legacy Part (1/2)
Conventional 802.11 systems apply phase rotation to the legacy part and EHT can also apply it in order to reduce PAPR
EHT can just reuse the 11ax phase rotation up to 160MHz and additionally design new phase rotation for 240 / 320 MHz
By taking into account the preamble puncturing, we can design a new phase rotation in each bandwidth
  11ax just reuses the 11ac phase rotation so it may not be optimal in terms of the PAPR when the preamble puncturing is applied
In addition, the RF capability, i.e., the maximum bandwidth that RF can transmit can be also considered
  For example, when transmitting contiguous 160MHz PPDU, the transmitter can either use one RF which can cover 160MHz transmission or two RFs where each RF can only deal with 80MHz transmission at the most
    In this case, the phase rotation for 160MHz can be designed by considering the PAPR of the full bandwidth as well as two 80MHz bandwidths
 Note that preamble puncturing and RF capability can be also considered for EHT-STF/LTF sequence design

## Slide 8: PHY Features for 320MHz – Phase Rotation for Legacy Part (2/2)
CDF of the PAPR for the L-LTF with preamble puncturing in 80MHz and 160MHz

## Slide 9: PHY Features for 320MHz – EHT-SIGB Signaling
In 11ax, HE-SIGB has duplicated structures, 1/2 for 40MHz, 1/2/1/2 for 80MHz and 1/2/1/2/1/2/1/2 for 160MHz where 1/2 means 20MHz content channel 1 and 20MHz content channel 2
Just applying this structure to EHT-SIGB in a wide bandwidth transmission can lead to a large overhead, and thus modified SIGB structures can be considered in EHT for overhead reduction
  For example, duplicated structure based on 80MHz with a minimum content channel granularity of 20MHz/40MHz can be considered in wide bandwidths
    These modified structures need to be considered in conjunction with the preamble puncturing design
20MHz
240MHz / 320MHz
40MHz
…
…

## Slide 10: PHY Features for 16 SS
Feedback overhead reduction
LTF overhead reduction
P-matrix
CSD

## Slide 11: PHY Features for 16 SS – Feedback Overhead Reduction
If EHT allows MIMO transmission which transmits up to 16 streams in a particular RU, it incurs too much increase in feedback overhead
  Along with 16 SS, using 320MHz bandwidth also requires a lot of feedback overhead
A decent feedback method can be applied for overhead reduction
  Differential feedback, implicit feedback [7] and dimension reduction method [8] can be promising candidates
  Their performance and overhead should be compared

## Slide 12: PHY Features for 16 SS – EHT-LTF Overhead Reduction
In the 16 SS transmission, EHT-LTF can be 16 symbols when the EHT-LTF is constructed by the conventional way
For overhead reduction, we can modify the LTF structure and its sequence
  Orthogonal LTF in the frequency domain can be one possible solution
    For an example of the two-stream case, only one EHT-LTF symbol is needed where odd and even subcarriers are allocated to different streams and interpolation / extrapolation can be additionally used for channel estimation
    In terms of the orthogonal pattern, performance and overhead should be evaluated
  Time domain approach can be also considered

## Slide 13: PHY Features for 16 SS – P-Matrix / CSD
We need to design P-matrix and CSD table which can cover 9 to 16 SS
For the P-matrix design, DFT based approach and Hadamard matrix can be utilized as in the conventional Wi-Fi
  10x10 / 12x12 / 14x14 / 16x16 may need to be designed at least
  For 10x10 / 14x14, DFT based approach can be applied
  For 12x12 / 16x16, Hadamard matrix can be used
For the CSD table, legacy and EHT CSD tables are required to design
  By taking into account the practical sampling period, we can define a minimum CSD value and possible candidates of CSD values
  For a simple implementation, a nested structure can be used where CSD values for X+1 SS is constructed by adding one value to CSD values for X SS
    AGC error, power bumping, performance and so on should be evaluated
  Depending on the channel condition, the optimized CSD values may be different but it is advisable that EHT has a unified CSD table as in the conventional Wi-Fi

## Slide 14: PHY Features for Multi-AP Coordination
Impairments and requirements
AP selection and sounding procedure

## Slide 15: PHY Features for Multi-AP Coordination –Impairments and Requirements
We focus on the joint transmission, i.e., distributed (MU) MIMO where channel information and data sharing is required among APs
  Although the joint transmission is a quite complex method, it can effectively achieve the objectives of EHT, i.e., enhancing the throughput and efficiency compared to other coordination methods such as Multi-AP scheduling, interference nulling, dynamic AP selection, etc.
For a reliable performance of the joint transmission, there are several factors to be considered such as sampling frequency offset, carrier frequency offset, phase drift, transmission timing and power imbalance
Under these impairments, performance should be evaluated and consequently the hardware requirement needs to be specified
Also, in order to reduce implementation complexity, we can consider restricting the maximum number of APs participating in the joint transmission

## Slide 16: PHY Features for Multi-AP Coordination –AP Selection and Sounding Procedure
To enable the joint transmission, AP selection and sounding procedure need to be designed
AP selection can simplify the joint transmission procedure related to feedback and sharing while maintaining a comparable performance
  For the AP selection, appropriate selection procedures and signaling methods are required
One possible sounding procedure is proposed in [21]
  There are one master AP and several slave APs which participate in the joint transmission
  Master AP manages the joint transmission
  Channel reciprocity can be used for precoding matrix computation in the joint transmission
  Feedback overhead can be reduced considerably by using the channel reciprocity, but its feasibility should be identified

## Slide 17: Additional PHY Features
PPDU format
Higher MCS
HARQ

## Slide 18: Additional PHY Features – PPDU Format
Like as the PPDU of the conventional Wi-Fi, EHT may also use a legacy preamble for backward compatibility
Even in a 6GHz band where only non-HT / HEW / EHT PPDUs exist, the same EHT PPDU format can be used for a unified transmit and receive operation in all bands
A new packet classification method is required
  It seems hard to use a constellation based method which is applied to the conventional Wi-Fi classification
  Similar to the 11ba approach, we can consider RL-SIG modification as one possible solution
  Alternatively or additionally, PHY header such as L-SIG / EHT-SIG can contain a packet classification information

## Slide 19: Additional PHY Features – Higher MCS
A new modulation level such as 4096 QAM can be adopted
  It can increase the maximum throughput about 20% over 11ax
Due to the hardware complexity, its application can be restricted
  About 6dB lower EVM than 1024 QAM is required
  It can be applied only to a beamforming case to alleviate the EVM requirement [2]
Non-uniform constellation can be considered for a better performance
  Even if the receiver complexity is high, 11ay already adopted non-uniform constellation for 64 QAM which provides gain up to 2dB compared to the normal 64 QAM constellation [22]
  According to the channel condition and coding rate, optimal constellations can vary but a unified solution is required for simple implementation

## Slide 20: Additional PHY Features – HARQ
HARQ can enhance not only link quality but also BSS average throughput by applying an aggressive MCS and PHY combining [18]
Possible procedure
  When a PHY header decoding succeeds whereas a data part CRC fails, retransmission can occur after a NACK frame and then original and retransmitted data can be combined
For an efficient HARQ support, a decent PPDU design and a proper ACK / NACK feedback mechanism are required
  PPDU including multiple HARQ data and a short PHY feedback method such as HE TB NDP Feedback can be possible solutions, respectively

## Slide 21: Summary
By categorizing into four parts as below, we have looked into several PHY features which need to be designed to achieve the EHT objectives
  Wider bandwidth, i.e., 320MHz
  Increased spatial streams, i.e., 16 SS
  Multi-AP coordination
  Additional features : PPDU format / Higher MCS / HARQ

## Slide 22: References
[1] 802.11-18/0789r6 Extreme Throughput (XT) 802.11
[2] 802.11-18/1461r1 Discussions on the PHY features for EHT
[3] 802.11-18/1547r0 Technology Features for 802.11 EHT
[4] 802.11-18/1549r0 Recommended Direction for EHT
[5] 802.11-18/0818r3 16 Spatial Stream Support in Next Generation WLAN
[6] 802.11-18/1184r1 Follow up Discussions on Throughput Enhancement
[7] 802.11-18/1191r0 MU Sounding Improvements
[8] 802.11-18/1575r0 Further Study on Potential EHT Features
[9] 802.11-18/1116r0 Distributed MU-MIMO and HARQ Support for EHT
[10] 802.11-18/1155r1 Multi-AP Enhancement and Multi-Band Operations
[11] 802.11-18/1161r0 EHT Technology Candidate Discussions
[12] 802.11-18/1439r0 Constrained Distributed MU-MIMO
[13] 802.11-18/1509r0 Discussions on Multi-AP Coordination
[14] 802.11-18/1510r1 AP Coordinated Beamforming for EHT
[15] 802.11-18/1533r0 View on EHT Candidate Features
[16] 802.11-18/1576r1 Considerations on AP Coordination
[17] 802.11-18/1587r1 HARQ for EHT
[18] 802.11-18/1171r0 View on EHT Objectives and Technologies
[19] 802.11-18/857r0 Beyond 802.11ax – Throughput Enhancement Utilizing Multi-bands across 2.4/5/6 GHz Bands
[20] 802.11-18/1525r1 EHT features for Multi-Band Operation
[21] 802.11-18/1982r0 Consideration on Multi-AP Coordination for EHT
[22] 802.11-16/0072r0 Performance of Non-Uniform Constellations in Presence of Phase Noise