## Slide 1: NGV Indication within Legacy Broadcast PPDU
Date: 2018-11-12
Authors:

## Slide 2: Recap: NGV and 11P Device Coexistence
In the future, 11p devices and NGV devices need to coexist with each other.
Once a legacy 11p device is detected, 11p PPDU will be used for broadcast frame transmission.
  The recipient will broadcast frame in legacy PPDU which may disable NGV PPDU usage.
There is a need to announce NGV source in 11p PPDU:
  A NGV STA shouldn’t think that a the source STA of a 11p PPDU is 11p STA. Otherwise the chance to transmit NGV PPDUs become lower.

## Slide 3: Identification of Source Device Type of 11p PPDU
Duration based indication:
  In Duration field of MAC header, a specific addition, e.g. ½ slot time, slot time, or SIFS, to the actual duration value is used to identify that the frame in 11p PPDU is from a NGV device.
Broadcast frame in 11p PPDU
11p STA1
11p STA1
NGV STA2
NGV STA2
Broadcast frame in 11p PPDU
NVG STA2
Duration field with value 0
Duration field with value ½ slot time
A 11p neighbor exists
Broadcast frame in NGV PPDU
NVG STA3
Only NGV neighbor exists
Duration
Only NGV neighbor exists
11p STA1
NVG STA2
NVG STA3
Duration field with value 0
Duration field with value ½ slot time
A 11p neighbor exists
Only NGV neighbor exists
½ slot

## Slide 4: Identification of Source Device Type of 11p PPDU
Duration based indication:
  In Duration field of MAC header, a specific addition, e.g. ½ slot time, slot time, or SIFS, to the actual duration value is used to identify that the frame in 11p PPDU is from a NGV device.
Broadcast frame in 11p PPDU
11p STA1
11p STA1
NGV STA2
NGV STA2
Unicast frame in 11p PPDU to STA1
NVG STA2
Duration field with value 0
Duration field with value ½ slot time + SIFS + Ack PPDU Tx time
A 11p neighbor exists
Broadcast frame in NGV PPDU
NVG STA3
Only NGV neighbor exists
Duration
Ack
11p STA1
NVG STA2
Duration field with value 0
Duration field with value ½ slot time + SIFS + Ack PPDU Tx time
A 11p neighbor exists
NVG STA3
Only NGV neighbor exists
Duration
1 slot time

## Slide 5: Identification of Source Device Type of 11p PPDU
Frame Control or Sequence Control based indication:
  A specific field in Frame Control of MAC header or a specific value in Sequence Control is used to identify that the frame in 11p PPDU is from a NGV device.
Broadcast frame in 11p PPDU
11p STA1
11p STA1
NGV STA2
NGV STA2
Broadcast frame in 11p PPDU
NVG STA2
No specific Sequence Control value
A 11p neighbor exists
Broadcast frame in NGV PPDU
NVG STA3
Only NGV neighbor exists
Specific Sequence Control value
11p STA1
NVG STA2
No specific Sequence Control value
A 11p neighbor exists
NVG STA3
Only NGV neighbor exists
Specific Sequence Control value

## Slide 6: Identification of Source Device Type of 11p PPDU
Frame content based indication:
  A specific field is added to the frame body by higher layer, e.g. DSRC protocol, of a NGV device to identify that the frame in 11p PPDU is from a NGV device.
Broadcast frame in 11p PPDU
11p STA1
11p STA1
NGV STA2
NGV STA2
Broadcast frame in 11p PPDU
NVG STA2
No specific field in frame body
A 11p neighbor exists
Broadcast frame in NGV PPDU
NVG STA3
Only NGV neighbor exists
Specific field in frame body
11p STA1
NVG STA2
No specific field in frame body
A 11p neighbor exists
NVG STA3
Only NGV neighbor exists
Specific field in frame body

## Slide 7: Identification of Source Device Type of 11p PPDU
11p PPDU + NGV PPDU method:
  A NGV STA transmits a frame in 11p PPDU and NGV PPDU with SIFS between the two PPDUs.
Broadcast frame in 11p PPDU
11p STA1
11p STA1
NGV STA2
NGV STA2
Broadcast frame in 11p PPDU
NVG STA2
A 11p neighbor exists
Broadcast frame in NGV PPDU
NVG STA3
Only NGV neighbor exists
Broadcast frame in NGV PPDU
PE method (PHY extension):
  A NGV STA transmit a frame in 11p PPDU with an immediate PHY extension of fixed pattern and length.
Broadcast TA method:
  A NGV STA transmits a frame in 11p PPDU where the unicast/broadcast bit in TA is set to broadcast.
Scramble initial value method:
  A NGV STA transmits a frame in 11p PPDU with a specific scramble initial value.
It can also be a MPDU Delimiter, a frame with the shortest length, NGV NDP fame etc.
11p STA1
NVG STA2
A 11p neighbor exists
NVG STA3
Only NGV neighbor exists
It can also be a MPDU Delimiter, a frame with the shortest length, NGV NDP fame etc.

## Slide 8: Broadcast Frame Transmission
Adaptive broadcast frame through NGV PPDU.
  Transmitting broadcast frame through .11p PPDU once a neighbor .11p device is detected. Otherwise transmitting broadcast frame through NGV PPDU
    The receiver of broadcast frame in 11p PPDU should be able to detect whether the frame is from 11p device or NGV device.
Deciding whether the broadcast frames are allowed in NGV PPDU per the channel being used.
Deciding whether the broadcast frames are allowed in NGV PPDU per the type/subtype/Category, e.g.
  The broadcast frames for the new features that are not supported by .11p device, e.g. NDP ranging feedback for snoop-based ranging.
Disallowing the broadcast frame through NGV PPDU.
  It is not a good idea especially when a feature being only support by NGV devices requires broadcast frame support.

## Slide 9: Timeout of Neighbor 11p STA
Each time a NGV STA receives a 11p frame from a 11p STA, 11p neighbor timer is set to a threshold, e.g. 1000ms, and then counts down
  If no 11p frame from 11p neighbor is received until the timer becomes 0, the NGV STA assume no neighbor 11p STAs exist. It can transmit broadcast frames in NGV PPDUs.