## Slide 1: Consideration on multi-AP coordination for EHT
Date: 2019-01-09
Authors:
Name | Affiliations | Address | Email
Kiseon Ryu | LG Electronics | 10225 Willow Creek Rd, San Diego, CA, USA | kiseon.ryu@lge.com
Sanggook Kim | LG Electronics |  | sanggook.kim@lge.com
Sungjin Park | LG Electronics | LG Seocho R&D Campus, Korea | allean.park@lge.com
Eunsung Park | LG Electronics |  | esung.park@lge.com
Jeongki Kim | LG Electronics |  | jeongki.kim@lge.com
Jinsoo Choi | LG Electronics |  | js.choi@lge.com
HanGyu Cho | LG Electronics |  | hg.cho@lge.com

## Slide 2: Introduction
In July and September IEEE meeting, multi-AP coordination was proposed in several contributions for EHT such as [1] to [12]
Multi-AP coordination can be considered as an EHT key feature to improve what we already have
  Mesh wifi devices are already in the market
  Wi-Fi Alliance Multi-AP program is based on the multiple AP network over the wireless backhaul.
In this contribution, we discuss the high level issues to be considered for multi-AP coordination

## Slide 3: Definition of New Type of Device
New type of devices for joint transmission was mentioned in [5]
Master AP (M-AP)
  Being a role of the AP coordinator
Slave AP (S-AP)
  Participating in the joint transmission coordinated by Master AP
  May have functionalities of both STA and AP
M-AP
S-AP1
Coordination
Coordination
S-AP2
STA
Joint transmission
Joint transmission

## Slide 4: Categorization of Multi-AP Coordination
At first, we can categorize the multi-AP coordination features as the following high levels
  Level 1: Multi-AP coordinated scheduling/beamforming
    Required features: Multi-AP sounding and feedback
  Level 2: Dynamic AP selection
    Required features: Multi-AP channel measurement and Feedback mechanism for best AP selection, STA context and data sharing among multi-APs
  Level 3: Joint Transmission (JTX)
    Required features: Multi-AP sounding, Context sharing, Synch among multi-APs, Data and control info. sharing among multi-APs
At second, we can further categorize it according to resource utilization for multiple AP transmission
  Same or different freq. resources (RU or unit of 20MHz channel)
  Same or different time
Tech. Cat. | Time | AP1 Tx | AP2 Tx | Gain
C-BF/C-SCH | T1 | RU1 (STA1) | RU1 or RU 2 (STA2) | Interference nulling, Freq. re-use
D-AP selection | T1 | RU (STA1) |  | Best link selection
 | T2 |  | RU (STA1) | 
JTX (D-MIMO) | T1 | RU1 (STA1) | RU1 (STA1) | Spatial diversity, SNR gain

## Slide 5: Possible Scenarios for Joint Transmission (JTX)
Scenario #1 Scenario #2
For both cases, data sharing among multiple APs is performed at T1 and JTX is performed at T2
  Master AP
    AP1 for both scenarios
  APs participating in JTX
    AP2 and AP3(scenario1), AP1 and AP2(scenario2)
In case of scenario2, another approach is also possible as follows:
  AP1 sends a data frame to both AP2 and STA at T1
  AP2 sends the data frame to STA at T2
  STA gets the time diversity or combining gain through the data frames received from AP1 and AP2 at the different time
AP1
AP2
Data frame
Data frame
AP3
STA
Data frame
Data frame
at T1
at T2
AP1
AP2
Data frame at T1
Data frame at T2
STA
Data frame
at T2

## Slide 6: Selection of APs and Sounding for JTX
Possible procedure
  Master AP transmits a JTX NDPA frame
    Inform slave APs that JTX will be performed to STA1, and request the slave AP1 associated with STA1 to transmit a Trigger frame which solicits STA’s NDP frame
    Request slave APs to feed back the channel state information after receiving NDP from STA1 so that the master AP selects the slave APs which will participate in JTX
  Slave AP1 transmits a Trigger frame which solicits STA’s NDP frame (Note. This can be omitted if a STA can receive the JTX NDPA frame directly from the master AP)
  STA transmits an NDP frame
  Slave APs estimate the channel state and feed it back to the master AP
    UL MU procedure can be used to transmit the feedback from multiple slave APs
    Channel reciprocity can be used to compute the precoding matrix in the joint transmission
  Master AP selects slave APs and share the channel state information / data
  JTX is performed (refer to the next slide)
M-AP
S-AP1
S-AP2
S-AP3
NDP Trigger frame
JTX BFRP Trigger frame
JTX NDPA frame
NDP
STA
CQI & BF Report frame

## Slide 7: Multi-AP Coordinated JTX
Joint transmission from multiple APs should be controlled and initiated by the master AP
Master AP can be a TXOP holder for joint transmission
  Similar procedure to the existing mechanism (e.g., NDP sounding procedure and RD Protocol) can be defined.
    Joint Transmission Announcement (like NDPA) sent by Master AP
      It may be the first frame of the TXOP for joint transmission
      Identifying slave AP(s) participating in joint transmission
    Data frame (like NDP) sent by master AP
      Data for joint transmission is shared to slave AP(s)
    Joint Transmission Trigger frame (like BFRP Trigger) sent by Master AP
      Scheduling and other control information for joint transmission can be included
      Synch. among slave APs for joint transmission may be carried out
    Joint transmission (like RD protocol) by slave AP(s) (and master AP)
      Joint transmission of data frame to non-AP STA(s) by multiple APs
M-AP
S-AP1
S-AP2
STA
Data frame
JT Trigger frame
Data frame using joint transmission
JTA frame

## Slide 8: Issues for further consideration
How to enable the joint transmission
  Capability based enabling such features as NDP Feedback Report, Punctured Preamble, ER SU PPDU in 11ax
  Enabling the mode of operation such as the OM Control field indication for Rx/Tx operating mode parameter change
  Moreover, both of them are used to enable the multi-AP JTX
How to share the data for joint transmission among APs (in case of wireless backhaul)
  Master AP generating and sharing the jointly transmitted MPDUs
    Need to define the rule to set the fields with the dynamic values in the MPDUs (e.g., Duration/ID field set to a specific value like 32 768)
  Master AP sharing MSDUs along with the STA’s context (e.g., security keys) and slave APs generating jointly transmitted MPDUs with the same contents in them
How to access the channel for joint transmission among APs
  Can only be triggered by a master AP, and no CS may be considered by slave APs
  If the virtual CS is considered and the joint transmission is triggered, slave APs can consider the non-zero NAV values except the NAV set by the frame received from the master AP or any slave AP belonging to the same group for joint transmission

## Slide 9: Summary
Multi-AP coordination feature can be categorized with 3 levels.
  Level 1: Coordinated Scheduling and Beamforming
  Level 2: Dynamic AP Selection
  Level 3: Joint Transmission
New type of device such as the master AP and the slave AP can be defined.
Through the master AP coordination, only slave APs or master and slave APs can participate in joint transmission.
The Multi-AP sounding and the joint transmission procedure can be defined

## Slide 10: References
[1] Jianhan Liu, “Multi-AP Enhancement and Multi-Band Operations’, IEEE 802.11-18/1155
[2] Hongyuan Zhang, “EHT technology candidate discussions”, IEEE 802.11-18/1161
[3] Ron Porat, “Multi-AP and HARQ for EHT”, IEEE 802.11-18/1116
[4] David Yang, “Discussion on EHT Study Group Formation”, IEEE 802.11-18/1180
[5] Ron Porat, “Distributed MU-MIMO”, IEEE 802.11-18/1439
[6] Jianhan Liu, “Features for Multi-AP Coordination”, IEEE 802.11-18/1509
[7] Yusuke Tanaka, “View on EHT Candidate Features”, IEEE 802.11-18/1533
[8] Kome Oteri, “Technology Features for 802.11 EHT”, IEEE 802.11-18/1547
[9] Tianyu Wu, “Further study on potential features”, IEEE 802.11-18/1575
[10] Hongyuan Zhang, “AP Coordinated beamforming for EHT”, IEEE 802.11-18/1510
[11] Xiaogang Chen, “Discussions on the PHY Features for EHT”, IEEE 802.11-18/1461
[12] Yang Bo, “Considerations on AP Coordination”, IEEE 802.11-18/1576