## Slide 1: EVM Requirement Negotiation for NDP Ranging Packets
Date: 2018-11-11
Authors:

## Slide 2: Problem Statement
NDPs (null-data-packet) are used as the measurement frames for the TB and NTB ranging modes in 802.11az_D0.5 [1].
There are no EVM requirements for NDP in 802.11az_D0.5 [1] and 802.11-2016 [2].
  NDP is a frame that has only the PHY header but does not contain the MAC data payload.
  The EVM requirement specified in [2] is a fixed value for a particular packet data rate, and is not negotiable.
However, ranging accuracy is tightly coupled with EVM.

## Slide 3: Ranging Accuracy vs. EVM
The result of our investigation:
  The ToA accuracy in a multipath environment is affected by the EVM level of the transmitted measurement frames.
  Ranging error decreases as the increasing EVM level (in absolute value).
  Advanced algorithms benefit from from EVM as much as -40dB

## Slide 4: Low/High EVM Trade off
A higher EVM level improves ranging accuracy but usually requires the transmitter to reduce its output power and therefore limits the distance at which a ranging session can be performed.
A lower EVM level degrades accuracy but enables the ranging operation at a further distance.

## Slide 5: Proposal
In order to achieve a certain desired accuracy for a particular ranging session, an iSTA transmits its required/desired EVM level that rSTA should meet when transmitting the NDP measurement frames to the iSTA.
When the iSTA transmits its required/desired EVM level, the iSTA also:
  Option 1: commits to meet such an EVM level in its own transmission to the rSTA.
  Option 2: indicates the actual EVM level of the transmission from iSTA to the rSTA.

## Slide 6: Proposal – cont’d
The iSTA includes its desired/required EVM level in the Ranging Parameter field of the Ranging Parameter element in the Initial FTM Request frame
The rSTA responds by including its actual EVM level, which is a level closest to what’s requested by the iSTA and is supported by the rSTA, in the Ranging Parameter field of the Ranging Parameter element in the Initial FTM frame.
The iSTA decides whether to continue or terminate the ranging session accordingly.
Status Indication
Value
Secure LTF Required
Secure LTF Support
ISTA2RSTA LMR Feedback
Format and Bandwidth
Number of Antennas
iSTA’s EVM requirement / rSTA’s acutal EVM
Bits:
2
5
1
1
1
6
8
6
Figure xxx: Ranging Parameters field format
New

## Slide 7: Proposal – cont’d
The method that the iSTA uses to decide its EVM requirement is implementation specific.
The iSTA may take the following information into account in generating the requirement:
  The use case for the ranging session
  The SNR at the iSTA
  The internal algorithm used by the iSTA to estimate the ToA of the NDPs
  Other internal factors.
The method that the rSTA uses to decide its actual EVM level is implementation specific.

## Slide 8: Proposal – Measurement Method
A method for measuring EVM on NDPs needs to be defined.
Suggested method:
  NDP EVM can be tested using a standard VSA (vector signal analyzer) device by measuring the L-Sig symbol’s EVM on each of the Tx antennas.
  We verified this option exists in Agilent VSA device.

## Slide 9: Summary
A mechanism for the iSTA and rSTA to negotiate the EVM requirement on the NDP transmission is proposed.
The proposed method enables the selection of a suitable EVM level for a specific ranging session that has a desired ranging accuracy and operating distance.

## Slide 10: Straw Poll 1
Do you support to add a method to negotiate the EVM requirement on the NDP transmission within a ranging session?
Results: Yes: No: Abstain:

## Slide 11: Straw Poll 2
Do you support to include the EVM requirement by iSTA and the actual EVM level of the rSTA using the method described on slide 6?
Results: Yes: No: Abstain:

## Slide 12: References
[1] IEEE Draft P802.11az_D0.5 - Draft Standard for Information Technology - Telecommunications and Information Exchange Between Systems Local and Metropolitan Area Networks - Specific Requirements Part 11: Wireless LAN Medium Access Control (MAC) and Physical Layer (PHY) Specifications - Amendment 8: Enhancements for Positioning
[2] IEEE Std 802.11-2016 (Revision of IEEE Std 802.11-2012) - IEEE Standard for Information technology—Telecommunications and information exchange between systems Local and metropolitan area networks—Specific requirements - Part 11: Wireless LAN Medium Access Control (MAC) and Physical Layer (PHY) Specifications