## Slide 1: NTB Ranging Flow Control and Power Save
Date: 2018-11-11
Authors:

## Slide 2: Related CIDs
This document relates to the following CIDs:
  495, 496

## Slide 3: Proposal Overview
For NTB ranging, we propose to use the following parameters to control the timing when the iSTA can initiate the next round of measurement.
  MinTimeBetweenMeasurement_rSTA (MinTBM_rSTA):
    rSTA’s announcement of the minimal time interval between two consecutive measurements rounds
  MaxTimeBetweenMeasurement_rSTA(MaxTBM_rSTA):
    rSTA’s announcement of the maximal time interval between two consecutive measurement rounds
  MinTimeBetweenMeasurement_iSTA (MinTBM_iSTA):
    iSTA’s announcement of the minimal time interval between two consecutive measurement rounds
  MaxTimeBetweenMeasurement_iSTA(MaxTBM_iSTA):
    iSTA’s announcement of the maximal time interval between two consecutive measurement rounds

## Slide 4: Proposal Benefits
The method in 802.11az_D0.5 uses the following parameters, all announced by the rSTA only, to control the NTB ranging timing:
  MinToAReady, defined as rSTA’s timestamp processing time
  MaxToaAvailable, defined as rSTA’s timestamp storage time
  MinTimeBetweenMeasurements
Relative to the existing method, the proposal:
  Enables power save at the rSTA;
  Taking the iSTA’s timestamp processing time and storage time and possibly other internal considerations into account
  Taking rSTA’s other internal considerations, in addition to timestamp processing and storage time, into account.

## Slide 5: Existing Problem Description
Parameter setting rules in [1] for immediate rSTA-to-iSTA LMR:
  MinToAReady = 0
  MinTimeBetweenMeasurement <= MaxToAAvailable
However, MaxToAAvailable is an ill defined concept for immediate rSTA-to-iSTA report
  The timing of the measurement round N does not depend on how long the rSTA keeps the results of round (N-1)
Fig. 1 VHTz with immediate report in [1]

## Slide 6: Existing Problem Description – cont’d
Parameter setting rules in [1] for delayed rSTA-to-iSTA LMR:
  MaxToAAvailable > MinToAReady > 0
  MinTimeBetweenMeasurement = MinToAReady
As a result, the rSTA must remain awake during the “LMR Availability”
  Ex: For MinToAReady = 25.5ms, MaxToAAvailable = 256ms, the rSTA needs to remain awake for (256 - 25.5 = 230.5)ms,
Fig. 2 VHTz with delayed report in [1]

## Slide 7: Proposal Description
During Negotiation, the iSTA announces
  MinTBM_iSTA
  MaxTBM_iSTA
  Both parameters are mandatory for delayed rSTA-to-iSTA LMR, optional for immediate rSTA-to-iSTA LMR
In response, the rSTA announces:
  MinTBM_rSTA
  MaxTBM_rSTA
If negotiation successful, Min/Max_TBM_rSTA are used for NTB ranging.
  When the rSTA cannot accommodate the Min/Max_TBM_iSTA, or the iSTA rejects Min/Max_TBM_rSTA, the negotiation fails; re-negotiation if desired.

## Slide 8: Proposal Description – cont’d
In selecting Min/Max_TBM_iSTA, the iSTA considers:
  iSTA’s need to go to power save,
  iSTA’s timestamp processing time and the timestamp storage time, for delayed rSTA-to-iSTA LMR,
  iSTA’s other internal considerations.
In selecting Min/Max_TBM_rSTA, the rSTA considers:
  rSTA’s timestamp processing time and the timestamp storage time,
  rSTA’s need to go to power save,
  rSTA’s other internal considerations,
  MinTBM_iSTA, if any.
  MaxTBM_iSTA, if any.

## Slide 9: Proposal Description – Cont’d
The proposed method solve all cases listed below:
The proposal described in the subsequent slides assumes the same reference start point for the time intervals of Min/Max_TBM_rSTA/iSTA,
  If different start points are specified for these intervals, the rules for the relationships among these intervals need to be adjusted accordingly, to achieve the same effect.
 | No iSTA-to-rSTA LMR | Immediate iSTA-to-rSTA LMR | Delayed iSTA-to-rSTA LMR
Immediate rSTA-to-iSTA LMR | Case 1 | Case 2 | Case 3
Delayed rSTA-to-iSTA LMR | Case 4 | Case 5 | Case 6

## Slide 10: Solution Detail for Case 1 and Case 2 (1)
The iSTA does not announce Min/Max_
TBM_iSTA.
Proposed parameter setting rules for rSTA:
  MinTBM_rSTA < MaxTBM_rSTA
Resulting behavior:
  The rSTA can go into power save after the completion of the measurement, and remain asleep for the duration of the MinTBM_rSTA time interval.
  The iSTA can go into power save after the completion of the measurement, and wakes up to initiate the next round of measurement taking into account of the parameters announced by the rSTA.
 | No iSTA-to-rSTA LMR | Immediate iSTA-to-rSTA LMR | Delayed iSTA-to-rSTA LMR
Immediate rSTA-to-iSTA LMR | Case 1 | Case 2 | Case 3
Delayed rSTA-to-iSTA LMR | Case 4 | Case 5 | Case 6
Fig. 3 Proposal - case 1 and case 2
(without iSTA’s parameter announcement)

## Slide 11: Solution Detail for Case 1 and Case 2 (2)
Optionally, the iSTA announces Min/Max_TBM_iSTA.
Proposed parameter setting rules for rSTA:
  MinTBM_rSTA >= MinTBM_iSTA
  MaxTBM_rSTA <= MaxTBM_iSTA
Resulting behavior:
  The rSTA can go into power save after the completion of the measurement, and remain asleep for the duration of the MinTBM_rSTA time interval.
  The iSTA can go into power save after the completion of the measurement, and remain asleep for the duration of the MinTBM_rSTA time interval.
 | No iSTA-to-rSTA LMR | Immediate iSTA-to-rSTA LMR | Delayed iSTA-to-rSTA LMR
Immediate rSTA-to-iSTA LMR | Case 1 | Case 2 | Case 3
Delayed rSTA-to-iSTA LMR | Case 4 | Case 5 | Case 6
Fig. 4 Proposal - case 1 and case 2
(with iSTA’s parameter announcement)

## Slide 12: Solution Detail for Case 3
Parameter setting rules for iSTA:
  MinTBM_iSTA >= processing time_iSTA
  MaxTBM_iSTA <= storage_time_iSTA
Parameter setting rules for rSTA:
  MinTBM_rSTA >= MinTBM_iSTA
  MaxTBM_rSTA <= MaxTBM_iSTA
Resulting behavior:
  The rSTA can go into power save after the completion of the measurement, and remain asleep for the duration of the MinTBM_rSTA time interval.
  The iSTA can go into power save after the timestamp processing and remain asleep until the end of the MinTBM_rSTA time interval
 | No iSTA-to-rSTA LMR | Immediate iSTA-to-rSTA LMR | Delayed iSTA-to-rSTA LMR
Immediate rSTA-to-iSTA LMR | Case 1 | Case 2 | Case 3
Delayed rSTA-to-iSTA LMR | Case 4 | Case 5 | Case 6
Fig. 5 Proposal - case 3

## Slide 13: Solution Detail for Case 4 and Case 5 (1)
The iSTA does not announce Min/Max_TBM_iSTA
Parameter setting rules for rSTA:
  MinTBM_rSTA >= processing_time_rSTA
  MaxTBM_rSTA <= stroage_time_rSTA
  MinTBM_rSTA < MaxTBM_rSTA
Resulting behavior:
  The rSTA can go into power save after the completion of the measurement, and remain asleep until the end of the MinTBM_rSTA time interval.
  The iSTA can go into power save after the completion of the measurement, and wakes up to initiate the next round of measurement taking into account of the parameters announced by the rSTA.
 | No iSTA-to-rSTA LMR | Immediate iSTA-to-rSTA LMR | Delayed iSTA-to-rSTA LMR
Immediate rSTA-to-iSTA LMR | Case 1 | Case 2 | Case 3
Delayed rSTA-to-iSTA LMR | Case 4 | Case 5 | Case 6
Fig. 6 Proposal - case 4 and case 5
(without iSTA’s parameter announcement)

## Slide 14: Solution Detail for Case 4 and Case 5 (2)
Optionally, iSTA announces Min/Max_TBM_iSTA
Proposed parameter setting rules for rSTA:
  MinTBM_rSTA > = processing_rSTA
  MinTBM_rSTA >= MinTBM_iSTA
  MinTBM_rSTA <= MaxTBM_iSTA
  MaxTBM_rSTA <= storage_time_rSTA
  MaxTBM_rSTA >= MinTBM_iSTA
  MaxTBM_rSTA <= MaxTBM_iSTA
Resulting behavior:
  The rSTA can go into power save after the completion of the measurement, and remain asleep for the duration of the MinTBM_rSTA time interval.
  The iSTA can go into power save after the completion of the measurement, remain asleep for the duration of the MinTBM_rSTA time interval, then wakes up to initiate the next round of measurement.
 | No iSTA-to-rSTA LMR | Immediate iSTA-to-rSTA LMR | Delayed iSTA-to-rSTA LMR
Immediate rSTA-to-iSTA LMR | Case 1 | Case 2 | Case 3
Delayed rSTA-to-iSTA LMR | Case 4 | Case 5 | Case 6
Fig. 7 Proposal - case 4 and case 5
(with iSTA’s parameter announcement)

## Slide 15: Solution Detail for Case 6
Parameter setting rules for iSTA:
  MinTBM_iSTA >= processing_time_iSTA
  MaxTBM_iSTA <= storage_time_iSTA
Parameter setting rules for rSTA:
  MinTBM_rSTA > = processing_time_rSTA
  MinTBM_rSTA > = MinTBM_iSTA
  MinTBM_rSTA <= MaxTBM_iSTA
  MaxTBM_rSTA <= Storage_time_rSTA
  MaxTBM_rSTA >= MinTBM_iSTA
  MaxTBM_rSTA <= MaxTBM_iSTA
Resulting behavior:
  The rSTA can go into power save after timestamp processing and remain asleep until the end of the MinTBM_rSTA time interval.
  The iSTA can go into power rave after timestamp processing and remain asleep until the end of the MinTBM_rSTA time interval.
 | No iSTA-to-rSTA LMR | Immediate iSTA-to-rSTA LMR | Delayed iSTA-to-rSTA LMR
Immediate rSTA-to-iSTA LMR | Case 1 | Case 2 | Case 3
Delayed rSTA-to-iSTA LMR | Case 4 | Case 5 | Case 6
Fig. 8 Proposal - case 6

## Slide 16: Summary
We have proposed a flow control mechanism for NTB ranging so that both iSTA and rSTA can go to power save.
The proposed solution addresses all combinations of immedate/delayed rSTA-to-iSTA and/or iSTA-to-rSTA LMR.

## Slide 17: Straw Poll
Do you support to the mechanism described in this document for NTB mode?
Results:
Yes: No: Abstain:

## Slide 18: References
[1] IEEE Draft P802.11az_D0.5 - Draft Standard for Information Technology - Telecommunications and Information Exchange Between Systems Local and Metropolitan Area Networks - Specific Requirements Part 11: Wireless LAN Medium Access Control (MAC) and Physical Layer (PHY) Specifications - Amendment 8: Enhancements for Positioning