## Slide 1: Packet Prioritization Issues follow-up
Date: 2018-12-12
Authors:

## Slide 2: Abstract
The purpose of this presentation is a follow up on the previous presentation[1]. It discusses a few simulation results that were suggested during the last RTA TIG meeting and a follow up to the last presentation[2].

## Slide 3: Preface:
Packet prioritization issues demonstrated in DCN 802.11-18-2098-00-0rta had time sync issues

## Slide 4: Things to observe
Simulation focuses on Client to AP latency
1st simulation shows time taken from Client to AP
2nd simulation shows Round trip time of a packet between Client and Echo Server
Observing delay and jitter with different intensity of load in the network

## Slide 5: Initial Simulation
Client
AP
Internet
Server
Video
Packet Sniffer
Packet Sniffer

## Slide 6: Delay with no load
Chart: Best Effort
Chart: Voice
Min Delay | 0.0007s
Max Delay | 0.0246s
Average | 0.0021s
Standard dev | 0.0024s
Packet Loss | 0
Min Delay | 0.0007s
Max Delay | 0.0126s
Average | 0.0018s
Standard dev | 0.0018s
Packet Loss | 0

## Slide 7: Delay with 1 video Steamer
Chart: Best Effort
Min Delay | 0.0007s
Max Delay | 0.451s
Average | 0.0100s
Standard dev | 0.0357s
Packet Loss | 0
Chart: Voice
Min Delay | 0.0006s
Max Delay | 0.0234s
Average | 0.0037s
Standard dev | 0.0036s
Packet Loss | 0

## Slide 8: Delay with 2 video Steamer
Chart: Best Effort
Min Delay | 0.0006s
Max Delay | 1.3082s
Average | 0.0323s
Standard dev | 0.1438s
Packet Loss | 0.4%
Chart: Voice
Min Delay | 0.0007s
Max Delay | 0.0407s
Average | 0.0039s
Standard dev | 0.0043s
Packet Loss | 0.2%

## Slide 9: Delay with 3 video Steamer
Chart: Best Effort
Min Delay | 0.0008s
Max Delay | 0.2106s
Average | 0.0098s
Standard dev | 0.0213s
Packet Loss | 0.4%
Chart: Voice
Min Delay | 0.0008
Max Delay | 0.0317s
Average | 0.0040s
Standard dev | 0.0035s
Packet Loss | 0.4%

## Slide 10: 2nd Simulation
Client
AP
Video
Echo Server
Internet
Packet Sniffer

## Slide 11
Delay with no load
Chart: Best Effort
Min Delay | 0.0009
Max Delay | 0.0696
Average | 0.009029
Standard Dev | 0.009235
Packet Loss | 0
Chart: Voice
Min Delay | 0.0009
Max Delay | 0.0316
Average | 0.002862
Standard Dev | 0.003377
Packet Loss | 0.2%

## Slide 12
Delay with 1 video Steamer
Chart: Best Effort
Min Delay | 0.0009s
Max Delay | 0.1799s
Average | 0.0108s
Standard Dev | 0.0167s
Packet Loss | 0
Chart: Voice
Min Delay | 0.0009s
Max Delay | 0.154s
Average | 0.0118s
Standard Dev | 0.0171s
Packet Loss | 0.4%

## Slide 13
Delay with 2 video Steamer
Chart: Best Effort
Min Delay | 0.001s
Max Delay | 0.1056s
Average | 0.0077s
Standard Dev | 0.0097s
Packet Loss | 0
Chart: Voice
Min Delay | 0.001s
Max Delay | 0.0703s
Average | 0.0080s
Standard Dev | 0.0093s
Packet Loss | 0.2%

## Slide 14
Delay with 3 video Steamer
Chart: Best Effort
Min Delay | 0.001s
Max Delay | 0.1386s
Average | 0.0124s
Standard Dev | 0.0126s
Packet Loss | 0.6%
Chart: Voice
Min Delay | 0.001s
Max Delay | 0.1096s
Average | 0.0121s
Standard Dev | 0.0124s
Packet Loss | 0.6%

## Slide 15: Observation & Summary
Voice priority helps reducing latency upstream
Voice priority has some packet loss which will be variable depending on the packet transmission interval

## Slide 16: References
[1] Karthik, Allan Jones, “Real-time Console Game Network Profile” – September 2018; https://mentor.ieee.org/802.11/dcn/18/11-18-1499-00-0000-real-time-console-game-network-profile.pptx