## Slide 1: Phase Roll Based TOA in Passive Location Ranging
Date: 2019-01-14
Authors:

## Slide 2
Passive Location with Phase Roll Based TOA Reporting
- ISTA PR-TOA reporting
RSTA
Phase roll based TOA, PR-TOA, measured by the ISTA
ISTA
Corrected PR-TOA, calculated by the RSTA using the PR-TOA reported by the ISTA and the assumption of reciprocity
Phase roll based TOA reported by the ISTA to the RSTA
Passive Station (PSTA)
Broadcasting of corrected PR-TOA from the RSTA to the passive station.

## Slide 3: Passive Location Ranging Sequence with PR-TOA – ISTA PR-TOA reporting
DL
NDP
UL
NDP
TF
RSTA
ISTA 1
ISTA 2
UL
NDP
UL
NDP
DL
NDPA
Poll
TF
PR
PR
iSTA to rSTA
LMR
TF
rSTA to
iSTA
LMR
UL
NDP
TF
iSTA to rSTA
LMR
LCI, DL LMR
UL LMR
iSTA to rSTA
LMR
LCI/LMR broadcasting frames
RSTA corrected ISTA
PR-TOAs
(No change in format)
ISTA
PR-TOAs
- Indicate PR-TOA feedback

## Slide 4: ISTA PR-TOA Reporting Benefits in Passive Location Ranging
Enables simple design of passive location ISTAs
Simplifies immediate feedback for ISTAs
Makes feedback of immediate of all time-stamps more feasible
Can use the Secundus broadcast frame to convey the PR-TOAs corrected by the RTSA

## Slide 5: Straw Poll
Do you support the use of phase roll based TOA reporting by ISTAs in Passive Location Ranging, using a reserved bit in the ‘Time Stamp Measurement Report field’ in the ‘ISTA Passive Location Measurement Report Element’ to indicate PR-TOA type and conveying the corrected PR-TOAs by the RSTA in the Secundus RSTA Broadcast Passive Location Measurement Report frame?
Y: N: A:

## Slide 6
Thank You!