## Slide 1: CR for CID 1105
Date: 2019-01-11
Authors:

## Slide 2
Abstract
In this contribution, we discuss CID 1105 and its resolutions.

## Slide 3
CID 1105
CID | Commenter | P.L. | Clause | Comment | Proposed Change
1105 | Xiaofei Wang | 36.29 | 9.4.2.276 | A WUR Discovery frame offset compared to current TBTT of the transmitting AP may be beneficial and enable a discovering STA to quickly switching through different channels to scan for WUR discovery frames. | Add a field of "WUR Discovery frame offset" to indicate the offset of current TBTT of WUR discovery frames to enable a discovering STA to quickly switching through different channels to scan for Wur discovery frames.

## Slide 4: Introduction (1/2)
TGba has agreed to advertise Neighboring BSS’s Discovery information in the WUR Discovery element [1]
  Information includes Short-SSID, BSSID, WUR Discovery Period
  Such information is meant to make it easier for the WUR non-AP STA to receive the Discovery frame
WUR non-AP STAs can use its WURx to scan for WUR Discovery frames [2]
  To conduct ultra-low power location scan
  To identify suitable APs for roaming purpose when link quality degrades
In case of WUR scanning for roaming purposes, it is desirable to identify suitable APs quickly to avoid becoming a sticky client

## Slide 5: Introduction (2/2)
However, WUR Discovery Period may be very long and WUR non-AP may need to monitor each of the Discovery Channels for a long period of time to receive a WUR Discovery frame of a particular indicated AP
More precise information may help WUR non-AP to identify the timing of the WUR Discovery frame and allows a faster WUR Scanning process
  E.g., a WUR non-AP STA may switch to different Discovery channels at desired time to scan for WUR Discovery frames

## Slide 6: Need to Provide Neighboring BSS’s Discovery frame offset (1/2)
WUR Discovery Period may be very long
  WUR Discovery Period can be indicated in 16 bits, and therefore may be 1 – 65536 TU long
  Each TU is 1024 us, so the WUR Discovery Period may be longer than 67s, much longer than the 100ms periods that are typical for regular beacons
Monitoring a Discovery Channel using the WURx without knowing when the WUR Discovery frame is transmitted takes a long time
  Each scanning WUR non-AP STA needs to monitor a Discovery Channel for at least the Discovery Period to receive a WUR Discovery frame from a particular indicated AP
It is easier to provide a more precise timing for the WUR Discovery frame by providing the Discovery frame offset for neighboring BSSs.
  Similar TBTT offsets for regular beacons provide efficiency and scheduling advantages for non-AP STA’s using Reduced Neighbor Reports
  More precise timing allows WUR STAs to switch Discovery Channels for faster WUR Scanning as shown in the following slide

## Slide 7: Need to Provide Neighboring BSS’s Discovery frame offset (2/2)

## Slide 8: Indicating WUR Discovery frame offset
The WUR Discovery frame offset may be included in the WUR Discovery element
  Optional 2-bytes element in the WUR AP subfield
  WUR Discovery frame offset in TUs, rounded down to the closest TU, from the transmitting AP’s TBTT
  Transmitting AP advertises its own WUR Discovery frame offset so that neighbor APs may include such information in their own WUR Discovery element
WUR non-AP STA may use such information to scan for relevant APs’ WUR Discovery frame
  This would allow the WUR non-AP STA to switch Discovery channels when conducting WUR scanning to quickly receive all desired WUR Discovery frames
  This also allows some power savings

## Slide 9: Conclusion
In this contribution, we discussed CID 1105 and proposed a resolution
  Propose to add a WUR Discovery Frame Offset
Such information can be included in the WUR Discovery element
This allows WUR non-AP STA to switch to different Discovery Channels for faster WUR scanning

## Slide 10
References
[1] IEEE P802.11ba Draft 1.1, Nov. 2018
[2] IEEE 802.11-17/1386r6, Examining 802.11ba Usage Models for Mainstream Devices, Sept. 2017
[3] IEEE P802.11RevMD Draft 1.0, Feb. 2018
[4] IEEE 802.11-18/1554r0, Providing Neighboring BSS Discovery Frame Offset, September 2018

## Slide 11: SP 1
Do you agree with the CR for CID 1105 as contained in 11-19/0057r0?
  Y/N/A: