## Slide 1: Interoperable Approach for NGV New Modulations
Date: 2019-01-09
Authors:

## Slide 2: Abstract
This submission provides technical details on a new PPDU and waveform design for NGV, bringing performance improvements, while maintaining full backward compatibility with legacy IEEE 802.11p stations and providing It fairness for access to the channel among all stations.
The new PPDU can include two different sections, which use two different modulations. This facilitates a smooth transition from an environment dominated by legacy 802.11p equipment to one with increasing amounts of 802.11bd equipment.

## Slide 3: Introduction
In this document we provide technical details on a new PPDU and waveform design for NGV, bringing performance improvements, while maintaining full backward compatibility with legacy IEEE 802.11p stations, by means of physical layer parameter adaptation (such as MCS adaptation).
This new PPDU design is fully compatible with the adaptive retransmission technique that was presented to the NGV SG (see 11-18/1186 and 11-18/1577). The combination of the new PPDU and the adaptive retransmission technique is shown toward the end of this document.

## Slide 4: NGV PPDU concept: append new modulated symbols to legacy IEEE 802.11 symbols
« Legacy » IEEE 802.11p section of the message
« Legacy » IEEE 802.11p section of the message
Able to decode the new symbols standalone (without using legacy data)
Treated as energy that occupies the channel (channel is busy as viewed by 802.11p stations)
« new modulation » section of the message
Exact content discussed on the next slides
« Legacy » IEEE 802.11p section of the message
L-LTF
SIG
DATA (802.11p)
New modulation symbols
How legacy 802.11p stations treat the new NGV PPDU
How NGV stations treat the new NGV PPDU
New NGV PPDU format
L-LTF
SIG
DATA
(high-power) energy
L-LTF
SIG
DATA
New modulation symbols
L-STF
L-STF
L-STF

## Slide 5: NGV PPDU format: proposal for inclusion of the new modulation symbols
Legacy IEEE 802.11p PPDU
New modulation symbols
« New DATA » symbols
« New SIG » symbols
New « SIG-like » symbols
Goal: carries the essential parameters for decoding thee new data symbols.
Baseline for discussion: L-SIG, with changes
Main difference vs L-SIG: more rate options, MIMO-precoding options, CRC protection.
« New LTF »
symbols
New « LTF-like » symbols
Goal: perform channel
Estimation
Baseline for discussion:
Suggest starting from HT-LTF (802.11-2016 19.3.9.4.6)
Alternative is VHT-LTF
New « Data » symbols
Goal: carries the encoded payload
Should provide quantitively performance improvement vs 802.11p
Baseline for discussion:
HT-PPDU (802.11-2016 19.3.00), or VHT-PPDU
Main difference vs 802.11p DATA symbols: more subcarriers, LDPC option, STBC options, various spatial streams, small GI option.
Note: some combinations may be excluded (ex: >2 spatial streams)
L-LTF
SIG
Payload (802.11p)
L-STF
time
freq
Possible configurable gap

## Slide 6: Indicating NGV Capability
It is necessary for NGV-capable stations to indicate their NGV capability to other NGV stations when transmitting legacy 802.11p broadcast messages. There are several ways to provide this capability information:
  Provide capability indication using an appended new modulation symbol. This technique is described below, but is not a required part of this proposal.
  Provide capability indication in Duration/ID field of the MAC header. This technique is described is a separate submission, 11-19/0083.
    This approach has the advantage that up to five capability bits are available.
  Provide indication using the reserved bit in the 802.11p PHY header
    This approach is only usable if all legacy equipment will accept PPDUs with the reserved bit =1.
    This approach has the disadvantage that only one capability bit is available.

## Slide 7: Dynamic Monitoring of Nearby Station Characteristics
NGV stations monitor received PPDUs to determine NumStationsNGV and NumStationsLegacy which are used to calculate TechPercentage:
TechPercentage = NumStationsNGV / (NumStationsNGV+NumStationsLegacy)
  NumStationsNGV is the number of PPDUs received during the preceding one second originating from 802.11p stations.
  NumStationsLegacy is the number of PPDUs received during the preceding one second originating from NGV-capable stations.
    The TechPercentage measurement duration is preliminary, further discussion is needed.
  Received legacy PPDUs that indicate NGV capability are counted in the NumStationsNGV category, not the NumStationsLegacy category.

## Slide 8: Dynamic balance between legacy and new modulation (1)
 | TechPercentage | Legacy 802.11p PPDU encoding (10 MHz channel) | Legacy 802.11p DATA symbols time duration | New modulation encoding time duration | New modulation encoding, example
state 1 | ≤ 60% | QPSK ½ (6 Mb/s) | 100% | 0% | none
state 2 | [60%-70%[ | QPSK ¾ (9 Mb/s) | 67% | 33% | 16QAM ¾
state 3 | [70%-80%[ | 16QAM ½ (12 Mb/s) | 50% | 50% | 16QAM ½
state 4 | [80%-90%[ | 16QAM ¾ (18 Mb/s) | 33% | 67% | QPSK ¾
state 5 | [90%-100%[ | 64QAM 2/3 (24 Mb/s) | 25% | 75% | QPSK 2/3
state 6 | 100 % | none | 0% | 100% | QPSK ½
Example based on “Table 21-30—VHT-MCSs for mandatory 20 MHz, NSS = 1”
NGV stations use the TechPercentage to select an operating state as shown in the table:
The ranges indicated in the TechPercentage column are an initial proposal, further discussion is needed

## Slide 9: Dynamic balance between legacy and new modulation (2)
Legacy 802.11p PPDU (QPSK ½)
time
Legacy 802.11p PPDU (QPSK ¾)
New modulation
time
State #1
State #2
Legacy 802.11p PPDU (16QAM ½)
New modulation
time
State #3
Legacy (16QAM ¾)
New modulation
time
State #4
Legacy (64QAM 2/3)
New modulation
time
State #5
New modulation
t=0
State #6
STF
New LTF
end of PPDU
time
Adjustable durations of the legacy and new modulation sections are based on actual channel usage – NGV stations form NGV PPDUs according to their measured TechPercentage
Total PPDU duration is similar to 802.11p PPDU with same payload, encoded with QPSK ½ (rate 6 Mb/s)

## Slide 10: Why it is possible to extend the legacy PPDU?
Not different than the case where a receive station gets overlapping messages, due to different geographical situation.
TXA
TXB
RX
1000 meters
100 meters
time
TX A PPDU
TX B PPDU
From receiver RX perspective, processing over time axis:

## Slide 11: Append new modulated symbols with configurable gap
« new modulation » section of the message
Exact content discussed on the next slides
« Legacy » section of the message
L-LTF
SIG
Payload
New modulation symbols
L-STF
Configurable gap time
The configurable gap can be set zero (direct concatenation) for best efficiency, to a short interval such as SIFS for instance, or to a longer time interval.
The total duration of the legacy + NGV sections, either with a zero time gap or a deterministic time gap, can be set to a similar total duration as the legacy 802.11p PPDU encoded with QPSK ½ (rate 6 Mb/s).

## Slide 12: Additional comments on NGV waveform
When defining the new modulation symbols based on HT or VHT modulations, the accommodation to narrower channels should be the same as was used when going from 802.11a to 802.11p. For 10MHz channels the data rate is divided by two and the symbol duration is multiplied by two.

## Slide 13: Compatibility with adaptive retransmission technique (1)
The adaptive retransmission technique described in document 11-18/1577r0 can be used along with the new NGV PPDU format described above. This combination is shown on the next slide.

## Slide 14: Compatibility with adaptive retransmission technique (2)
info* : typically, but not limited to, LLR values
Message #2 “new”
- Combined decoding (with “new” info* saved in accumulator)
- Save “new” info* in accumulator
Message #2 “legacy”
- Combined decoding (with “legacy” info* saved in accumulator)
- Save “legacy” info* in accumulator
Message #1 “new”
- Decode as standalone msg
- Save “new” info* in accumulator
Message #1 “legacy”
- Decode as standalone message
- Save “legacy” info* in accumulator
Treated as energy that occupies the channel
Message #2
Decode as standalone message
Treated as energy that occupies the channel
Message #1
Decode as standalone message
How legacy IEEE 802.11p stations treat the PPDU (RX perspective): 2 independent messages
New NGV PPDU format (TX perspective)
Retransmission (example with 1 retransmission) = exact copies of the initial message
Initial message
How NGV stations treat the PPDU (RX perspective): combine messages (example: combining at LLR level)
L-LTF
SIG
DATA (IEEE 802.11p)
New modulation symbols
L-STF
L-LTF
SIG
DATA (IEEE 802.11p)
New modulation symbols
L-STF
Configurable gap time
L-LTF
SIG
DATA (IEEE 802.11p)
L-STF
L-LTF
SIG
DATA (IEEE 802.11p)
L-STF
L-LTF
SIG
DATA (IEEE 802.11p)
New modulation symbols
L-STF
L-LTF
SIG
DATA (IEEE 802.11p)
New modulation symbols
L-STF
(high-power) energy
(high-power) energy

## Slide 15: Benefits
This technique for incorporating new modulation symbols improves performance while maintaining interoperability, coexistence, backward compatibility, and fairness with 802.11p equipment
This technique can be used in conjunction with the adaptive retransmission technique described in 11-18/1577r0
This technique does not increase channel load in congested environments
This technique does not require changing higher layers of the ITS protocol stack