## Slide 1: Proposal for Downlink Broadcast Requirements
Date: 2019-01-14
Authors:

## Slide 2: Abstract
This presentation describes a proposal for downlink broadcast requirements.

## Slide 3: Definitions
eBCS data frame
  A frame which delivers broadcast content.
eBCS AP
  An AP that supports eBCS; an eBCS AP is the sender of eBCS data frames in downlink use cases.
eBCS non-AP STA
  A non-AP STA that supports eBCS; an eBCS STA is the receiver of eBCS data frames in downlink use cases.

## Slide 4: Requirement #1: Capacity
An eBCS AP shall accommodate at least 3,000 eBCS STAs.
  By the simulation in 11-18/1581r0, an AP can cover 3,000m2 (5GHz, MCS 7, Short GI, 80MHz bandwidth, 10mW)
  Reference: 11-18/1581r0

## Slide 5: Requirement #2: Security
Every eBCS data frame shall be authenticated to be protected from rogue-eBCS APs.
  Although higher layer protocol can provide equivalent security, it depends on higher layer protocol.
  If IEEE802.11bc does not provide security mechanism and users does not care about security, it is dangerous.
  Actually existing free WLAN services without security setup (IEEE802.11i) cause security issues when users use HTTP, POP, IMAP, SMTP etc. without TLS.

## Slide 6: Requirement #3: Privacy
eBCS STAs shall have capability to receive eBCS data frames without transmission of any frames.
  By this feature, it can be completely hidden who is receiving.
  This means the eBCS STA can receive eBCS data frames regardless of the association state.

## Slide 7: Requirement #4: Reliability
Optional error correction mechanism should be provided to increase reliability.
  Shall not modify PHY FEC mechanism.
  Inter-frame error correction.
    e.g. transmit multiple identical frames and/or inter-frame LDPC.

## Slide 8: Comments & Questions